ADD	EUR/13A8/9

5.XX1	In order to avoid unacceptable interference to the Earth exploration-satellite (passive) service in the band 31.3-31.5 GHz, the unwanted emissions power delivered to the antenna of any station in the fixed service operating in the band 31.0-31.3 GHz shall be limited to –38 dBW in a 100 MHz reference bandwidth in the band 31.3-31.5 GHz (see also No. 5.543A).

Reasons:	This footnote is related to No. 5.543A as proposed to be modified in EUR/13A13/3.