MOD	IRN/32/44

5.502	In the band 13.75-14 GHz, an earth station of a geostationary fixed-satellite service network shall have a minimum antenna diameter of 1.2 m and an earth station of a non-geostationary fixed-satellite service system shall have a minimum antenna diameter of 4.5 m. In addition, the e.i.r.p. averaged over one second, radiated by a station in the radiolocation or radionavigation services shall not exceed 59 dBW above 2º elevations and 65 dBW below. An administration planning to use FSS earth stations with an antenna diameter less than 4.5 m in a geostationary network in this band shall ensure that the single-entry power flux-density produced by any earth station operating within its territory does not exceed:

–	–105.2 dB(W/(m2 ( 10 MHz)) not to be exceeded for more than 1.0% of the time produced at 36 m above sea level at the [normal baseline, straight baseline, baseline as defined in the UN Convention on the Law Of the Sea 1982 or at a point specified by the coastal State].