SUP	KEN/33/18

Kenya supports the suppression of Resolution 34 and subsequent modifications to the RR, specifically Table 21-4 of Article 21 in order to incorporate the regulatory provisions which apply to the use of BSS in Region 3 in the band 12.5-12.75 GHz, in respect to space and terrestrial services in all Regions.

vii)	Rule of Procedure 9.35 provisionally adopted to reduce backlog in the processing of satellite filings

Kenya supports Method A of the CPM Report which requires WRC-03 not to endorse the provisional RoP No. 9.35.

1.32	to consider technical and regulatory provisions concerning the band 37.5-43.5 GHz, in accordance with Resolutions 128 (Rev.WRC-2000) and 84 (WRC-2000)

Resolution 128 (Rev.WRC-2000)

This Resolution deals with the protection of the radio astronomy service in the 42.5-43.5 GHz frequency band.

Proposal

Method A: For the 42-42.5 GHz band GSO network and 41.5-42.5 GHz band non-GSO systems, protect-dish radio telescope sites on an individual bilateral basis, modify levels in No. 5.551G to be modified to adopt the single-dish, continuum threshold of –137 dB(W/(m2 · GHz)) and
–153 dB(W/(m2 · 500 kHz)) as a threshold for bilateral arrangements at single-dish radio telescope sites.

A Resolution, which would not require the involvement of the Bureau, would provide operational rules for bilateral sharing arrangements with affected single-dish radio telescope sites where the levels in No. 5.551G are exceeded for more than 2% of the time.

Resolution 84 (WRC-2000)

This Resolution deals with power flux-density limits in the bands 37.5-42.5 GHz for the fixed-satellite service, broadcasting-satellite service and mobile-satellite service.

Proposal