| INTERNATIONAL TELECOMMUNICATION UNION |  |
| --- | --- |
|  | WRC-03 | WORLD RADIOCOMMUNICATION CONFERENCE | Document 342-E |
|  |  |  | 1 July 2003 |
|  |  |  | Original: English |
| GENEVA, 9 JUNE – 4 JULY 2003 |  |
|  | COMMITTEE 8 |
| THIRTEENTH SERIES OF TEXTS SUBMITTED BY COMMITTEE 6 TO THE EDITORIAL COMMITTEE |

ADD	COM6/343/1

DRAFT  RESOLUTION  [COM 6/4]  (WRC-03)

Application of the grouping concept in 
Appendices 30 and 30A in Regions 1 and 3

The World Radiocommunication Conference (Geneva, 2003),

considering

a)	that the grouping concept as it is applied in Appendices 30 and 30A with respect to Regions 1 and 3 was considered by WRC-03;

b)	that the protection of assignments in the Plan and the List in Appendices 30 and 30A is based upon an aggregate EPM criterion;

c)	that concerns have been raised that use of the grouping concept by one administration may reduce access to spectrum resources by others;

d)	that coordination of one network in a group shall not lead to reduction of coordination requirements for other networks in the same group;

e)	that WRC-2000 accepted grouping in the Regions 1 and 3 List for some networks which are separated by up to 0.2( in the geostationary arc according to their respective nominal orbital locations,

noting

- that CPM-02 considered a proposed solution in which there is a limit to the number of assignments in a group and/or number of groups in one orbital location;

- that the Radio Regulations Board has developed Rules of Procedure with respect to the application of the grouping concept,

resolves

1	that grouping of networks which all are separated by not more than 0.4( in the geostationary arc is regarded as grouping at the same orbital location according to their respective nominal orbital locations;

2	that the limitations referred to in resolves 4 do not apply to grouping of networks before the inclusion of the corresponding assignments in the List;

3	that the limitations in resolves 4 do not apply to grouping within one network;

4	that under Appendices 30 and 30A in Regions 1 and 3 the following principles with respect to the application of the grouping concept between networks at the same orbital location shall apply:

a)	these limitations apply for networks with overlapping frequency bands;

b)	for networks received by the Bureau under § 4.1.3 of Appendix 30 or 30A after 4 July 2003, not more than three networks within the same overlapping frequency bandwidth can be in a group in the List unless under the provisions of d) or e) below;

c)	for networks received by the Bureau under § 4.1.3 of Appendix 30 or 30A, but not yet processed under § 4.1.5 before 5 July 2003, not more than five networks within the same overlapping frequency bandwidth can be in a group in the List unless under the provisions of d) or e) below;

d)	for networks received by the Bureau under § 4.1.3 of Appendix 30 or 30A and processed under § 4.1.5 before 5 July 2003, the number of networks that can be in a group in the List within the same overlapping frequency bandwidth cannot be further expanded by new networks beyond five;

e)	for a group of networks in the List established prior to 5 July 2003, the number of networks within the same overlapping frequency bandwidth in the group cannot be further expanded by new networks beyond five;

ebis)	if a number of networks in a group in the List reaches the maximum limit specified above, no new networks can be entered into the List in this group without removal of another overlapping part of a network from the List;

f)	as a provisional measure, networks in the List may be optimized or merged to reduce the number of networks in accordance with the following principles:

–	no optimization or merging of networks in a group shall lead to increased probability of harmful interference or require more protection than that of those networks prior to optimization/merging;

–	the associated priority date and date of bringing into use for each assignment shall be maintained;

–	networks in the List can be optimized/merged as described above before 1 January 2004;

–	upon entering into the List of networks submitted to the Bureau in accordance with § 4.1.3 before 5 July 2003, the List may be optimized/merged as described above,

5	that as of 5 July 2003, in the processing and publication by the Bureau of submissions related to Regions 1 and 3 under Article 4 to Appendices 30 or 30A received after 2 June 2000 and the identification of affected administrations in accordance with § 4.1.5, each network in a group is examined separately, without taking into account the other networks in the group3,

instructs the Director of the Radiocommunication Bureau

1	to implement resolves 1 to 5 above as of 5 July 2003;

2	by 1 September 2003, to send a notice to administrations having networks in the Regions 1 and 3 List as of 5 July 2003 to bring resolves 4 f) to their attention;

3	upon processing and publication of a network submitted by an administration under § 4.1.3 prior to 5 July 2003, send a notice to the notifying administration, bringing the provisions of resolves 4 f) to their attention and allowing the administration to, within 30 days from the date of the notice to optimize/merge its networks in the List in accordance with the principles in resolves 4 f),

instructs the Radio Regulations Board

to review and revise, as appropriate, the Rules of Procedure relating to the application of the grouping concept in Regions 1 and 3.

__________

# Footnotes

It is noted that the application of the grouping concept in Region 2 does not require any change. Therefore, the Radiocommunication Bureau shall continue to apply the grouping concept in Region 2 as it has applied it prior to WRC-03.

In application of this Resolution, a network is understood as being a submission by one administration, or one administration acting on behalf of a group of administrations to the Bureau of a set of assignments, received on the same date (except for merged networks referred to in resolves 4 f), with the same name for the satellite network and at the same orbital location.

3	In application of § 4.1.11, the use of the new methodology in this resolves to networks received before 3 June 2000 shall not result in additional coordination requirements for those networks.