## Slide 1
Khalid Al Awadhi
Panel Sessions 7 & 8 WRC-15 Agenda items 7 & 9.1 issues (9.1.2, 9.1.3, 9.1.5, 9.1.8)

## Slide 2
Issue A of WRC-15 AI 7
Informing the Bureau of a suspension under RR No. 11.49 beyond six months
Method A1: NOC
OR
Method A2: modification to RR No. 11.49 to provide a regulatory mechanism to clarify the issue, with two options:
Option A: Day-for-day reduction in the suspension period after 6 months, or
Option B: Day-for-day reduction in the suspension period after 6 months up to 12 months* followed by two times reduction thereafter
* The 12 months period can be changed

## Slide 3
Issue A of WRC-15 AI 7
Regional Positions
Method | APT | ASMG | ATU | CEPT | CITEL | RCC
Method A1: NOC |  |  |  |  | Support | 
Method A2: Option A Day-for-day reduction | Support | Support | Support | Support |  | Support
Method A2: Option B Day-for-day reduction and then two times reduction | Oppose |  |  |  |  | 

## Slide 4
Issue B of WRC-15 AI 7
Publication of information on bringing into use of satellite networks at the ITU website
Clarifying the BR’s action through one of the following:
Method B1-Option A: implement amendments to RR Nos. 11.44B, 11.49 and 11.49.1
Method B1-Option B: Same as previous + stating that BR publish the info as received
Method B2-Option A: implement amendments to RR Nos. 11.44B, 11.49 and 11.49.1, availing the BIU info at ITU-R website, and including the information in a Special Section (Res. 49)
Method B2-Option B: Same as previous + stating that BR publish the info as received
Method B3: Identify the BR actions required, and include in minutes of WRC-15

## Slide 5
Issue B of WRC-15 AI 7
Regional Positions
Method | APT | ASMG | ATU | CEPT | CITEL | RCC
Method B1 Option A |  |  |  | Support | Support | 
Method B1 Option B | Support |  |  |  |  | 
Method B2 Option A |  |  |  |  |  | 
Method B2 Option B |  |  |  |  |  | 
Method B3 |  | Support |  |  |  | 
Remarks |  |  |  |  | Additional Measures | Necessary to MOD Art. 11

## Slide 6
Issue C of WRC-15 AI 7
Review or possible cancellation of the advance publication mechanism for satellite networks subject to coordination under section II of Article 9 of the Radio Regulations
Method C1: NOC
OR
Method C2: Cancellation of the current API mechanism
Option A: suppress the need for API
Option B: Automatically generate API by BR as soon as CR/C received
OR
Method C3: Review of API mechanism
Option A: Reduce the two-year validity period for an API (without CR/C)
Option B: Suppress the minimum period of six months between API and CR/C

## Slide 7
Issue C of WRC-15 AI 7
Regional Positions
Method | APT | ASMG | ATU | CEPT | CITEL | RCC
Method C1 - NOC |  |  |  |  |  | Oppose
Method C2 Option A |  |  |  |  |  | 
Method C2 Option B |  |  |  | Support |  | 
Method C3 Option A |  |  |  |  |  | 
Method C3 Option B |  | Support | Support |  | Support | Support
Remarks |  |  |  |  |  | Consideration for other solutions

## Slide 8
Issue D of WRC-15 AI 7
General use of modern electronic means of communications in coordination and notification procedures
Method D: Conclusion towards amendments to Resolutions 907 (WRC-12) to include the use of modern electronic means, and to Resolution 908 (WRC-12) to expand its scope to all kind of satellite network filings and to request the BR to analyze whether it is possible to have a single consolidated interface for both the submission of satellite network filings and the related correspondence
Method | APT | ASMG | ATU | CEPT | CITEL | RCC
Method D | Support | Support | Support | Support | Support | Support

## Slide 9
Issue E of WRC-15 AI 7
Failure of a satellite during the bringing into use period
Different possible conclusions:
Method E1: adding a footnote to RR No. 11.44B: if failure during BIU, frequency assignments brought into use
Method E2: Same as previous + adding a footnote to RR No. 11.49: if failure during BBIU, frequency assignments brought into use
Method E3: NOC
Method E4: additional provision RR No. 11.44.3 allows to extend for 3 years the date of bringing into use from the date of the failure
Method E5: consideration by the RRB on a case-by-case basis, based on BR report
Method E6: If no decision from BR within three months: BR develop report and submit to the RRB

## Slide 10
Issue E of WRC-15 AI 7
Regional Positions
Method | APT | ASMG | ATU | CEPT | CITEL | RCC
Method E1 | Oppose |  |  |  |  | 
Method E2 | Oppose |  |  |  |  | 
Method E3 - NOC | Support |  | Support | Support | Support | 
Method E4 | Oppose |  |  |  |  | Support
Method E5 |  | Support |  |  |  | 
Method E6 |  |  |  |  |  | 

## Slide 11
Issue F of WRC-15 AI 7
Modifications to RR Appendix 30B in relation to the suspension of use of a frequency assignment recorded in the MIFR
Conclusion towards aligning provisions of App 30B with Article 11, APP 30 & 30A, by extending the period allowed for suspension of the use of a frequency assignment to space station to three (3) years
Method | APT | ASMG | ATU | CEPT | CITEL | RCC
Single Method | Support | Support | Support | Support | Support | Support

## Slide 12
Issue G of WRC-15 AI 7
Clarification of bringing into use information provided under RR Nos. 11.44/11.44B
Conclusion towards new regulatory provisions:
enables BR to seek clarification from the notifying administrations under RR Nos. 11.44 and 11.44B
allow BR to validate the information provided under RR No. 11.44
for GSO station: ensure information provided under RR No. 11.44B correspond to the deployed space station with transmission capability
Method | APT | ASMG | ATU | CEPT | CITEL | RCC
Method G | Support | Support | Support | Support | Support | Support

## Slide 13
Issue H of WRC-15 AI 7
Using one space station to bring frequency assignments at different orbital locations into use within a short period of time
Different possible conclusions:
Method H1: NOC + enquire from Admin about BIU and make info available:
    Previous orbital position of satellite
    satellite network BIU’ed by this satellite at previous location
    The reason for its relocation.
Option A: include in the minutes of the Plenary of WRC-15
Option B: new WRC Resolution detailing the above
Method H2: NOC

## Slide 14
Issue H of WRC-15 AI 7
Using one space station to bring frequency assignments at different orbital locations into use within a short period of time
Different possible conclusions:
Method H3: extend the period of BIU from 90 days to 12 months + use space monitoring facilities to verify
Method H4: reducing the time available for suspension to the cumulative number of days that the satellite network has been in use, up to a limit of three years
Method H5: Administrations include the following information as part of confirmation of the BIU of frequency assignments to a satellite network:
    Previous orbital position of satellite
    the date the satellite left the previous orbital position
    the name of the ITU filing(s) used by the in-orbit satellite at the previous orbital position.

## Slide 15
Issue H of WRC-15 AI 7
Using one space station to bring frequency assignments at different orbital locations into use within a short period of time
Different possible conclusions:
Method H6: A new resolution based on:
Indicate if newly-launched satellite or in-orbit
Explanation of abusive “satellite hopping”
If in-orbit satellite: BR request clarifications
BR accepts the BIU or refers to RRB
RRB makes the decision

## Slide 16
Issue H of WRC-15 AI 7
Regional Positions
Method | APT | ASMG | ATU | CEPT | CITEL | RCC
Method H1 Option A |  | Support |  |  |  | 
Method H1 Option B |  |  |  |  |  | 
Method H2 - NOC |  |  |  |  |  | 
Method H3 |  |  |  |  |  | 
Method H4 |  |  |  |  |  | 
Method H5 |  |  |  |  |  | 
Method H6 |  |  | Support |  |  | 
Remarks |  |  |  |  |  | No Additional restrictions

## Slide 17
Issue I of WRC-15 AI 7
Possible method to mitigate excessive satellite network filings issue
Possible conclusions for excessive CR/C filing issue:
Method I1.1: Initial notification and due diligence information without Bureau examination
Method I1.2: Initial notification and due diligence information with Bureau examination
Method I1.3: Optional submission to initial notification information
Method I1.4: NOC
Possible conclusions for excessive API filing issue:
Method I2.1: NOC
Method I2.2: Suppression of the current API mechanism
Method I2.3: removal of six months requirement between API and CR/C

## Slide 18
Issue I of WRC-15 AI 7
Regional Positions
Method | APT | ASMG | ATU | CEPT | CITEL | RCC
Possible conclusions for excessive CR/C filing issue |  |  |  |  |  | 
Method I1.1 |  |  |  |  |  | 
Method I1.2 |  |  |  |  |  | 
Method I1.3 |  |  |  |  |  | 
Method I1.4 – NOC | Support | Support |  | Support |  | Support
Possible conclusions for excessive API filing issue: |  |  |  |  |  | 
Method I2.1 – NOC |  |  |  |  |  | Oppose
Method I2.2 |  |  |  | Support |  | 
Method I2.3 |  | Support | Support |  |  | Support

## Slide 19
Issue J of WRC-15 AI 7
Removal of the link between the date of receipt of the notification information and the date of bringing into use in RR No. 11.44B
Method J1: Conclusion towards eliminating from RR No. 11.44B the only instance where the notification information for a frequency assignment to a space station in the geostationary-satellite orbit is not in conformity with RR No. 11.44B because of the requirement to confirm the notified date of BIU within 120 days of this date
OR
Method J2: NOC
Method | APT | ASMG | ATU | CEPT | CITEL | RCC
Method J1 |  | Support | Support | Support |  | Support
Method J2 – NOC |  |  |  |  |  | 

## Slide 20
Issue K of WRC-15 AI 7
Addition of a regulatory provision in RR Article 11 for the case of launch failure
Method K1: Conclusion towards An additional provision of RR No. 11.XX to regulate any launch failure of a satellite that such failure makes the satellite unable to start BIU or BBIU of a notified frequency assignment
Method K2: An alteration of this previous regulation is to make it on a case-by-case basis by the RRB
OR
Method K3: NOC

## Slide 21
Issue K of WRC-15 AI 7
Regional Positions
Method | APT | ASMG | ATU | CEPT | CITEL | RCC
Method K1 |  |  |  |  |  | 
Method K2 | Support |  |  |  |  | 
Method K3 – NOC |  | Support | Support | Support |  | 
Remarks |  |  |  |  |  | Support the extension of time-limit

## Slide 22
Issue L of WRC-15 AI 7
Modification of certain provisions of Article 4 of RR Appendices 30 and 30A for Regions 1 and 3 namely replacement of tacit agreement with explicit agreement or alignment of those provisions of RR Appendices 30 and 30A for Regions 1 and 3 with those of Appendix 30B
Method L1: Modify the corresponding provisions of RR Appendices 30 and 30A in such a manner that the notion of tacit agreement be replaced by explicit agreement.
OR
Method L2: Harmonization of the provisions in Article 4 of both RR Appendices 30 and 30A with the corresponding provisions of Article 6 of Appendix 30B
OR
Method L3: NOC

## Slide 23
Issue L of WRC-15 AI 7
Regional Positions
Method | APT | ASMG | ATU | CEPT | CITEL | RCC
Method L1 |  |  | Support |  |  | 
Method L2 |  | Support |  |  |  | 
Method L3 – NOC |  |  |  | Support |  | 
Remarks |  |  |  |  |  | Support studies

## Slide 24
Issue 9.1.2 of WRC-15 AI 9.1
Studies on possible reduction of the coordination arc and technical criteria used in application of No. 9.41 in respect of coordination under No. 9.7
Proposed Conclusions on Resolves 1 (technical criteria)
Option 1A
  Retain RR Nos. 9.7, 9.41 and 11.32A essentially unchanged
  Change trigger criteria from ΔT/T to C/I=C/N + X dB, where X is less than 12.2 dB (the value corresponding to 6% ΔT/T)
  RR No. 11.32A would use the same C/I criteria as above
Option 1B
  NOC to current RR App. 5 identification of coordination requirements
  Change threshold levels for application of RR No. 9.41 for some frequency bands
  Replace C/I in RR No. 11.32A with uplink/downlink PFD masks for some frequency bands
Option 1C
  Same as Option 1B, with PFD thresholds outside the Coordination Arc
Option 1D: NOC

## Slide 25
Issue 9.1.2 of WRC-15 AI 9.1
Studies on possible reduction of the coordination arc and technical criteria used in application of No. 9.41 in respect of coordination under No. 9.7
Proposed Conclusions on Resolves 2 (Coordination Arc)
Option 2A: Reduce coordination arc as:
    6/4 GHz band ±8⁰ reduces to ±6⁰
    14/10/11/12 GHz band ±7⁰ reduces to ±5⁰
    30/20 GHz band NOC to ±8⁰
Option 2B: Reduce coordination arc as:
    6/4 GHz band ±8⁰ reduces to ±6⁰
    14/10/11/12 GHz band ±7⁰ reduces to ±5⁰
    30/20 GHz band ±8⁰ reduces to ±6⁰
Option 2C: NOC

## Slide 26
Issue 9.1.2 of WRC-15 AI 9.1
Regional Positions
Method | APT | ASMG | ATU | CEPT | CITEL | RCC
Resolves 1 (technical criteria) |  |  |  |  |  | 
Option 1A |  |  |  |  |  | Support
Option 1B |  |  | Support |  |  | 
Option 1C |  |  |  |  |  | 
Option 1D – NOC |  | Support |  |  |  | 
Resolves 2 (Coordination Arc) |  |  |  |  |  | 
Option 2A |  |  | Support | Support | Support | 
Option 2B |  | Support |  |  |  | Support
Option 2C – NOC |  |  |  |  |  | 
Remarks |  |  |  |  |  | Alteration

## Slide 27
Issue 9.1.3 of WRC-15 AI 9.1
Use of satellite orbital positions and associated frequency spectrum to deliver international public telecommunication services in developing countries
Two possible conclusions:
Option A: NOC
Option B: Revise Resolution 11 (WRC-12) in order to continue with the studies as it may be required for resolves 2 of Resolution 11 (WRC-12) to continue even after WRC-15
Method | APT | ASMG | ATU | CEPT | CITEL | RCC
Option A - NOC | Support | Support |  |  |  | 
Option B |  |  | Support |  |  | 
Remarks |  | Supress Res 11 (WRC-12) |  | Alteration |  | 

## Slide 28
Issue 9.1.5 of WRC-15 AI 9.1
Consideration of technical and regulatory actions in order to support existing and future operation of fixed-satellite service earth stations within the band 3 400-4 200 MHz, as an aid to the safe operation of aircraft and reliable distribution of meteorological information in some countries in Region 1
Conclusion towards modification to Resolution 154 (WRC-12), calling for relevant administrations in Region 1 to use special care in the coordination, assignment, and management of frequencies taking into consideration the potential impact on the FSS earth stations used for satellite communications related to safe operation of aircraft and reliable distribution of meteorological information in the frequency band 3 400-4 200 MHz.
Consideration may be given to modifying RR No. 5.430A to include a reference to the modified Resolution

## Slide 29
Issue 9.1.5 of WRC-15 AI 9.1
Regional Positions
Method | APT | ASMG | ATU | CEPT | CITEL | RCC
Single conclusion |  | Support | Support |  |  | Support
Remarks |  |  |  | Alteration |  | 

## Slide 30
Issue 9.1.8 of WRC-15 AI 9.1
Regulatory aspects for nanosatellites and picosatellites
The ITU-R Study Groups have concluded that additional efforts should be undertaken by the BR, administrations, and others to help increase knowledge and raise awareness about the applicable regulatory procedures for satellite networks among those entities involved in development and launch of nanosatellites and picosatellites.
Another relevant response to this issue could be to consider modifications to the regulatory procedures for notifying satellite networks to accommodate nanosatellite and picosatellite missions

## Slide 31
Issue 9.1.8 of WRC-15 AI 9.1
Regional Positions
 | APT | ASMG | ATU | CEPT | CITEL | RCC
views | Retention of Res 757 (Rev.WRC-12) with Modifications | new agenda item, but no additional complications | Simplified regulatory procedures | propose a new ITU-R Resolution | NOC + no need for new Agenda Item | Can have new agenda item, but no additional complications