## Slide 1: Demonstration of 7680×4320 UHDTV with 22.2 multichannel sound using 85-inch LCD
September 26 – 27, 2011 at ITU
NHK (Japan Broadcasting Corp.)

## Slide 2: Background (R&D at NHK)
In 1995, started study on UHDTV and three-dimensional multichannel sound.
In 2000, started study on 8K×4K UHDTV.
In 2002, produced the first UHDTV programme.
Since then, has produced a number of UHDTV programmes, conducted live transmission, and demonstrated them at World Expo., IBC, NAB, and others.
Also developed video and sound equipment for capture, production, transmission, and display.
In 2011, developed the world’s first 8K×4K LCD.
In 2020, will launch test broadcasting of 8K×4K UHDTV.

## Slide 3: Background (ITU-R Recommendations)
Rec. ITU-R BT.1201 “Extremely high resolution imagery” (1995, 2004)
Rec. ITU-R BT.1769 “Parameter values for an expanded hierarchy of LSDI image formats for production and international programme exchange” (2006)
PDN Rec. ITU-R BT.[IMAGE-UHDTV] “Parameter values for UHDTV systems for production and international programme exchange” (under development)

## Slide 4: Content
A programme titled “Gift” produced in 2009 (10 min)
Four video clips and two still pictures (45 sec)
Two sound programmes, orchestra and pipe organ, with still pictures (3 min each, to be presented at a special session for audio experts)

## Slide 5: Equipment
85-inch LCD
  7680×4320/60/P, 10-bit, HDMI (1.3) ×16-ch
Loudspeakers
  Loudspeaker array frame integrated with LCD
    102 loudspeaker units reproduce side and rear sound using signal processing in addition to frontal sound
  Tallboy type loudspeakers (for studio production)
    10 pillars for 22.2-ch reproduction
    Playback
      Video: Solid state drive and frame memory, RGB 4:4:4, 12-bit
      Audio: Hard disk drive (Digital Audio Workstation), 48 kHz, 24-bit

## Slide 6: Schedule
Monday, 26 September
  09:00 – 18:00
Tuesday, 27 September
  09:00 – 16:00
  Note: Special sessions may be held for video and audio experts during the days.