|  | Project Team 1 of the Conference Preparatory Group of the European Radiocommunications Committee | CEPT/ERC/CPG2000/PT1(99) LUX-01r2 |
| --- | --- | --- |

DRAFT

Reference: PT1(98)10, PT1(98)45, PT1(98)68, PT1(99)002

Subject:	Role of the Notifying Administration when acting as the Notifying Administration on Behalf of a Named Group of Administrations.

Origin:	Luxembourg

Date:	22 February, 1999

Attached is the revised draft on this subject based on the discussions at the recent PT1 meetings. This document is submitted as a draft submission to the SC.

There was a CEPT ECP to the PP98 on this issue and as a result of the discussion at the PP, Resolution [COM5/19] was adopted which requests the Director BR to prepare a report to the next WRC on this issue and requests the next WRC to address this issue.

It is also to be noted that WARC-88 covered this subject for App. 30B by including in App. 30B No 6.38, which only applies to this Appendix.

|  | INTERNATIONAL TELECOMMUNICATION UNION RADIOCOMMUNICATION STUDY GROUPS | Document SC99-1/LUX01-E 19 February 1999 Original: English |
| --- | --- | --- |

|  | INTERNATIONAL TELECOMMUNICATION UNION RADIOCOMMUNICATION STUDY GROUPS | Document SC99-1/LUX01-E 19 February 1999 Original: English |
| --- | --- | --- |

DRAFT

LUXEMBOURG

Role of the Notifying Administration When Acting as the

Notifying Administration on Behalf of a

Named Group of Administrations.

Resolution [COM5/19] Minneapolis

1.	This document has been prepared within the framework of CEPT. During the past year there has been a situation in which the role and responsibility of the notifying administration when it is acting on behalf of a group of named administration is not clear. The BR and RRB see the administration as being responsible for the data, whereas, some notifying administrations see their responsibility as that of a ”post office” and only to forward to the BR the information that they receive from the intergovernmental organization that is responsible for the satellite network. It is to be noted that under the Radio Regulations only administrations may submit notices and data to the BR for processing and also there are certain rights and obligations that flow from the application of the Radio Regulations and that these rights and obligations relate to the notifying administration. Intergovernmental satellite organizations that operate satellite networks are not recognized within the Radio Regulations.

2.	Annex 1 provides a partial listing of some provisions of the Regulations that deal with the rights and obligation of the notifying administration.

3.	PP98 addressed this issue and Resolution [COM5/19] was adopted which requests the Director BR to prepare a report to the next WRC on this issue and requests the next WRC to address this issue.

4.	This situation only applies to satellite networks and Nos S9.1.1 and S11.15.1 are the relevant provisions. There are no specific similar provisions in Appendices 30 and 30A but the Rules of Procedure of the RRB provide for such a process.

5.	These provisions clearly indicate that each administration has the right to act on its behalf with respect to other networks of its own. There have been cases in which the notifying administration submits notices on behalf of a group of named administration and also raises concerns about the submitted notices on the basis of its own networks. Under these provisions it is possible for a different administration to be the notifying administration for different satellite networks operated by an intergovernmental organization.

6.	App.S30B in No. 6.38 already recognizes the principle of having one of the administrations listed to be identified to act as the notifying administration.

7.	Under the arrangements between the intergovernmental organizations that are responsible for such networks and the host administration, the host administration has a responsibility to submit to the BR whatever it receives from the organization. On the other hand, there must be some single administration that is accountable to the BR as it is impracticable for the ITU to deal will all administrations that are members of the organization or all members on whose behalf the publication is made. Normally the present situation does not result in any problems, but only in those cases when there are studies or questions raised, one administration should be responsible for investigating the case and reporting to the BR/RRB, and this logically is the notifying administration. It is proposed to add to the present No. S9.1.1 as follows and adopt the attached Resolution:

MOD S9.1.1	1 Whenever, under this provision, an administration acts on behalf of a group of named administrations, all members of that group retain the right to respond in respect of their own networks or systems. (see Resolution XXX) [Annex 2].

MOD		Similar changes to App.S30 and App. S30A

ANNEX 1

Provisions of the Radio Regulations that Relate to the Roles

and Responsibilities of the Notifying Administration

Some of the main provisions of the Radio Regulations that relate to the roles and responsibilities of the notifying administration are the following:

·	S4.4-assignment of frequencies not in conformity with the RR by an administration on the condition of no interference;

·	S8.4- recording of assignments with a reference to S4.4 only when the administration makes a commitment;

·	S9.3-no comments within a time period equals no objection by the administration, and administrations shall endeavor to cooperate to resolve any difficulties;

·	S9.4-the administration shall explore all possible means etc.;

·	S9.43- an administration not responding shall be considered as not affected;

·	S9.47-49	-administration undertakes to not make a claim about harmful interference and to not cause HI

·	S9.51-an administration shall act within a specified period;

·	S11.36- undertaking by the notifying administration to not cause HI;

·	S11.39B- as per S11.36;

·

This is only a partial listing of such provisions and there are many other provisions that state that an administration shall do certain things.

ANNEX 2

Draft

Resolution  XXX

The Role of the Notifying Administration of Satellite Networks

when acting on Behalf of a Group of Named Administrations

The World Radiocommunications Conference (Istanbul 2000)

Considering

a)	that the Radio Regulations permit one administration to act as the notifying administration for a satellite network on behalf of a group of named administrations;

b)	that there are certain rights and obligations under the Radio Regulations between administrations;

c)	that in the case of the host administration which notifies on behalf of a group of named administrations, that administration normally has the obligation under the agreement with the intergovernmental satellite organization/operator concerned to submit all information, which it has received from the organization responsible for the satellite network, to the ITU;

d)	that it is not necessary under the Radio Regulations for the same administration (the host administration) to be the notifying administration for all satellite networks of that intergovernmental organization;

e)	that there is need for one administration to be responsible for carrying out the obligations under the Radio Regulations and to act on behalf of the group of administrations for each satellite network;

f)	that No. 6.38 of App. S30B already recognizes the principle of having one of the listed administration for regional systems to be identified as the notifying administration and to act on behalf of all the administrations in carrying out the provisions of the Regulations;

g)	the report of the Director BR on this subject as requested by Res. [COM5/19] Minneapolis 1998;

resolves

1.	that when an administration acts as the notifying administration of a satellite network on behalf of a group of named administrations in accordance with Nos S9.1.1 and S11.15.1 and the Rules of Procedures for App. 30/30A, the following procedures shall be applied:

·	the notifying administration shall be one of the named administrations on whose behalf the network is being notified to the ITU;

·	the intergovernmental organization responsible for the network shall select one of the named administrations to act as the notifying administration for that particular network

·	the administration named as the notifying administration shall act on behalf of all the administrations listed and assume all of the responsibilities of a notifying administration as prescribed in the Radio Regulations.

2.	that the intergovernmental organization responsible for such networks shall ensure that the named notifying administration is able to assume these responsibilities under the Radio Regulations.