| INTERNATIONAL TELECOMMUNICATION UNION | Focus Group On IPTV |
| --- | --- |
| TELECOMMUNICATION STANDARDIZATION SECTOR STUDY PERIOD 2005-2008 | FG IPTV-C-0171 |
|  | English only |
| WG(s): 5 | 2nd FG IPTV meeting: Busan , 16-20 October 2006 |
| CONTRIBUTION |
| Source: | CATR / MII, China |
| Title: | Proposal on some interfaces between an IPTV end system and the other components |

# 1. Abstract

This contribution proposes some interfaces between an IPTV end system and the other IPTV system components defined in the IPTV architecture.  The interfaces described here can be viewed as the external interfaces, if compared to the “internal” interfaces described in the first meeting WG5 FGIPTV OD-0019 draft.

# 2. Discussion

The IPTV end system is the service presentation point and a customer terminal of an end-to-end network in an IPTV system. Through an IP network, the IPTV end system exchanges the control and management information with other IPTV system components, and gets media contents from the network. Hence, the IPTV end system has some logical and physical interfaces with other IPTV system components. The interfaces among an IPTV end system and the other IPTV system components are showed in figure 1.

Figure1  The interfaces among an IPTV end system and the other components

Content provision related interface: the interface between a customer and a content provider for content protection and other reasons, the functions may include getting a DRM licence, etc.

Management and security related interface: the interface between a consumer and management/security systems for terminal management and security, the functions may include terminal equipment management, authentication, etc.

Service related interface: the interface between a consumer and a service provider for service operation, the functions may include the exchange a subscriber’s service management/state management information, retrieve the portal navigation and the service selection information, etc.

Media Delivery related interface: the interface between a content delivery system and a customer terminal for media content transmission, the functions may include the distribution of media streaming and/or the customer’s control information to media, etc.

# 3. Proposal

It is proposed to discuss the interfaces between IPTV end system and other system components in WG5 and added to the current OD or to start a new draft.

_______________