|  | INTERNATIONAL TELECOMMUNICATION UNION | Focus Group On IPTV |
| --- | --- | --- |
|  | TELECOMMUNICATION STANDARDIZATION SECTOR STUDY PERIOD 2005-2008 | FG IPTV-IL-0062 |
|  |  | English only |
| WG(s): 1, 5 & 6 |  | 4th FG IPTV meeting: Bled, Slovenia, 7-11 May 2007 |
| INCOMING LIAISON STATEMENT (Ref.: Document 6M/TEMP/87) |
| Source: | ITU-R Working Party 6M |
| Title: | Liaison reply to ITU-T FG-IPTV (WGs 1, 5 And 6) on Retransmission of free-to-air broadcast content over IPTV |

Source:		Document 6M/TEMP/87

Subject:		Question ITU-R 13/6 and 101/6

Working Party 6M

LIAISON REPLY to ITU-T FG-IPTV (WGs 1, 5 and 6)
on retransmission of free-to-air broadcast content
over IPTV

ITU-R Working Party 6M thanks ITU-T FG-IPTV for its information on the development of IPTV system. In response to your request regarding broadcaster’s concern and other issues as described in Document 6M/164, and as a result of review of your document FG IPTV-DOC-0069, the comments are provided in the Annex.

ITU-R Working Party 6M welcomes any information on further development and keep ITU-T FG-IPTV informed on any further development.

Annex

As a result of review of the Document FG IPTV-DOC-0069, following matters arise for consideration for retransmission of free-to-air broadcast content over IPTV.

1)	Middleware aspect

IPTV services can comprise interactive TV applications. Recommendations ITU-R BT.1699 and ITU-R BT.1722 are Recommendations of harmonization of declarative and procedural content format respectively for broadcast content. These Recommendations would enable proper presentation and interactivity for broadcast programme content over IPTV.

2)	Content protection issue

Followings are comments on this issue for retransmission of free-to-air broadcast content, from the viewpoint of Recommendation ITU-R BT.1736.

–	Retransmitted free-to-air broadcast content should be handled such as to conform to the content protection assigned by the content provider.

–	In clause 7.6, redistribution control capability for external interfaces to transmit captions and information provided by On Screen Display facilities will be required to conform to the content protection assigned by the content provider.

3)	Privacy protection issue

Report ITU-R BT.2052 describes overall analysis of end-user’s privacy protection in interactive broadcast chain. In the case of retransmission of free-to-air broadcast content, section 4 through 6 of this Report provide useful information on this issue.

4)	Delivery control of retransmission

In case that delivery control for retransmission of free-to-air broadcast content is needed, the IPTV system is requested to provide such functionality. ITU-T Recommendation J.281 describes the requirement of similar control.

5)	Provision of Emergency broadcast

Recognizing the need and the importance of emergency broadcasting, ITU-R has developed the Recommendations ITU-R BT.1774 and ITU-R BO.1774. Support of this function by IPTV system may be required depending on the national regulations.

________________