|  | INTERNATIONAL TELECOMMUNICATION UNION | Focus Group On IPTV |
| --- | --- | --- |
|  | TELECOMMUNICATION STANDARDIZATION SECTOR STUDY PERIOD 2005-2008 | FG IPTV-IL-0073 |
|  |  | English only |
| WG(s): 2 |  | 5th FG IPTV meeting: Geneva, 23-31 July 2007 |
| INCOMING LIAISON STATEMENT (Ref.: COM 12 – LS 81) |
| Source: | Study Group 12, Rapporteurs' Group for Q 17/12 (Geneva, 4-6 June 2007) |
| Title: | Reply to LS on Performance Monitoring for IPTV |

|  | INTERNATIONAL TELECOMMUNICATION UNION | COM 12 – LS 81 – E |
| --- | --- | --- |
|  | TELECOMMUNICATION STANDARDIZATION SECTOR STUDY PERIOD 2005-2008 |  |
|  |  | English only Original: English |
| Question(s): | 17/12 | Geneva, 4-6 June 2007 |
| LIAISON STATEMENT |
| Source: | Study Group 12, Rapporteurs' Group for Q 17/12 (Geneva, 4-6 June 2007) |
| Title: | Reply to LS on Performance Monitoring for IPTV |
| LIAISON STATEMENT |
| To: | IPTV FG |
| Approval: | Agreed to at the Rapporteurs' Group meeting |
| For: | Action/Comment |
| Deadline: | September 2007 |
| Contact: | A.C.Morton, Q17 Rapporteur AT&T USA | Tel:+1 732-420-1571 Fax:+1 732-368-1192 Email: acmorton@att.com |

SG 12, Question 17/12 noted with interest your LS informing us of your latest draft documents.

Regarding OD-87, “Traffic Management Mechanism for the Support of IPTV Services”, Table 2 on Y.1541 class assignments, it seems possible that a standard definition Download VOD application (to hard drive) with play-out <4 Mb/s could be satisfied with the loss ratio of Class 2, or Class 3 with <200 ms delay commitment, and HD Download VOD could be satisfied with Class 6, or Class 7 with <200 ms delay commitment. Delay is a factor in the throughput of a retransmission protocol, and we assume that TCP will be used as Appendix IX/Y.1541.

HD Network PVR seems correctly aligned with Class 6, or Class 7 with <200 ms delay commitment.

The Multiplayer game application should probably avoid the >100 ms delay in Class 1, and be restricted to Class 0. We assumed that MOD is Music on Demand.

The meeting agreed that this is a good summary of the QoS Mechanisms and features that will be needed to support IPTV services throughout the architecture.

____________