## Slide 1
Energy COnsumption NETworks
Prof. Raffaele Bolla
(raffaele.bolla@unige.it)
National Inter-University Consortium for Telecommunications (CNIT)
C/o DIST- University of Genoa
ITU Workshop “Moving to a Green Economy through ICT Standards”
Rome 6-8 September 2011
Session 8: Connecting Research to the Market through Green ICT Standardization

## Slide 2: Summary
  General data
  Motivations
  Main ideas
  Project approach
  Estimated impact
  Current lessons
  Example
  Conclusions

## Slide 3
Project data at a glance | 
Project duration | October 2010 – September 2013 (36 months)
Consortium | 15 partners from 8 countries and 2 American University associated
Project budget | 10.5 M€ (6.2 M€ from EU)
Resources | 1168 PM (33 full time persons for three years)
Website | http://www.econet-project.eu

## Slide 4: The ECONET Consortium
4
Participant organisation name | Short name | Country
Consorzio Nazionale Interuniversitario per le Telecomunicazioni – UdR at DIST University of Genoa (Coordinator) | CNIT | Italy
Mellanox Technologies | MLX | Israel
Alcatel Lucent | ALU | Italy
Lantiq | LQDE | Germany
Ericsson Telecomunicazioni S.p.A. | TEI | Italy
Telecom Italia | TELIT | Italy
Greek Research & Technology Network | GRNET | Greece
Research and Academic Computer Network | NASK | Poland
Dublin City University | DCU | Ireland
VTT Technical Research Centre | VTT | Finland
Warsaw University of Technology | WUT | Poland
NetVisor | NVR | Hungary
Ethernity | ETY | Israel
LightComm | LGT | Italy
InfoCom | INFO | Italy
Portland State University | PSU | USA
University of South Florida | USF | USA

## Slide 5: Motivations
Increasing the energy efficiency and the sustainable growth of our world is a global process where Telecommunications technologies (and the ICTs in general) play a key role.
But to obtain optimum results the process should involve the “two faces of the same coin”:
  Green ICT – reducing the carbon footprint of ICT
  ICT for Green – using ICT for reducing third party-wastes.
ECONET is dealing with the first aspect
  Focused on short and medium time exploitation

## Slide 6: Motivations
Today’s network infrastructures are characterized by:
  design capable to deal with strong requests and constraints in terms of resources and performances (for networking: huge loads, very low delay, high availability, ….)
  Services characterized by high variability of load and resource requests along time (burstness, rush hours, …)
The solution:
  Smart power management: energy consumption should follow the dynamic of the service requests.
  Flexibility in resource usage: virtualization and aggressive sharing of physical resources

## Slide 7: The Main Ideas
Re-Engineering
Energy-efficient Silicon
Complexity Reduction
Power Scaling
Low Power Idle
Dynamic Adaptation
Proxying Network Presence
Virtualization
Smart Standby
Energy profile
Smart Standby
Active state 1
Active state n-1
Active state n
Idle state
Standby
Full
Loaded
Low
Load
Idle
(for short periods)
Idle
(for long periods)
…..
…..
Energy Consumption
Low
Max
Near to zero
Dynamic Adaptation
Power Scaling
Low Power Idle

## Slide 8: The Main Objectives
The ECONET project aims at studying and introducing adaptive technologies (standby and performance scaling) that allow saving energy when a network device or part of it is not used in wire-line networks.
  Access/home -> standby when users are not “connected”; idle/performance scaling when users are “connected”
  Core/metro -> standby for redundant and unused HW; idle/performance scaling for active HW
The final objective is to obtain an average consumption reduction of 50-80%
The ambition is to produce a feasible and concrete solution exploitable within very few years to improve the behaviour of the current equipment and architecture.
This goal is also pursued by
  promoting bridging actions between the Research/Academia and the Standardization arena to guarantee early and effective adoption of the new energy efficient techniques.
  exploiting clustering activities with other projects running on same green subject

## Slide 9: The Project Approach

## Slide 10: The Project Approach

## Slide 11: The Estimated Impact
Network load statistics and topology data
2015-2020 network forecast: device density and energy requirements
(example based on Italian network)
customers per DSLAM | 640
average usage of a network access | 30%
average traffic when a user is connected | 10%
redundancy degree for metro/transport devices | 13%
redundancy degree for core devices | 100%
redundancy degree of metro/transport device links | 100%
redundancy degree of core device links | 50%
average traffic load in metro networks | 40%
average traffic load in core networks | 40%
standby efficiency | 85%
performance scaling efficiency | 50%
network-wide control efficiency | 20%
air cooling/power supply efficiency | 15%
Home/Access
Metro/Transport/Core
target
Source: forecast based on: carrier grade topologies; traffic analysis and indicators (ETSI TR 102530, ODYSSEE) and projected traffic load.
 | power consumption (Wh) | number of devices | overall consumption (GWh/year)
Home | 10 | 17,500,000 | 1,533
Access | 1,280 | 27,344 | 307
Metro/transport | 6,000 | 1,750 | 92
Core | 10,000 | 175 | 15
Sources: 1) BroadBand Code of Conduct V.3 (EC-JRC) and “inertial” technology improvements to 2015-2020 (home and access cons.)
2) Telecom Italia measurements and evaluations (power consumption of metro/core network and number of devices)
 | Data Plane | Control Plane | Cooling/Power Supply
Home | 79% | 3% | 18%
Access | 84% | 3% | 13%
Metro/transport | 73% | 13% | 14%
Core | 54% | 11% | 35%
Device internal sources of energy consumption
Sources: Information from vendors.
Sources: BroadBand Code of Conduct V.3 (EC-JRC) and technology improvements to 2015-2020.

## Slide 12: The Estimated Impact
Chart: 
| Stanby | Active
 | 0.7 | 0.3
Full Load
Idle
Standby
Full Load
Idle
Standby
Full Load
Idle
Standby
Full Load
Idle
Standby
Chart: 
| Active | Stanby | Network-wide Control | Redundant HW
 | 0.375 | 0.09375 | 0.53125
Chart: 
| Active | Stanby | Network-wide Control | Redundant HW
 | 0.3 | 0.075 | 0.625
Overall Energy Gains |  |  |  |  |  |  |  |  |  |  | 
 | full load power consumption (Wh) | number of devices | Overall full consumption (GWh/year) |  | Gains | Energy gains with ECONET technologies (GWh /year) |  |  |  |  | 
Home | 10 | 17,500,000 | 1533 |  | 70% | 1060 |  |  |  |  | 
Access | 1,280 | 27,344 | 307 |  | 70% | 213 |  |  |  |  | 
Metro/transport | 6,000 | 1,750 | 92 |  | 54% | 49 |  |  |  |  | 
Core | 10,000 | 175 | 15 |  | 58% | 9 |  |  |  |  | 
 |  |  |  | Overall gain | 68% |  |  |  |  |  | 
 | Total BAU [GWh / year] |  |  | 1947 | Total ECONET gains [GWh / year] |  |  |  |  | 1331 | 
Energy effic. target
State dependent energy consumption of devices
Network load statistics and topology data
Home/access
Network load statistics and topology data
Metro/transport/core
Chart: Home
| 0.0 | 2.0 | 3.0 | 4.0
 | 10 | 7.61 | 5.22
 | 1.755 | 1.755
Chart: Access
| 0.0 | 2.0 | 3.0 | 4.0
 | 1280 | 1007.68 | 735.36
 | 224.64 | 224.64
Chart: Transport
| 0.0 | 2.0 | 3.0 | 4.0
 | 6000 | 4842 | 3684
 | 1563 | 1563
Chart: Core
| 0.0 | 2.0 | 3.0 | 4.0
 | 10000 | 8387.5 | 6775
 | 2435 | 2435
Customers’ savings | 1060 GWh/year
Networks’ savings | 270 GWh/year
Per-customer money savings
 | Direct (Home) | Indirect (Telco) | Total
At today’s energy cost | 12€ | 2€ | 14€
At 2020 energy cost* | 30€ | 6€ | 36€
* Based on past 5-year trends in energy costs after inflation

## Slide 13: Lessons from the project
Energy efficiency key aspects :
  Flexibility and Smartness
    capability of moving functionalities and tasks along the network (virtualization at different levels).
    exploiting the flexibility capabilities :
      by avoiding additional consumptions due to e.g. “side effects” .
      by effectively modelling device consumptions and performances versus load
  Integrated/holistic solutions
    Strict cooperation among different
      applications and services in the resource management for better resource and energy utilization.
      approaches and technologies in different fields (e.g. smart grids).
    take care about all the “side effects”
  Standards: get from standardization the future needs and architectures and offer to standardization tables proposals for efficiency improvement.

## Slide 14
Proxing for application layer
P2P application active -> PC should be maintained active along all the time
Homegateway
P2P application “energy aware”
Protocols for the functionality delegations
DSLAM
DSLAM
Protocols for managing the standby state
A simple example of integration
Current Situation
Everything active
(and consuming)
Smart Homegateway
with proxy capabilities
Zzzzz

## Slide 15: Conclusions
ECONET is
  enabling the fixed network devices to be energy adaptive and controllable;
  demonstrating the potential gain by exploiting the above capabilities in some typical devices.
  producing an effective solution exploitable in few years
Some aspects should be integrated within other contexts:
  Energy Flexibility and Smartness
  Standards
  Holistic approach