RECOMMENDATION  ITU-R  BO.1213-1

Reference receiving earth station antenna pattern
for the broadcasting-satellite service
in the 11.7-12.75 GHz band

(Question ITU-R 73/6)

(1995-2005)

Scope

This Recommendation intends to establish reference earth station co-polar and cross-polar antenna patterns for the broadcasting-satellite service (BSS) in the 11.7-12.75 GHz band.

The ITU Radiocommunication Assembly,

considering

a)	that a common reference antenna pattern was used at WRC-97 and WRC-2000 for revising the Regions 1 and 3 broadcasting-satellite service (BSS) Plan;

b)	that this same reference antenna pattern was used at WRC-03 for revising the inter and intraregional/inter- and intraservice sharing criteria contained in Appendix 30 of the Radio Regulations (RR);

c)	that data from measurements of BSS receiving antennas support this same reference antenna pattern1;

d)	that this same reference antenna pattern may be useful for interservice sharing between the BSS and other services and for other coordination purposes,

recommends

1	that the co-polar and cross-polar antenna patterns given by formulae provided in Annex 1 should be recognized as reference earth station antenna patterns for the BSS in the 11.7-12.75 GHz band.

Annex 1

Antenna pattern formulae:

These formulae are valid for D/λ ≥ 11:

Co-polar pattern:

for	0	(	(	<	(m

where:

G1 = 29 – 25 log (r, and

Gco (()  G1  	for	(m	(	( < (r

Gco (()  29 – 25 log 	for	r		b	where b = 10(34/25)

Gco (()  –5 dBi	for	b		  70

Gco (()  0 dBi	for	70		  180

Cross-polar pattern:

Gcross (()  Gmax – 25	for	     0     0.25  0

where 0

 3 dB beamwidth

for 0.25	(0		  0.44 0

Gcross ()  Gmax – 17	for 0.44	(0		  0

Gcross () = Gmax – 17 + C	for	(0 	≤ 	( < (1 where

and C = 21 – 25 log(1) – (Gmax – 17)*

Gcross (()  21 – 25 log 	for	1		 < 	where  = 10(26/25)

Gcross (()  –5 dBi	for	2		  70

Gcross (()  0 dBi	for	70º	(	(  180º

where:

D:	equivalent antenna diameter

(:	wavelength expressed in the same unit as the diameter

:	off-axis angle of the antenna relative to boresight (degrees)

η:	antenna efficiency.

Examples:

For the 60 cm reference antenna pattern used at WRC-03 for revising the interregional/interservice sharing criteria contained in RR Appendix 30, the following parameters apply:

Co-polar:

Gmax	  35.5 dBi

η	=  0.65

D/(	  23.4 (assumed frequency is 11.7 GHz)

(m	  3.98

(r	  4.06

G1	  13.78 dB

(b	  10 (34/25)

Cross-polar:

(0		=  2.96º

(1		=  4.73º

(2		  10.96º

C		=  –14.36 dB

The corresponding reference antenna pattern is given in Fig. 1.

For the 45 cm reference antenna pattern used at WRC-03 for revising the interregional/interservice sharing criteria contained in RR Appendix 30, the following parameters apply:

Co-polar:

Gmax	=  33.3 dBi

η	=  0.65

D/(	=  18.3 (assumed frequency is 12.2 GHz)

(m	=  5.15°

(r	=  5.19°

G1	=  11.12 dB

(b	=  10(34/25)

Cross-polar:

(0 =  3.79°

(1 =  6.04°

(2 =  10.96°

C =  –14.83 dB

The corresponding reference antenna pattern is given in Fig. 2.

# Footnotes

1	It should be noted that the antenna measurements were performed on single-feed antennas.

*	The value of C must be less than 0 for any combination of antenna efficiency (η) and D/λ.