RECOMMENDATION  ITU-R  F.1496

RADIO-FREQUENCY  CHANNEL  ARRANGEMENTS  FOR  RADIO-RELAY  SYSTEMS 
IN  THE  FIXED  SERVICE  OPERATING  IN  THE  BAND  51.4-52.6  GHz

(Question ITU-R 108/9)

(2000)

Rec. ITU-R F.1496

The ITU Radiocommunication Assembly,

considering

a)	that the band 51.4-52.6 GHz is allocated to the fixed and mobile services on a primary basis;

b)	that RR No. S5.547 identifies the 51.4-52.6 GHz band as being available for high-density applications in the fixed service (FS);

c)	that ITU-R should develop radio-frequency channel arrangements in order to make the most effective use of the spectrum available;

d)	that the propagation characteristics of the 51.4-52.6 GHz band are ideally suited for use of short-range digital point-to-point radio links in high-density applications in the FS networks;

e)	that in the frequency range a high antenna directivity is achievable even with small size antennas, increasing the density of equipment and further reducing risk of interference with same and other radio services;

f)	that differing applications licensed by various administrations may require different radio-frequency channel arrangements;

g)	that the applications in this frequency band may require differing channel bandwidths;

h)	that several radio services with various transmission signal characteristics and capacities may be in simultaneous use in this frequency band;

j)	that a high degree of compatibility between radio-frequency channels of different arrangements can be achieved by selecting channel centre frequencies within a homogeneous basic pattern,

recommends

1	that administrations consider the channel arrangement given in Annex 1 for FS system deployment in the frequency range 51.4-52.6 GHz.

ANNEX  1

Radio-frequency channel arrangement in the band 51.4-52.6 GHz

The radio-frequency channel arrangement for channel separations of 56 MHz, 28 MHz and 14 MHz shall be derived as follows:

Let			be the reference frequency of 51 412 MHz,

be the centre frequency (MHz) of the radio-frequency channel in the lower half of the band,

be the centre frequency (MHz) of the radio-frequency channel in the upper half of the band,

Tx/Rx separation  616 MHz,

band separation  112 MHz,

then the frequencies (MHz) of individual channels are expressed by the following relationships:

a)	for systems with a channel separation of 56 MHz:

lower half of the band:	  fr  56 n

upper half of the band:	  fr  616  56 n

where:

n  1, 2, … 9

b)	for systems with a channel separation of 28 MHz:

lower half of the band:	  fr  14  28 n

upper half of the band:	  fr  630  28 n

where:

n  1, 2, 3, … 18

c)	for systems with a channel separation of 14 MHz:

lower half of the band:	  fr  21  14 n

upper half of the band:	  fr  637  14 n

where:

n  1, 2, 3, … 36.

ANNEX  2

TABLE  1

Calculated parameters according to Recommendation ITU-R F.746

| XS (MHz) | n | f1 (MHz) | fnmax (MHz) | (MHz) | (MHz) | Z1S (MHz) | Z2S (MHz) | YS (MHz) | DS (MHz) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 56 | 1, ... 9 | 51 468 | 51 916 | 52 084 | 52 532 | 68 | 68 | 168 | 616 |
| 28 | 1, ... 18 | 51 454 | 51 930 | 52 070 | 52 546 | 54 | 54 | 168 | 616 |
| 14 | 1, ... 36 | 51 447 | 51 937 | 52 063 | 52 533 | 47 | 47 | 168 | 616 |
| XS: separation between centre frequencies of adjacent channels YS: separation between centre frequencies of the closest go and return channels Z1S: separation between the lower band edge and the centre frequency of the first channel Z2S: separation between centre frequencies of the final channel and the upper band edge DS: duplex spacing |