RECOMMENDATION  ITU-R P.1510

Annual mean surface temperature

(Question ITU-R 201/3)

(2001)

The ITU Radiocommunication Assembly,

considering

a)	that information on annual mean surface temperature is needed for propagation modelling purposes;

b)	that the information is needed for all locations of the globe, especially when regional or continental calculations are necessary,

recommends

1	that the data in Annex 1 be used to obtain the annual mean surface temperature when no local data are available. For easy reference the data are also shown in Fig. 1.

ANNEX  1

# 1	Surface mean annual temperature

The data file ESATEMP.TXT contains the annual mean surface temperature (C) at 2 m above the surface of the Earth with a resolution of 1.5 in both latitude and longitude. The companion data files ESALAT.TXT and ESALON.TXT contain respectively the latitudes and longitudes of the corresponding entries (gridpoints) in data file ESATEMP.TXT.

The data are from 0 to 360 in longitude and from +90 to –90 in latitude. For a location different from the gridpoints, the temperature at the desired location can be derived by performing a bi-linear interpolation on the values at the four closest grid points.

The data files can be obtained from the ITU Radiocommunication Bureau (BR).