RECOMMENDATION  ITU-R  P.368-7*

GROUND-WAVE  PROPAGATION  CURVES  FOR  FREQUENCIES
BETWEEN  10  kHz  AND  30  MHz

(1951-1959-1963-1970-1974-1978-1982-1986-1990-1992)

Rec. 368-7

The ITU Radiocommunication Assembly,

considering

that, in view of the complexity of the calculation, it is useful to have a set of ground-wave curves for a range of standard frequency values and ground characteristics,

recommends

1.	that the curves of Annex 1, applied in the conditions specified below, should be used for the determination of ground-wave field strength at frequencies between 10 kHz and 30 MHz;

2.	that, as a general rule, these curves should be used to determine field strength only when it is known that ionospheric reflections will be negligible in amplitude;

3.	that these curves should not be used in those applications for which the receiving antenna is located well above the surface of the Earth;

Note 1 – That is, when r  <<  60  the curves may be used up to a height h    1.2 1/2 3/2. Propagation curves for terminal heights up to 3 000 m and for frequencies up to 10 GHz can be found in the separately published ITU Handbook of Curves for Radio-Wave Propagation over the Surface of the Earth;

4.	that these curves, plotted for homogeneous paths under the conditions established in Annex 1, may also be used to determine the field strength over mixed paths as indicated in Annex 2.

ANNEX  1

Propagation curves and conditions of validity (homogeneous paths)

The propagation curves in this Recommendation are calculated for the following assumptions:

–	they refer to a smooth homogeneous spherical Earth;

–	in the troposphere, the refractive index decreases exponentially with height, as described in Recommendation
ITU-R P.453;

–	both the transmitting and the receiving antennas are at ground level;

–	the radiating element is a short vertical monopole. Assuming such a vertical antenna to be on the surface of a perfectly conducting plane Earth, and excited so as to radiate 1 kW, the field strength at a distance of 1 km would be 300 mV/m; this corresponds to a cymomotive force of 300 V (see Recommendation ITU-R P.525);

–	the curves are drawn for distances measured around the curved surface of the Earth;

–	the curves give the value of the vertical field-strength component of the radiation field, i.e. that which can be effectively measured in the far-field region of the antenna.

Note 1 – The inverse-distance curve shown as a broken line in the figures, to which the curves are asymptotic at short distances, passes through the field value of 300 mV/m at a distance of 1 km. To refer the curves to other reference antennas, see Table 1 of Recommendation ITU-R P.341.

Note 2 – The curves were calculated using the computer program GRWAVE which is briefly described in Annex 3.

Note 3 – The basic transmission loss corresponding to the same conditions for which the curves were computed may be obtained from the value of field strength E(dB(V/m)) by using the following equation:

For the influence of the environment on both the transmitting and the receiving antenna, refer to Recommendation ITU-R P.341.

Note 4 – The curves give the total field at distance, r, with an error less than 1 dB when k r is greater than about 10, where k    2/. Near-field (i.e. induction and static field) effects may be included by increasing the field strength (in decibels) by:

This gives the total field within  0.1 dB for sea and wet ground, and within  1 dB for any ground conductivity greater than 10 –3 S/m.

Note 5 – For either antenna, if the antenna site location is higher than the average terrain elevation along the path between the antennas, then the effective antenna height is the antenna height above the average terrain elevation along the path. This effective antenna height value should be compared to the computed value of antenna height limit in recommends 3 to determine if the curves are valid for the path.

Figures 1 to 11 contain field-strength curves as a function of distance with frequency as a parameter.

Figure  1  [D01]  = PAGE PLEINE

Figure  2  [D02]  = PAGE PLEINE

Figure  3  [D03]  = PAGE PLEINE

Figure  4  [D04]  = PAGE PLEINE

Figure  5  [D05]  = PAGE PLEINE

Figure  6  [D06]  = PAGE PLEINE

Figure  7  [D07]  = PAGE PLEINE

Figure  8  [D08]  = PAGE PLEINE

Figure  9  [D09]  = PAGE PLEINE

Figure  10  [D10]  = PAGE PLEINE

Figure  11  [D11]  = PAGE PLEINE

ANNEX  2

Application to mixed paths (inhomogeneous paths)

1.	Figures 14 to 50 of this Annex may be used for the determination of propagation over mixed paths (non-homogeneous smooth Earth) as follows:

Such paths may be made up of sections S1, S2, S3, etc., of lengths d1, d2, d3, etc., having conductivity and permittivity 1, 1; 2, 2; 3, 3, etc., as shown below for three sections:

Figure  [D11a]  2,5 cm = 98 %

The Millington method used in this Annex for determining propagation over mixed paths is the most accurate available and satisfies the reciprocity condition. The method assumes that the curves are available for the different types of terrain in the sections S1, S2, S3, etc., assumed to be individually homogeneous, all drawn for the same source T defined, for instance, by a given inverse-distance curve. The values may then finally be scaled up for any other source.

For a given frequency, the curve appropriate to the section S1 is then chosen and the field E1(d1) in dB(V/m) at the distance d1 is then noted. The curve for the section S2 is then used to find the fields E2(d1) and E2(d1  d2) and, similarly, with the curve for the section S3, the fields E3(d1  d2) and E3(d1  d2  d3) are found, and so on.

A received field strength ER is then defined by:

(1)

The procedure is then reversed, and calling R the transmitter and T the receiver, a field ET is obtained, given by:

(2)

The required field is given by ½ [ER  ET], the extension to more sections being obvious.

The method can in principle be extended to phase changes if the corresponding curves for phase as a function of distance over a homogeneous earth are available. Such information would be necessary for application to navigational systems. The method is generally easy to use, particularly with the aid of a computer.

2.	For planning purposes where the coverage of a certain transmitter is needed, a graphical procedure, based on the same method, is convenient for a rough and quick estimation of the distance at which the field strength has a certain value.

A short description of the graphical method is given here.

Figure 12 applies to a path having two different sections characterized by the values 1, 1 and 2, 2, and extending for distances d1 and d2, respectively. It is supposed that the modulus of the complex permittivity (dielectric constant)  (1, 1)  is greater than  (2, 2) . For the distances d  d1 the field-strength curve obtained by the Millington method (§ 1) lies between the curves corresponding to the two different electrical properties E(1, 1) and E(2, 2). At the distance d = 2 d1, where d1 is the distance from the transmitter to the border separating the two sections, the curve goes through the mid-point between the curves E(1, 1) and E(2, 2) provided that the field strength is labelled linearly in decibels. In addition, the same curve approaches an asymptote, which differs by m dB from the curve E(2, 2) as indicated in Fig. 12, where m is half the difference in decibels between the two curves E(1, 1) and E(2, 2) at d = d1. The point at d = 2 d1 and the asymptote make it easy to draw the resulting field-strength curve.

Figure  12  [D12] 12cm = 460 %

Figure 13 shows the curve for a two-section path with electrical constants changing from 2, 2 to 1, 1 where the modulus of the complex permittivity  (1, 1)    (2, 2) . The above-mentioned procedure can be applied here bearing in mind that the asymptote is now parallel to the curve of the E(1, 1).

For paths consisting of more than two sections, each change can be considered separately in the same way as the first change. The resulting curve has to be a continuous curve, and the portions of curves are displaced parallel to the extrapolated curve at the end of the previous section.

The accuracy of the graphical method is dependent on the difference in slope of the field-strength curves, and is therefore to an extent dependent on the frequency. For the LF band, the difference between the method described in § 1 and this approximate method is normally negligible, but for the highest part of the MF band the differences in most cases will not exceed 3 dB.

Figures 14 to 50 contain field-strength curves as a function of distance with the electrical characteristics of the ground as a parameter.

Figure  13  [D13]  12 cm = 460 %

Figure  14  [D14]   PAGE PLEINE

Figure  15  [D15]   PAGE PLEINE

Figure  16  [D16]   PAGE PLEINE

Figure  17  [D17]   PAGE PLEINE

Figure  18  [D18]   PAGE PLEINE

Figure  19  [D19]   PAGE PLEINE

Figure  20  [D20]   PAGE PLEINE

Figure  21  [D21]   PAGE PLEINE

Figure  22  [D22]   PAGE PLEINE

Figure  23  [D23]   PAGE PLEINE

Figure  24  [D24]   PAGE PLEINE

Figure  25  [D25]   PAGE PLEINE

Figure  26  [D26]   PAGE PLEINE

Figure  27  [D27]   PAGE PLEINE

Figure  28  [D28]   PAGE PLEINE

Figure  29  [D29]   PAGE PLEINE

Figure  30  [D30]   PAGE PLEINE

Figure  31  [D31]   PAGE PLEINE

Figure  32  [D32]   PAGE PLEINE

Figure  33  [D33]   PAGE PLEINE

Figure  34  [D34]   PAGE PLEINE

Figure  35  [D35]   PAGE PLEINE

Figure  36  [D36]   PAGE PLEINE

Rec. 368-7

Figure  37  [D37]   PAGE PLEINE

Figura 38  [D38]   PAGE PLEINE

Figure  39  [D39]   PAGE PLEINE

Figure  40  [D40]   PAGE PLEINE

Figure  41  [D41]   PAGE PLEINE

Figure  42  [D42]   PAGE PLEINE

Figure  43  [D43]   PAGE PLEINE

Figure  44  [D44]   PAGE PLEINE

Figure  45  [D45]   PAGE PLEINE

Figure  46  [D46]   PAGE PLEINE

Figure  47  [D47]   PAGE PLEINE

Figura 48  [D48]   PAGE PLEINE

Figura 49  [D49]   PAGE PLEINE

Figure  50  [D50]   PAGE PLEINE

ANNEX  3

Generation of propagation curves

The computer program GRWAVE has been used to generate the propagation curves in Annexes 1 and 2. GRWAVE performs the calculation of ground-wave field strength in an exponential atmosphere as a function of frequency, antenna heights and ground constants; approximate frequency range 10 kHz-10 GHz.

The program is available, with documentation, from that part of the ITU-R website dealing with Radiocommunication Study Group 3.

# Footnotes

* 	Radiocommunication Study Group 3 made editorial amendments to this Recommendation in 2000 in accordance with Resolution ITU-R 44.