RECOMMENDATION  ITU-R  P.839-3

Rain height model for prediction methods

(Question ITU-R 201/3)

(1992-1997-1999-2001)

The ITU Radiocommunication Assembly,

considering

a)	that information is required regarding the height to which rain extends during periods of precipitation,

recommends

1	that for areas of the world where no specific information is available, the mean 0( C isotherm height above mean sea level, h0, be obtained from the data file ESA0HEIGHT.TXT (the data file may be obtained from the ITU Radiocommunication Bureau (BR));

2	that the mean rain height above mean sea level, hR, may be obtained from the 0 C isotherm as:

hR = h0 + 0.36 km

3	that for easy reference, values can be taken from Fig 1.

NOTE 1 – The data file ESA0HEIGHT.TXT contains the 0 C isotherm height above mean sea level (km) with a resolution of 1.5° in both latitude and longitude. The companion data files ESALAT.TXT and ESALON.TXT contain respectively the latitudes and longitudes of the corresponding entries (gridpoints) in data file ESA0HEIGHT.TXT.

The data are from 0 to 360 in longitude and from +90 to –90 in latitude. For a location different from the gridpoints, the 0( C isotherm height above mean sea level at the desired location can be derived by performing a bilinear interpolation on the values at the four closest gridpoints.

The data files can be obtained from the BR.