RECOMMENDATION  ITU-R  SM.1052

AUTOMATIC  IDENTIFICATION  OF  RADIO  STATIONS

(Question ITU-R 34/1)

(1994)

Rec. ITU-R SM.1052

The ITU Radiocommunication Assembly,

considering

a)	that the Radio Regulations require that all transmissions shall be capable of being identified either by identification signals or by other means;

b)	that the variations in the types of automatic data transmission systems are increasing;

c)	that the identification of such data transmission systems made manually is very time consuming;

d)	that there are methods of identification by automatic system analysis,

recommends

1.	that modern microprocessor technology-based equipment should be used to assist in identification;

2.	that for the HF-range the equipment perform at least:

–	measurement of frequency shift;

–	measurement of baud rate;

–	continuous analysis of the transmission code;

–	text output for standard code signals (for the most used codes see Annex 1);

3.	that for VHF range, the following identification signal format is accepted:

| Bit synchronization | Frame synchronization | Data | Error correction |
| --- | --- | --- | --- |

ANNEX  1

Bases for the named systems are the alphabets ITA number 2/3/5 and SITOR. One way or another those alphabets are involved in the codes of the named systems.

| ITA2 | ITA3 | ITA5 | SITOR | Special |
| --- | --- | --- | --- | --- |

BAUDOT

BAUDOT – CYRILLIC

BAUDOT – ARABIC

ARQ-1000 duplex

ARQ-N

TORG 10-11

UN-ARQ

HC-ARQ

ARTRAC

F7 Baudot/Morse

FEC-100

AUTOSPEC

HNG-FEC

Piccolo mk 6/2

Coquelet mk 1

Coquelet mk 2

ARQ – E3

TOR 342 1 channel

TOR 342 2 channel

TOR 342 4 channel

TOR 242 2 channel

ARQ-1000 simplex

ARQ-6 70

FEC-100 simplex

ASCII

PACKET

Piccolo mk 6/5

TRA-2300

PAC-TOR

POL_ARQ

Simplex TOR-A

Simplex TOR-B

ARQ-SWE

ARQ-6 98

ARQ-6 90

F7B –1 –2 –3 –4 –5 –6

Russ. Piccolo		–1
			–2
			–3
			–4

ROU-FEC

RS-ARQ

SITA (VHF)

POCSAC (VHF)

FACSIMILE