## Slide 1: ITU Regional Workshop on SMS4DC for English Speaking countries in Africa, Abuja, Nigeria , 20-31-May 2013

## Slide 2: Earth Station Using SMS4DC
Prepared by :
Eng.yasir Mohammed Bashar
Yasir_192@ntc.gov.sd

## Slide 3
Import Space Radio-communication Station (SRS) Database
into SMS4DC

## Slide 4
Step1: choose (Import from SRS) opting from Database menu
Import (SRS) Database
into SMS4DC

## Slide 5
Import from SRS: This item imports information of Earth stations which belong to one or more administrations, into the SMS4DC database. The information source must be an “mdb” file having a data format identical with the BR SRS database format (including space BR IFIC and electronic notices).
As will be displayed in the next slide, choosing this item opens the “SRS import” dialogue box and provides a mask to specify the source database (with mdb extension) and one or more administrations whose Earth station information is to be imported. The browse button enables the user to find the correct “mdb” file location.
After choosing the administration(s) of interest and pushing the “Import” button, SMS4DC displays a Yes/No dialogue screen and the number Earth station records available for import (according to the administrations selected). This screen enables the user to continue or abandon the data import. A progress bar is included at the bottom of the main import screen.
Import (SRS) Database
into SMS4DC

## Slide 6
Import (SRS) Database
into SMS4DC
Step2: select the MDB source and the administration

## Slide 7
Import (SRS) Database
into SMS4DC
Step3: choose (Display selected Stations) option from Database menu

## Slide 8
Import (SRS) Database
into SMS4DC
Step4: select any number of selected earth stations to be Shown

## Slide 9
How to Create a new earth Station with SMS4DC

## Slide 10
 First: Create an Earth Station with general Information (Station Information).
 Second: Create the Uplink or Downlink beams for the Earth Station (Antenna Information).
 Third: Establish the frequencies for each beam (Downlink or Uplink)(frequencies Information).
Steps to Create a new earth Station with SMS4DC in Brief
Creation of Earth Station

## Slide 11
1: Create Earth Station by pressing and moving earth station symbol button a and place “Earth Stations icon in DEM map.
Add new Earth Station

## Slide 12
2: Set the general parameters of new earth station
Earth Station General Parameters

## Slide 13
3 : Go to Database>> license and find your station under anonymous station to set additional parameters
Earth Station Information (1/2)

## Slide 14
Earth Station Information (2/2)

## Slide 15
4. Right Click on your Earth Station Name and then Press Add Beam in order to establish new Uplink beam
Add Beam (UP)

## Slide 16
Earth Station antenna information
4. Right Click on your Earth Station Name and then Press Add Beam in order to establish new Uplink beam

## Slide 17
Earth Station antenna information
4. Right Click on your Earth Station Name and then Press Add Beam in order to establish new Downlink beam

## Slide 18
By using the “Library” push button, a library of Earth station antenna patterns is opened and the user may select an existing antenna or define a new pattern, using the push button “New Pattern”. A new antenna pattern will be characterized by a set of new coefficients and, after definition, will be added to the library for selection.
Antenna Pattern (1/2)
4. Right Click on your Earth Station Name and then Press Add Beam in order to establish new Uplink beam
Library of antenna patterns of earth station
Entry mask of coefficients for a new antenna pattern

## Slide 19
In case of having no reference coefficients for earth station antenna pattern, the antenna gain values for different offset angles with respect to the antenna main beam direction may be entered directly into the SMS4DC database
Antenna Pattern (2/2)
The earth station antenna pattern definition entry table

## Slide 20
5. Under your Earth Station Name “UAE EARTH STATION NO 1” >> beam: beam 1 Press right click to establish a group of frequencies for the new Uplink.

## Slide 21
5. Under your Earth Station Name “UAE EARTH STATION NO 1” >> beam: beam 1 Press right click to establish a group of frequencies for the new Uplink.
Description of fields in the entry table of Group Information

## Slide 22
6: Set the emissions for the established group (UL)
Description of fields in the entry table of Emission Information

## Slide 23
Emissions: This item provides a list of emissions in the downlink and uplink directions. Selecting this item opens an entry table to define a multiple emission specification. At the top of table there are three push buttons to add new emissions, to delete registered emissions in the table and to save entered emissions into the database.
Description of fields in the entry table of Emission Information

## Slide 24
7. Right Click on your Earth Station Name “UAE EARTH STATION NO 1” and then Press Add Beam in order to establish new Downlink beam as follows

## Slide 25
9. Under your Earth Station Name “SUDAN EARTH STATION NO 1” >> beam: beam 1 Press right click to establish a group of frequencies for the new Downlink

## Slide 26
10. Set the emissions for the established group (Downlink).

## Slide 27
11: Set the class of station and nature of service and frequencies for the established group

## Slide 28
Class of Station (1/2)
This item sets class of stations and nature of services applicable to the group of beams. Selecting this item opens an entry table to define class of stations and nature of services using the relevant combo box.

## Slide 29
Class of Station (2/2)

## Slide 30
This item sets class of stations and nature of services applicable to the group of beams. Selecting this item opens an entry table to define class of stations and nature of services using the relevant combo box.
Nature of Service

## Slide 31
12. Right Click on your Earth Station Name “UAE EARTH STATION NO 1” and then Press notice in order to create notice
Class of Station

## Slide 32
Earth Station Coordination Contours

## Slide 33
COORDINATION OF EARTH STATIONS
WITH RESPECT TO TERRESTRIAL STATIONS
AS WELL AS (other) EARTH STATIONS
When ?
• Frequency bands allocated with equal rights to space and terrestrial services or earth stations operating in the Opposite Direction of Transmission (ODT)
The coordination area includes the territory of another country

## Slide 34
COORDINATION Area and Coordination Contours OF EARTH STATIONS
 Appendix
7 of the Radio Regulations
(RR)
contains the method for the determination of the
coordination area around a transmitting or receiving earth station that is sharing spectrum in frequency bands between 100 MHz and 105 GHz
with terrestrial radiocommunication services or
with earth stations operating in the opposite direction of transmission.
 Appendix
7 is based on ITU-R SM.1448
recommendation

## Slide 35
How to determine the coordination area around an earth station (1)
 The coordination area is determined on the basis of :
known characteristics for the coordinating earth station .
Conservative assumptions for the propagation path.
Conservative assumptions for the system parameters for the unknown terrestrial stations, or the unknown receiving earth.

## Slide 36
How to determine the coordination area around an earth station (2)
 Calculations are performed separately for great circle propagation mechanisms(propagation
mode (1)) and, if required by the sharing scenario for scattering from hydrometeors(propagation
mode (2)).
 The coordination contour is then determined using the greater of the two distances predicted by the propagation mode (1) and propagation mode (2) calculations for each azimuth around the coordinating earth station.

## Slide 37
Coordination Contours around an earth station using
SMS4DC

## Slide 38
Step one
From Window bar >> Launch IDWM Map1 by selecting IDWM Map1

## Slide 39
From option bar select >> RR appendix 7 >> Earth Station in order to choose the transmitting earth station.
Step Two (1/4)

## Slide 40
Step Two (2/4)
From option bar select >> RR appendix 7 >> Earth Station in order to choose the transmitting earth station.

## Slide 41
Step Two (3/4)

## Slide 42
optionally: you may want to view the input file which contains the selected earth station parameters needed to determine the coordination contour
Step Two (4/4)

## Slide 43
Step Three (1/2)
From option menu select >> RR appendix 7 >> Draw Contour

## Slide 44
Step Three (1/2)
From option menu select >> RR appendix 7 >> Draw Contour

## Slide 45
optionally you may need to change the contours styles for clarification
Step Four (1/3)

## Slide 46
optionally you may need to change the contours styles for clarification
Step Four (2/3)

## Slide 47
optionally you may need to change the contours styles for clarification
Step Four (3/3)

## Slide 48
optionally: you may want to view the Output file (RESULT.LST) to show details of calculation result

## Slide 49
Step Six
optionally: you may want to view the Output file (UPD.DAT) to show contour data

## Slide 50
Step Seven
Optionally: you may want to draw these contours on DEM Map

## Slide 51
Inference Calculation using
SMS4DC
Earth Stations

## Slide 52
Types of Interference Calculation
 Interference from selected transmitting earth station to receiving Fixed terrestrial Stations above 1 GHz.
 Interference to selected receiving earth station from transmitting Fixed terrestrial Stations above 1 GHz.
 Interference from selected transmitting earth stations to receiving earth stations

## Slide 54
References
Main References
2. ITU Training on Space Services (Bangkok, 24-27 April 2012).
3. ITU SMS4DC Training ( Jordan 2008).
4. SMS4DC V4 manual.
5- ITU-R, Radio Regulation BOOK