## Slide 1
Radio Interference Calculations
NBTC/ITU Workshop on Cross-Border Frequency Coordination
June 29 - 30, 2015
Bangkok, Thailand

## Slide 2
Basic Concepts of Measurements
How radio interference prediction helps
Filed strength measurements
Relevant ITU reports and Recommendations
What to expect in these slides

## Slide 3
Basic Concept of Measurement
    The measurement is the process of assigning a value to an attribute or phenomenon.
    The result is, in principle, independent of the procedure used.
    Nevertheless, the accuracy of the measurement process is essential to obtain a reliable value.

## Slide 4
Basic Concept of Measurement
    The measurement process should define
      Attribute or phenomenon to measure
Measurement of electromagnetic fields which could be characterized as either a value of E or H fields or as characteristics of a signal (frequency, amplitude, phase, bandwidth, etc.)
      Conditions of operations
Details of all conditions including influences caused by surrounding infrastructure, weather, limitation with measuring equipment (size of antenna, embedded equipment) have to be known to ensure the measurement is reproducible
      The measurement system and parameters to use
All devices involved in the measurement should be specified to take into account all parameters in the measurement result (type of equipment, characteristics and uncertainties)

## Slide 5
Basic Concept of Measurement
    The measurement process should define:
      Sequence of technical operations to apply.
A general description of how to perform the measurements is provided below:
The description of the measurement chain set up, including identification of equipment used.
The description of preliminary measurements to carry out (e.g. measurements to ensure that there’s no strong emitter at the measurement location which could lead to a wrong result).
Measuring device settings to be used (e.g. frequency band, resolution bandwidth (RBW), span, etc.)
Tasks to be achieved to carry out the measurement
Consistency of the result (e.g. checking of the result by comparison with theoretical reckoning, uncertainty calculation, etc.)
      Result reckoning and uncertainties
To provide a reliable value of the measurement, post-processing is necessary to take into account uncertainties of the measurement chain to assess the uncertainty of the final result.
The final step could be, if necessary, to specify the form of publication of the results.

## Slide 6
      Helps in
      Planning and co-ordinating a station
      Determine if special protection required?
      Determine if Co-ordination required?
      Having reference values for calculation of interfering field strength at specified height on border
      Having reference values for calculation of cross-border interference range according to prediction method, band, etc.
      Need to consider
      Station’s technical characteristics
      Frequency offset and bandwidth of stations affected
      Use of specific propagation curves
Radio Interference Prediction

## Slide 7
      Interference field strength based on ITU-R P.1546 (Method for point-to-area predictions for terrestrial services in the frequency range 30 MHz to 3 000 MHz)
      Determine Type of Propagation path
      Determine Nominal Time percentages and Nominal frequencies
      Estimate field strength while factoring in:
Terrain clearance angle
Tropospheric scattering
Receiving antenna height
Clutter around the transmitting/base terminal
Slope-path correction
Adjustment for different climatic regions etc.
Radio Interference Prediction - Example

## Slide 8
Basic two ways of measurements
      At a monitoring station;
      Along a route (Mobile)
      Time durations can vary and the measurements can be more complex involving coordinated use of mutiple measurements equipments at different geographical sites
Field Strength Measurements - Ways

## Slide 9
    The term “measurement of field strength” is intended to apply to four general categories of measurement:
Measurements performed with portable or mobile facilities, to obtain relatively instantaneous or short-term data at one or several locations;
Measurements performed with mobile facilities to obtain statistical parameters of coverage in the field of mobile radio;
Short-term measurements at a fixed location, generally in support of other monitoring operations;
Long-term measurements involving field strength recordings and analysis of chart records, respectively storage and analysis of measured data using computers.
Field Strength Measurements - Categories

## Slide 10
Two types of measurements:
      Simple “go-no go” test based on a spectrum mask
      Method used when the values of the deviation and modulation power are required
Field Strength Measurements - Types

## Slide 11
Mask method
      May be used as a verification to indicate whether the frequency deviation of an FM broadcasting station exceeds the limits;
      Cannot be applied on transmissions with 50 kHz peak deviation due to the fact that no appropriate spectrum mask is available;
Field Strength Measurements - Deviation

## Slide 12: Example Spectrum Mask measurement
Field Strength Measurements - Deviation

## Slide 13
Method when the values of the deviation and modulation power are required.
      Example
      The protection ratios specified in Recommendation ITU‑R BS.412 for the planning of FM sound broadcasting transmitters apply on the condition that a peak deviation of ±75 kHz is not exceeded and that the average modulation power over any interval of 60 s does not exceed that of a single sinusoidal tone which causes a peak deviation of ±19 kHz.
Field Strength Measurements - Deviation

## Slide 14
Conventional methods are :
Beat Frequency (BF) method
Offset Frequency (OF) method
Direct Lissajous (DL) method
Frequency Counter (FC) method
Frequency Discriminator (FD) method
Phase Recording (PR) method
Swept Spectrum Analyser (SSA) method.
At monitoring stations most of the time the methods DL, FC and SSA or used as these methods cover all types of frequency measurements. The other methods are included for completeness but are in practice not used anymore and not available due to the introduction of Digital signal processing (e.g. FFT, IFM…), which is now generalized in measuring equipment.
Field Strength Measurements - Frequency

## Slide 15
Digital Signal Processing (DSP) based methods are :
  Instantaneous Frequency Measurement (IFM) method
  FFT method.
DSP methods should be preferable on Monitoring Stations.
Field Strength Measurements - Frequency

## Slide 16
ITU Reports and Recomm. on Measurements
Category | Report/Recommendation Details
General | Recommendation ITU-R SM.1050 Recommendation ITU-R SM.1723 Recommendation ITU-R SM.1794 ITU Spectrum Monitoring Handbook, 2011, Chapter 1
Direction finding measurement and location determination | Recommendation ITU-R SM.854 Recommendation ITU-R SM.1598 ITU Spectrum Monitoring Handbook, 2011, Section 4.7
Spectrum and channel Occupancy measurement | Recommendation ITU-R SM.1880 Report ITU-R SM.2256 ITU Spectrum Monitoring Handbook, 2011, Section 4.10
Unwanted emissions | Recommendation ITU-R SM.328 Recommendation ITU-R SM.329 Recommendation ITU-R SM.1752 Recommendation ITU-R SM.1792 ITU Spectrum Monitoring Handbook, 2011, Section 4.12
Measurement on digital broadcasting systems | Recommendation ITU-R SM.1682 Recommendation ITU-R SM.1792 ITU Spectrum Monitoring Handbook, 2011,Sections 4.11 and 5.2
Mobile monitoring | Recommendation ITU-R SM.1708 Recommendation ITU-R SM.1723 ITU Spectrum Monitoring Handbook, 2011,Section 2.4.2
Standard data exchange format at monitoring stations | Recommendation ITU-R SM.1809

## Slide 17
ITU Reports and Recomm. on Measurements
Category | Report/Recommendation Details
Frequency | Recommendation ITU-R SM.377 ITU Spectrum Monitoring Handbook, 2011, Section 4.2
Field strength (see also Radio Regulations Art. 21) | Recommendation ITU-R P.845 Recommendation ITU-R SM.378 Recommendation ITU-R SM.1447 Recommendation ITU-R SM.1708 ITU Spectrum Monitoring Handbook, 2011, Section 4.10
Modulation | Recommendation ITU-R SM. 1268 ITU Spectrum Monitoring Handbook, 2011, Sections 4.6 and 4.8
Bandwidth | Recommendation ITU-R SM.443 ITU Spectrum Monitoring Handbook, 2011, Section 4.5
Identification | Recommendation ITU-R SM.1052 Recommendation ITU-R SM.1600 ITU Spectrum Monitoring Handbook, 2011, Section 4.8
Signal analysis | ITU Spectrum Monitoring Handbook, 2011, Section 4.8
Measurements related to inspection of radio installations | Report ITU-R SM.2130

## Slide 18
ITU Reports and Recomm. on Measurements
Category | Report/Recommendation Details
Selectivity of monitoring receivers | Recommendation ITU-R SM.1836 Report ITU-R SM.2125
IP3 of monitoring receivers | Recommendation ITU-R SM.1837 Report ITU-R SM.2125
Noise figure of monitoring receivers | Recommendation ITU-R SM.1838 Report ITU-R SM.2125
Scanning speed of monitoring receivers | Recommendation ITU-R SM.1839 Report ITU-R SM.2125
Sensitivity of monitoring receivers | Recommendation ITU-R SM.1840 Report ITU-R SM.2125
Other parameters | Report ITU-R SM.2125
Selectivity of monitoring receivers | Recommendation ITU-R SM.1836 Report ITU-R SM.2125

## Slide 19
  Thanks