## Slide 1: SPECTRUM UTILIZATION EVALUATION
Presented by : Gp 03

## Slide 2: ITU-R SM.1046
SPECTRUM UTILISATION FACTOR DEPENDS ON BANDWITH, SPACE , TIME
U=B*S*T
B-bandwidth
S-space
T-time
1. How do we evaluate the utilization efficiency of the spectrum already assigned ?

## Slide 3: SPECTRUM UTILISATION EFFICIENCY
SUE=M/U=M/B*S*T
M=Useful effect obtained
U-BST
Every services spectrum utilization efficiency depend on different factors. EXEMPLE-1:
Pico-cellular system’s point of view it depend on following
Total voice traffic/total spectrum*total coverage area

## Slide 4: Examples
If pico-cellular in building
SUE=total traffic carried in building/total channel*channel bandwidth*total floor area
SUE=Erlang/MHz*sqkm

## Slide 5: Examples
If Radio relay
SUE=C/B*S
C-capacity
B-bandwidth
S- geamectric measure of angle

## Slide 6: Evaluation step
Make list of all assigned services in described area. (divide areas)
Differentiate which systems depends similar factors divide factor related groups for all services.
Especially: Cellular mobile service, pico cellular broadband services
3. Area related list
4. Neighbor band related list etc.,
5 .Technology compatibility related list
So we make approach by ITU-R SM.1046 formulas for SUE.
And analyze how to make SUE in the area.

## Slide 7: How do we evaluate the utilization efficiency of the spectrum already assigned ?
Presence of interference through frequency monitoring from the assigned spectrum planning, frequency allocation, and type of service assigned for.
Feedback of utilization of spectrum.
Generation of revenue.
Permission to import eqpts.
Roll out plan compliance.
Deployed technology and use and presence of eco system and the global trends as well as regional trends.
Prepare and evaluate the database.

## Slide 8: 2. How do you react depending on the evaluation results ?
Before frequencies are for a new radio application, compatibility with existing radio systems and with non radio devices must be ensured. The spectrum engineers are responsible for defining appropriate technical parameters, finding clearly sharing conditions, and developing interference mitigation mechanisms to ensure the compatibility between different radio services in time, frequency and space domain. Following specific measures may be proved prudent in this case:
Consult with the operator.
Consult the regional and global trends and suggest measure.
Asking the reasons for non-compliance.
Regulate and enforce to comply with the licensing condition.
If need be revise the licensing condition in accordance with the global and regional trends.
Allow operators to have flexibility in deploying their technology to full fill their roll out obligation.
If some operator is not complying then punitive measures as per the licensing condition based on legal aspects.
Revoke frequency if unutilized for long time.
Re-farm, reassign frequency based on world regulations.

## Slide 9: 3. And whether the in-use SM results can contribute to the before –use SM in a proper way, formulating a close loop management.

## Slide 10: In use SM results and before use SM formulating a close loop SM
Evaluate existing assigned systems
Check and analyze its factors
B,S,T
Make reassignment decision
Make assumption before make assumption
Make reassignment
Prepare KPI for specific area for all similar systems (SUE)

## Slide 11: And whether the in-use SM results can contribute to the before –use SM in a proper way, formulating a close loop management.
The use of SM can contribute, especially focusing on spectrum monitoring. The sequence of events could be avoid harmful interference. At present with the rapid development of the ICT sector, the contradiction between supply and the spectrum permit is much more pronounced. Thus it is so necessary that SM can be controlled easily.
Identify the presence of interference therefore, find out the rationales like
(1) Difficulty with the technology.
(2) Presence of eco system.
(3) Allowing the operators to roll out flexibly.
(4) Clear interference so that spectrum planning can be done easily and auction can take place in due course of time.

## Slide 12: And whether the in-use SM results can contribute to the before –use SM in a proper way, formulating a close loop management.
(5) Ensure correct spectrum pricing.
(6) Facilitate spectrum rearrangement to support the technology.
(7) Facilitate carrier aggregation.
(8) Maximum utilization of spectrum planning and identifying feasible spectrum blocks basing on the channel planning.
(9) Finally, identify difficulties in spectrum monitoring to help finding way out in spectrum management

## Slide 13: 4. Is your country already consider such kind of management? If so, please introduce some practice as examples, if not try to give opinions.
Yes, such kind of management has already been considered in some of our countries.
Like, 2100 MHz band having X border interference in 3G (impacted 10 MHz) , was made free of interference and thus it could be made available for the upcoming auction with proper channel blacks and competency to be utilized with current technology. Govt got saved from the wastage of revenue.
Spectrum was revoked and license cancelled of the Wireless ISP operators not making correct utilization of spectrum. More so, considerations are being made to allow the operators to have flexibility in utilizing the current technology to fulfill their roll out plan.

## Slide 14: Any Question?

## Slide 15: THANKS....