## Slide 1: IMT- Identified Spectrum
Sameer Sharma
Senior Advisor , ITU
Industry Roundtable: Partnership for Digital Economy Growth
7 August 2018
Dhaka, Bangladesh

## Slide 2: ITU – Organization
Treaty
Organiz.
Advisory
Technical
Secretariat
Membership Inputs
WTDC
Action
Plan
Study Groups
WTSA
Study Groups
TDAG
TSAG
RPM
Action
Plan
RA
Study Groups
and CPMs
RAG
WRC
RPR
RR
Action
Plan
TSB
BR
BDT

## Slide 3
Definition
    Res. ITU-R 56-1: Naming for International Mobile Telecommunications
  Since ITU is the internationally recognized entity that has sole responsibility to define and to recommend the standards and frequency arrangements for IMT systems, with the collaboration of other organizations such as standard development organizations, universities, industry organizations and with partnership projects, forums, consortia and research collaborations, therefore the RA-15 debated especially on naming of IMT systems.
  the existing term IMT-2000 continues to be relevant and should continue to be utilized;
  the existing term IMT-Advanced continues to be relevant and should continue to be utilized;
  However for systems, system components, and related aspects that include new radio interface(s) which support the new capabilities of systems beyond IMT-2000 and IMT-Advanced, the term “IMT-2020” be applied
  In addition it was resolved that the term “IMT” would be considered the root name that encompasses all of IMT-2000, IMT-Advanced and IMT-2020 collectively.

## Slide 4
IMT
The values in the figures above are targets for research and investigation for IMT-2020 and may be revised in the light of future studies. Further information is available in the IMT-2020 Vision (Recommendation ITU-R M.2083)

## Slide 5
IMT Supports IoT

## Slide 6
Understanding IMT applications
Consumer – Fixed wireless
Business
IMT

## Slide 7: Recalling WRC-15 outcomes

## Slide 8: WRC-15 (General Information) 2-27 November 2015 in Geneva
  3275 participants attended WRC-15, including:
  2780 participants from 162 Member States, and
  495 participants representing 130 other entities, including industry, which also attended as observers
678 Documents including 2888 Member states proposals
  Two thirds (66%) of those were common proposals (either regional or multi-country).
WRC-15 addressed over 40 topics related to frequency allocation and frequency sharing for the efficient use of spectrum and orbital resources.

## Slide 9
Mobile Broadband (MBB)
(agenda Item 1.1 and 1.2)
Outcomes of WRC-15

## Slide 10: IMT Spectrum after WRC-07
Chart: IMT Spectrum After WRC-07 (MHZ)
| Region 1 (121 Countries) | Region 2 (35 Countries) | Region3 (37 Countries) | World
<20% of countries | 0 | 0 | 0 | 0
20 to 80 of countries | 200 | 0 | 292 | 292
80 to 99% Countries | 0 | 0 | 0 | 26
100% Countries | 885 | 951 | 885 | 859
    1085 MHz
    951 MHz
    1177 MHz
    1177 MHz

## Slide 11
User density | Total requirement by 2020 (MHz) | Region 1 |  | Region 2 |  | Region 3 | 
 |  | Already identified (MHz) | Additional demand (MHz) | Already identified (MHz) | Additional demand (MHz) | Already identified (MHz) | Additional demand (MHz)
Low | 1 340 | 981-1 181 | 159 – 359 | 951 | 389 | 885 - 1 177 | 163 – 455
High | 1 960 |  | 779 - 979 |  | 1 009 |  | 783 - 1 075
Source: CPM-15 report (Additional Spectrum Requirements)
    Need for More spectrum
  Estimated additional spectrum requirements by 2020 ranged from 159 to 1075 MHz depending on Region and user density)
Outcomes of WRC-15

## Slide 12
    New spectrum Identified
WRC - 15 |  |  |  | 
Band (MHz) | Bandwitdh (MHz) | R1 | R2 | R3
470 – 608 | 138 |  | some | 
608 – 698 | 84 |  | some | 
1427 – 1452 | 25 | any | any | any
1452 – 1492 | 40 | some | any | any
1492 – 1518 | 26 | any | any | any
3300 – 3400 | 100 | some | some | some
3600 – 3700 | 100 |  | some | 
4800 – 4990 | 190 |  | some | some
 | New BW 709 |  |  | 
Outcomes of WRC-15

## Slide 13
    Spectrum for IMT
Outcomes of WRC-15
Band (MHz) | Footnotes identifying the band for IMT |  |  | Bandwidth
 | Region 1 or parts thereof | Region 2 or parts thereof | Region 3 or parts thereof | 
450-470 | 5.286AA |  |  | 20
470-698 | - | 5.295, 5.308A | 5.296A | 228
694/698-960 | 5.317A | 5.317A | 5.313A, 5.317A | 262
1 427-1 518 | 5.341A, 5.346 | 5.341B | 5.341C, 5.346A | 91
1 710-2 025 | 5.384A, 5.388 |  |  | 315
2 110-2 200 | 5.388 |  |  | 90
2 300-2 400 | 5.384A |  |  | 100
2 500-2 690 | 5.384A |  |  | 190
3 300-3 400 | 5.429B | 5.429D | 5.429F | 100
3 400-3 600 | 5.430A | 5.431B | 5.432A, 5.432B, 5.433A | 200
3 600-3 700 | - | 5.434 | - | 100
4 800-4 990 | - | 5.441A | 5.441B | 190
Total Bandwidth | 1,886 (Regional allocations vary and therefore totals can be different for a specific region) |  |  | 

## Slide 14: IMT Bands after WRC-15
Chart: IMT Bands After WRC-15 (Number of countries identified)
| 450-470 | 470-608 | 608-610 | 610-614 | 614-694 | 694-698 | 698-790 | 790-806 | 806-862 | 862-890 | 890-902 | 902-928 | 928-960 | 1427-1452 | 1452-1492 | 1492-1518 | 1710-1885 | 1885-2025 | 2110-2200 | 2300-2400 | 2500-2690 | 3300-3400 | 3400-3500 | 3500-3600 | 3600-3700 | 4800-4900 | 4900-4990
Region 1 (121 Countries) | 121 | 0 | 0 | 0 | 0 | 121 | 121 | 121 | 121 | 121 | 121 | 121 | 121 | 121 | 53 | 121 | 121 | 121 | 121 | 121 | 121 | 33 | 121 | 121 | 0 | 0 | 0
Region 2 (35 Countries) | 35 | 5 | 0 | 0 | 7 | 7 | 35 | 35 | 35 | 35 | 35 | 0 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 35 | 6 | 35 | 35 | 4 | 1 | 0
Region 3 (37 Countries) | 37 | 4 | 4 | 7 | 7 | 7 | 26 | 37 | 37 | 37 | 37 | 37 | 37 | 37 | 37 | 37 | 37 | 37 | 37 | 37 | 37 | 6 | 11 | 10 | 0 | 3 | 2

## Slide 15: IMT Bands after WRC-15
    +26%
    1372 MHz
    +85%
    1764 MHz
    +52%
    1786 MHz
    +60%
    1886 MHz
Chart: IMT Spectrum After WRC-15 (MHz)
| Region 1 (121 Countries) | Region 2 (35 Countries) | Region3 (37 Countries) | World
<20% of countries | 0 | 438 | 518 | 514
20 to 80 of countries | 140 | 84 | 292 | 144
80 to 99% Countries | 0 | 0 | 0 | 318
100% Countries | 1232 | 1242 | 976 | 910

## Slide 16
Satisfy growing IMT broadband spectrum requirements:
  60% increase in IMT bands after WRC-15
  Total IMT spectrum of 1886 MHz
Harmonization of IMT bands:
  39% increase in globally harmonized spectrum after WRC-15
  318 MHz of harmonized bands in more than 80% of countries:
Secures future of other services through:
  coordination procedures,
  technical restrictions,
  In some cases operation on a non-interference basis
Outcomes of WRC-15 (Significance for MBB)

## Slide 17: WRC-15 (Follow up)
  WRC-15 Final ACTs available at:
    www.itu.int/pub/R-ACT-WRC.12-2015 (ITU CL-16/22 of 17 May 2016)
  Radio Regulation 2016 edition available at:
  http://www.itu.int/pub/R-REG-RR/en

## Slide 18: Going Forward

## Slide 19: Main Steps towards WRC-19
WRC-15: WRC-19 Agenda - Resolution 809 (WRC-15)
Final meetings of regional groups
Member States’ proposals to WRC-19
2nd Session of Conference Preparatory Meeting: CPM19-2 Planned dates at CICG in Geneva from 18 to 28 February 2019
1st Session of Conference Preparatory Meeting: CPM19-1 30 Nov – 1 Dec. 2015; Results @CA/226 of 23/12/2015
RA-19: 21 to 25 Oct. 2019 ; WRC-19: 28 Oct. to 22 Nov. 2019
C-16: WRC-19 agenda & dates in Res. 1380 with MOD venue @ C-17
Agenda & dates approved, new venue for consultation of MS

## Slide 20: CPM19-1
Following the WRC-15 the CPM19 had its first meeting from 30 November – 1 December 2015.
  269 participants from 63 Member States, 1 Observer from the State of Palestine and 25 Sector Members
The main task of the CPM was to decide on the structure of the CPM Report (for the WRC-19 conference) and the chapter rapporteurs and allocate the work to the relevant study groups.
Resolution COM 6/16 of WRC-15 contains the proposed agenda items for the WRC-19 and also references to the relevant Resolutions which are calling for the appropriate studies.

## Slide 21
CHAPTER 1: Land mobile and fixed services
  Agenda items: 1.11, 1.12, 1.14, 1.15
Rapporteur: Ms Keer ZHU (China (People's Republic of))
CHAPTER 2: Broadband applications in the mobile service
  Agenda items: 1.13, 1.16, 9.1 (issues 9.1.1, 9.1.5, 9.1.8)
Rapporteur: Mr José ARIAS (Mexico)
CHAPTER 3: Satellite services
  Agenda items: 1.4, 1.5, 1.6, 7, 9.1 (issues 9.1.2, 9.1.3, 9.1.9)
Rapporteur: Mr Nicolay VARLAMOV (Russian Federation)
CHAPTER 4: Science services
  Agenda items: 1.2, 1.3, 1.7
Rapporteur: Mr Vicent MEENS (France)
CPM19-1

## Slide 22
CHAPTER 5: Maritime, aeronautical and amateur services
  Agenda items: 1.1, 1.8, 1.9, 1.10, 9.1 (issue 9.1.4)
Rapporteur: Mr Wael EL SAYED (Egypt (Arab Republic of))
CHAPTER 6: General issues
  Agenda items: 2, 4, 9.1 (issues 9.1.6, 9.1.7), 10
Rapporteur: Mr Peter N. NGIGE (Kenya (Republic of))
CPM19-1

## Slide 23: Summary of AI
Agenda Item | Issues Covered | Chapter Number
1.1, 1.2, 1.3, 1.4 | Mobile and Amateur | 1
1.11, 1.12, 1.13, 1.14 | Science | 2
1.5,1.15, 1.16, 1.17, 1.18 | Aeronautical, Maritime and Radiolocation Issues | 3
1.6, 1.7, 1.8 , 1.9 (1.9.1 and 1.9.2), 1.10 | Satellite Services, FSS | 4
7, 9 (9.1, 9.2, 9.3) | Satellite Regulatory Issues | 5
2 (2.1 and 2.2), 4, 9, 10 | General Issues | 6
Res. 809 (WRC-15): 17 specific and 6 standing Items

## Slide 24: IMT spectrum requirements and WRC-19

## Slide 25: BB applications in MS (WRC-19 Agenda item 1.13 and 1.16)
The following bands, which are already allocated to mobile, will be studied with a view to an IMT-2020 identification:
  24.25 – 27.5 GHz
  37 – 40.5 GHz
  42.5 – 43.5 GHz
  45.5 – 47 GHz
  47.2 – 50.2 GHz
  50.4 – 52.6 GHz
  66 – 76 GHz
  81 – 86 GHz
The following bands will also be studied, although they do not currently have global mobile allocations: Res. 238 (WRC-15)
  31.8 – 33.4 GHz
  40.5 – 42.5 GHz
  47 - 47.2 GHz

## Slide 26: Overlapping Bands in WRC-19 Agenda Items
1.6 – NGSO FSS Res. 159 (WRC-15) | 1.13 – IMT Res. 238 (WRC-15) | 1.14 – HAPS Res. 160 (WRC-15) | 9.1 (9.1.9) – FSS Res. 162 (WRC-15)
 | 24.25 - 27.5 | 24.25 - 27.5 (Reg. 2) | 
37.5 - 39.5 (s-E*) | 37 - 40.5 | 38 ‑ 39.5 (globally) | 
39.5 - 42.5 (s-E*) | 40.5 - 42.5 |  | 
47.2 - 50.2 (E-s*) | 47.2 - 50.2 |  | 
50.4 - 51.4 (E-s*) | 50.4 - 52.6 |  | 51.4 - 52.4 (E-s*)
E-s: Earth-to-space; s-E: space-to-Earth. All bands in GHz |  |  | 
Studies to address mutual compatibility & sharing feasibility among the services/applications for which allocation/identification is envisaged under the corresponding Res. relating to the AI in the overlapping bands

## Slide 27: Future Spectrum need estimation for IMT (24.25 GHz - 86 GHz)
 | Examples | Associated conditions for different examples (For details, please see the corresponding sections in the Annex A) | Spectrum needs in total (GHz) | Spectrum needs (GHz) per range
Application-based approach ITU-R M.1651 | 1 | Overcrowded, Dense urban and Urban areas | 18.7 | 3.3 (24.25-33.4 GHz range) 6.1 (37-52.6 GHz range) 9.3 (66-86 GHz range)
 |  | Dense urban and Urban areas | 11.4 | 2.0 (24.25-33.4 GHz range) 3.7 (37-52.6 GHz range) 5.7 (66-86 GHz range)
 | 2 | Highly crowded area | 3.7 | 0.67 (24.25-33.4 GHz range) 1.2 (37-52.6 GHz range) 1.9 (66-86 GHz range)
 |  | Crowded area | 1.8 | 0.33 (24.25-33.4 GHz range) 0.61 (37-52.6 GHz range) 0.93 (66-86 GHz range)
Source: Chairman’s report TG 5/1 Annex 2: Working document towards Draft CPM text for WRC-19 AGenda Item 1.13

## Slide 28
 | Examples | Associated conditions for different examples (For details, please see the corresponding sections in the Annex A) | Spectrum needs in total (GHz) | Spectrum needs (GHz) per range
Technical performance-based approach (Type 1) Calculated on single technical performance requirement, i.e. user experienced data rate. | 1 | User experienced data rate of 1 Gbit/s with N simultaneously served users/devices at the cell‑edge, e.g., Indoor | 3.33 (N=1), 6.67 (N=2), 13.33 (N=4) | Not available
 |  | User experienced data rate of 100 Mbits/s with N simultaneously served users/devices at the cell-edge, for wide area coverage | 0.67 (N=1), 1.32 (N=2), 2.64 (N=4) | Not available
 | 2 | eMBB Dense Urban | 0.83-4.17 | Not available
 |  | eMBB Indoor Hotspot | 3-15 | Not available
 | 3 | With a file transfer of 10 Mbits by a single user at cell-edge in 1 msec | 33.33 GHz (one direction) | Not available
 |  | With a file transfer of 1 Mbit by a single user at cell-edge in 1 msec | 3.33 GHz (one direction) | 
 |  | With a file transfer of 0.1 Mbits by a single user at cell-edge in 1 msec | 333 MHz (one direction) | 
Future Spectrum need estimation for IMT (24.25 GHz - 86 GHz)
Source: Chairman’s report TG 5/1 Annex 2: Working document towards Draft CPM text for WRC-19 Agenda Item 1.13

## Slide 29: Future Spectrum need estimation for IMT (24.25 GHz - 86 GHz)
 | Examples | Associated conditions for different examples (For details, please see the corresponding sections in the Annex A) | Spectrum needs in total (GHz) | Spectrum needs (GHz) per range
Technical performance-based approach (Type 2) Calculated taking into account different technical performance requirements, i.e. user experienced data rate, peak data rate and area traffic capacity | – | Dense urban micro | 14.8-19.7 | 5.8-7.7 (24.25-43.5 GHz range)
 |  | Indoor hotspot |  | 9-12 (24.25-43.5GHz and 45.5‑86 GHz range)
Information from some countries based on their national considerations | – | – | 7-16 | 2-6 (24.25-43.5 GHz range) 5-10 (43.5-86 GHz range)
Source: Chairman’s report TG 5/1 Annex 2: Working document towards Draft CPM text for WRC-19 Agenda Item 1.13
Note: The spectrum needs estimates of the different approaches and examples should be considered separately.

## Slide 30: Future Spectrum need estimation for IMT (24.25 GHz - 86 GHz)
Source: WP 5D Liaison statement to Task Group 5/1
Deployment scenarios | Indoor hotspot | Dense urban |  | Urban macro
 |  | Micro | Macro | 
Frequency range | 24.25-86 GHz | 24.25-43.5 GHz | <6 GHz | <6 GHz
Deployment scenario | Micro | Indoor hotspot
Total spectrum needs for 24.25-86 GHz | 14.8-19.7 GHz* | 
Spectrum needs for 24.25-43.5 GHz | 5.8-7.7 GHz | 9-12 GHz
Spectrum needs for 45.5-86 GHz | –** | 
* Considering the coexistence between multiple network operators (e.g. the guard band(s) may be required in the case of multiple network operators scenarios), the total spectrum needs are expected to be increased. ** The division in this table regarding frequency ranges and deployment scenarios is just an indicative example on how spectrum needs could be distributed for different spectrum sub-ranges within 24.25-86 GHz and different deployment scenarios. This table should not be understood nor used to exclude any possible IMT-2020 deployment options in the range 45.5-86 GHz. |  | 

## Slide 31: LMS and FS systems and applications (WRC-19 Agenda item 1.14 and 1.15)
Res. 160 (WRC-15) Studies for considering appropriate regulatory actions for HAPS, within existing FS allocation i.e
  at 47.2-47.5, 47.9-48.2 & 31.0-31.3**/27.9-28.2GHz (outside Reg. 2, +5 ADMs @6.5/6.5MHz)
  or study new bands: 38-39.5 GHz & 21.4-22 &24.25-27.5 GHz
Res. 767 (WRC-15) Studies towards an identification for use by Administrations for LMS and FS applications operating in the frequency range 275-450 GHz

## Slide 32: New transport Systems in MS (WRC-19 Agenda item 1.11 and 1.12)
Res. 236 (WRC-15) Studies to facilitate global or regional harmonized bands to support railways RF systems between train & trackside within existing MS allocations
Res. 237 (WRC-15) Global or regionally harmonized bands, to the maximum extent possible, for implementation of evolving ITS within existing MS allocations

## Slide 33: Agenda for WRC-19 (Agenda item 10 of WRC-15)
Res. 958 (WRC-15): URGENT STUDIES to be reported under WRC-19 agenda item 9.1 :
  (9.1.6) Wireless Power Transmission (WPT) for electric vehicles
    Study suitable harmonized bands to minimize impact on RF services
  (9.1.7) Managing unauthorized operations of Earth Station terminals
    study need for possible additional measures and possible methods that will assist administrations
  (9.1.8) Narrowband & BB machine-type communication infrastructures
    study related technical and operational aspects of radio networks and systems (incl. spectrum needs & possible harmonized use of spectrum)

## Slide 34: Other studies in WRC-15 Res. to be reported in WRC-19
OTHER STUDIES to be reported under WRC-19 agenda item 9.1 :
  (9.1.1) Res. 212 – Terrestrial and Satellite components (Rev.WRC-15) of IMT, co- existence & compatibility @ 1 885-2025 & 2110-2200 MHz
  (9.1.2) Res. 761 – IMT and BSS sound @ 1452-1492 MHz (WRC-15) in R1&3
  (9.1.3) Res. 157 – N-GSO Sat. in “C-Band” allocated to (WRC-15) the FSS
  (9.1.4) Res. 763 – Stations on board sub-orbital vehicles (WRC-15)
  (9.1.5) Res. 764 – Incorporation by reference of (WRC-15) Rec. ITU-R M.1638-1 & ITU-R M.1849-1
  (9.1.9) Res. 162 – FSS needs @ 51.4-52.4 GHz(WRC-15)

## Slide 35
9.1.1*
TG 5/1**
9.1.4
1.6
9.1.6
WP 1B
WP 5C
9.1.2*
WP 4A
1.3
WP 5B
1.5
1.4
1.15
WP 1A
1.11
1.13
9.1.8
WP 4C***
1.12
7*
9.1.7
9.1.3
9.1.9
1.7
1.8 ***
1.9.1
1.10
1.9.2
1.16
WP 7B
1.14
Responsible ITU-R Groups
WRC-19 agenda items & Resp. Groups
2, 4, 10
CPM19-2
9.1 Issues BR Dir.’s Report (9)
1.1
1.2
WP 5A
WRC-19
8
Art. 5 (country) footnotes
3, 5, 6, 9
WP 5D
Railway in MS
ITS in MS
24.25 GHz < IMT < 86 GHz
HAPS
MS/FS Apps Id. @ 275-450 GHz
WAS/ RLAN
Sat. RR procedures
9.1.5
Amateur @ 50-54 MHz
FSS ESIM
MetSat/EESS @ 460-470MHz
BSS Plans/Lists & FSS App. 30 Annex 7 limitations
N-GSO QV-FSS
TT&C for NGSO of Short duration
GMDSS, incl. Sat.
Maritime radio devises
VDES Sat. comp.
GADSS
MSS/MetSat/EESS ES @ 400MHz
* Relevant part
** see 2nd next slide
*** WP 4C is also in charge of developing studies and draft CPM text on resolves to invite ITU-R 2 of Res. 359 (Rev.WRC-15) (AI 1.8) and sending that to WP 5B