## Slide 1
Workshop On The Efficient Use Of The Satellite Orbital Resource
Mobility over Typical and High Throughput Spot-beam Satellites
Daryl Hunter
Sr. Director, Regulatory Affairs
ViaSat, Inc.
Limassol, Cyprus
14 – 16 April, 2014

## Slide 2: Traditional Satellite Coverage
Single beam with multiple transponders
  Traditional means of covering a vast area such as trans-oceanic routes
Have supported mobility applications well for decades but some characteristics are not ideal for mobility
  EIRP and G/T are lowered as coverage area of beam increases
  Lower G/T typically requires BPSK and low code rate or spreading of return links to meet off-axis emission limits using low profile antennas
  Limited number of aircraft or vessels served at acceptable data rates per transponder

## Slide 3: Intelsat 21 Mobility Beam

## Slide 4: Traditional Mobility
National or regional mobility may occur entirely within a single beam
  IP networking is easier when all traffic is within the same beam
  Dense traffic may require multiple transponders and in some cases, more capacity than available on a single beam
Wider mobility requires stitching together coverage from multiple satellites
  More complex antenna pointing and IP networking as traffic switches from satellite to satellite

## Slide 5: ViaSat Ku band Mobility Coverage

## Slide 6: Spot Beam Coverage
Coverage area comprises many beams from same satellite
  Each beam may support one or more transponders
  Higher EIRP and G/T achievable per beam as spot beam size decreases
  Improved EIRP and G/T supports smaller user terminals while allowing operation at higher data rates
  Available frequency band can be reused many times resulting in greater overall network throughput capacity
  Network capacity increases faster than satellite cost enabling lower cost per bit to end user

## Slide 7: ViaSat-1 Spot Beams

## Slide 8: Spot Beam Mobility
Many spot beams cover the national or regional service area
  IP networking more complex as connectivity must be maintained when switching between spots
  Each spot beam provides capacity similar to a traditional satellite, supporting even dense networks at a higher grade of service
Wider area mobility now requires stitching together both multiple satellites and spot beams
  More complex IP networking but antenna pointing is similar to traditional satellite case

## Slide 9
ViaSat High Capacity Ka-band Coverage

## Slide 10: Hybrid Traditional / Spot Beam
Technology under development to allow blending of traditional and spot beam satellites
  Use high throughput Ka band spot beam coverage where available
  Switch to traditional Ku band coverage elsewhere
Allows users to take advantage of higher throughput Ka band satellites where available while still enjoying breadth of coverage from current Ku band fleet

## Slide 11: KuKarray Hybrid Antenna

## Slide 12: Ka band Frequency Reuse and Mobility
Frequency reuse achieved by alternating the frequency sub-band and/or polarization used by each spot beam across coverage area
Example, ViaSat-1 uses 28.1 – 29.1 and 29.5 – 30 GHz sub-bands
  RR FN 5.526 applies to 29.5 – 30 GHz sub-band (Region 2)
  RR 4.4 applies to 28.1 – 29.1 GHz sub-band
Results in Swiss Cheese Regulatory situation over coverage area

## Slide 13: Conclusion
Traditional Ku band satellites can be used to assemble nearly global seamless coverage
High throughput Ka band spot beam satellites are coming which will significantly improve the user connectivity experience in fixed and mobile applications
Solutions exist to help bridge the gap – not an either/or situation
Regulatory changes still need to be made to facilitate efficient use of Ka band spectrum for mobility