## Slide 1: 5G End-to-End Slicing Demo December 7th 2016 FG-IMT-2020 Geneva

## Slide 2: Outline
Background
Architecture
Prototype

## Slide 3: One Size Does Not Fit All
time
frequency
Access DC
Metro DC
Core DC
((
((
Multiple Applications 
Different QOS requirements 
Same air interface for every application +
Air interface controls most of QOS +
COMPROMISES 
Same authentication +
Same mobility +
Same reliability +
Same delay +
Same QOS +
COMPROMISES 
4G - air
4G – packet core
4G - UE
Mobile
Broad
Band
Machine
Machine
Reliable
Low
Latency
others
=
=

## Slide 4: Solution is custom tailoring (slice)
time
frequency
Access DC
Metro DC
Core DC
((
((
EMBB
URLLC
MMTC
No compromises air interface(s)
Ultra high bandwidth for MBB
Ultra low delay/reliability for URLLC
No reservations for MMTC
Room to grow for many others eg: improved mobility velocity
other
5G – air(s)
5G – packet core(s)
5G - UE
No compromises packet core(s)
Ultra high bandwidth for MBB/content near UE
Ultra low delay/reliability for URLLC (dedicated BW)
No reservations for MMTC
Virtualized core / programmable air interface allows Unlimited growth for ‘other’ slice types.

## Slide 5: Major Components of 5G Infrastructure
time
frequency
((
((
EMBB
URLLC
MMTC
other
5G – air(s)
5G - UE
Orchestration Hierarchy
SDN
(T)SDN
SDN NFV
NFV SDN
NFV SDN
1
2
1 F-OFDM – Filtered OFDM – flexibly isolates the bands allowing different behaviors
2 SCMA – Sparse Code Multiple Access – allows reservation free access
3 SDN – software defined networking – to program user plane or orchestrate F connectivity.
4 NFV – Network Function Virtualization – to run packet core functions on general CPUs
ORCHESTRATION – co-ordinate SDN / NFV / radios to create/change/manage slices.
6 POLAR CODES – flexible efficient error correcting codes for arbitrary block sizes.
1
2
3
4
5
3
3
4
4
5
SDN
3
5
6
MEC
MEC

## Slide 6: Slices however must “breathe”
time
frequency
Access DC
Metro DC
Core DC
((
((
EMBB
URLLC
MMTC
5G – air(s)
5G – packet core(s)
5G - UE
Since slices are allocated dedicated resources this can lead to inefficiencies. So:
Must be possible for slices to change size (breath) and to exchange physical resources
Example the MMTC slice shrinks and gives up capacity to the EMMB slice.
Example the ‘other’ slice is not present for some period of time. Its resources given to URLLC.
Must happen with minimum interference or the capability is not usable sufficiently often.

## Slide 7: Slicing in terms of resource sets/subsets.
+
+
+
+
Antennas
Fronthaul
CRAN fabric
CRAN CPU/S/W
RAT Numerology
+
+
Back Haul
Core CPU/S/W
UE
+
+
+
+
+
Antennas
Fronthaul
CRAN fabric
CRAN CPU/S/W
RAT Numerology
+
+
Back Haul
Core CPU/S/W
UE
+
From the Universe of resource sets..
A slice can be thought of as a set of subsets …

## Slide 8: Slices may share and trade resources – starting at UE Many levels of Slice Selection Implicit/Explicit
Different RATs
Different NG-EPC (demux at Slice Selection Function in NB)
Different downstream of the NG-EPC (eg different FW/LB etc.)
= Sj
= Sk
= Si
= Sl
Slices can be isolated all the way to antenna.
Slices can share antennas, fronthaul CRAN etc. but be separated by frequency
time or code space.
))))
))))
OS
))))
))))
OS
OS
Thing
Thing
APP
APP
APP
APP
APP
UEs/”Things” can be it a single slice, or multiple slices
A UE in multiple slices can be sliced A) horizontally (slice = QOS/QOE) or
B) vertically (slice = virtual UE).
A
B
SSF
+
+
+
+
Antennas
Fronthaul
CRAN fabric
CRAN CPU/S/W
RAT Numerology
+
+
Back Haul
Core CPU/S/W
UE
+
Eg 4.xG
= Sm

## Slide 9
Slices can“breath”i.e. grow/shrink & trade resources hit-lessley, automatically or on high level stimulus
+
+
+
+
Antennas
Fronthaul
CRAN fabric
CRAN CPU/S/W
RAT Numerology
+
+
Back Haul
Core CPU/S/W
+
+
+
+
Antennas
Fronthaul
CRAN fabric
CRAN CPU/S/W
RAT Numerology
+
+
Back Haul
Core CPU/S/W
Slicei =
Slicek =
f
f
f
D In response to various stimulus

## Slide 10
Various Stimuli to trigger resource D
After trigger (any type) everything is automatic closed loop and hitless.
Temporary H/W
maintenance
6
Schedules
time of Day
Operator
request for new slice or delete old
Profile or S/W version
changes
Physical resource add/remove
UE’s density changes
dramatically
Detected congestion
CPU thresholds
Spectrum
or spectral
efficiency change
Emergency Response
%
t
!!
!!

## Slide 11: Rapid Automation of every component is imperative!
CAPEX savings of 5G cloud come from statistical gains.
  Want to allocate resources less than peak requirements.
  Statistical gains need fast adaption to take advantage of ebb/flow of the tidal changes inter/intra slice.
  Slow reconfiguration means more equipment is required.
  Smaller Dt (i.e. better automation)  reduced peak HW.
  Trade-offs of resources is complex optimization problem.
time
eMBB
IOT
Dt
Larger Dt = More Peak HW More Loss
X
X
time
eMBB
IOT
Dt
Smaller Dt = Less Peak HW Less Loss
OPEX of 5G nf()/ng() without automation greater than physical f()/g().
  Many more components to manage/configure than physical.
  Exploiting parallelism requires many more logical conns/nfs.
  Dynamic management of infrastructure not just RAT/RAN.
  Hand debugging of virtualized entities requires specialized skills.
f()
g()
nfu[i]()
nfu[i]()
nfu[i]()
..
nfc[i]()
nfc[i]()
..
f()
ngu[i]()
ngu[i]()
ngu[i]()
..
ngc[i]()
ngc[i]()
..
g()
physical

## Slide 12
5g-1
auto p1
iface p1 inet manual
bond-master bond0
auto p2
iface p2 inet manual
bond-master bond0
auto bond0
iface p1 inet static
bond-mode 4
bond-miimon 100
bond-lacp-rate 1
bond-slaves p1 p2
Encoded
lxc start endoeB
ovs-vsctl add-port 5g-br0 enodeB_veth_0
ovs-vsctl set port enodeB_veth_0 tag=10
HSS
lxc start hss
ovs-vsctl add-port 5g-br0 hss_veth_0
ovs-vsctl set port hss_veth_0 tag=10
5g-2
auto p1
iface p1 inet manual
bond-master bond0
auto p2
iface p2 inet manual
bond-master bond0
auto bond0
iface p1 inet static
bond-mode 4
bond-miimon 100
bond-lacp-rate 1
bond-slaves p1 p2
5g-4
auto p1
iface p1 inet manual
bond-master bond0
auto p2
iface p2 inet manual
bond-master bond0
auto bond0
iface p1 inet static
bond-mode 4
bond-miimon 100
bond-lacp-rate 1
bond-slaves p1 p2
5g-6
auto p1
iface p1 inet manual
bond-master bond0
auto p2
iface p2 inet manual
bond-master bond0
auto bond0
iface p1 inet static
bond-mode 4
bond-miimon 100
bond-lacp-rate 1
bond-slaves p1 p2
5g-7
auto p1
iface p1 inet manual
bond-master bond0
auto p2
iface p2 inet manual
bond-master bond0
auto bond0
iface p1 inet static
bond-mode 4
bond-miimon 100
bond-lacp-rate 1
bond-slaves p1 p2
RRH
docker attach rrh
ovs-docker add-port 5g-br0 eth1 rrh –ipaddress==192.168.10.2/24
ovs-vsctl set port rrh_veth_0 tag=10
EPC
virsh net-define 5g-network.xml
virsh net-start 5g-network
virsh define epc
virsh start epc
ovs-vsctl add-port 5g-br0 epc_veth_0
ovs-vsctl set port epc_veth_0 tag=10
Switch-1
vlan 10
interface eth-trunk1
Description: To 5g-2
port link-type trunk
port trunk allow-pass vlan 10
mode lacp-dynamic
interface eth-trunk2
Description: To 5g-4
port link-type trunk
port trunk allow-pass vlan 10
mode lacp-dynamic
interface eth-trunk9
Description: To 5g-1 RRH
port link-type trunk
port trunk allow-pass vlan 10
mode lacp-dynamic
interface eth-trunk21
Description: To Optical Node
port link-type trunk
port trunk allow-pass vlan 10
mode lacp-dynamic
Switch-2
vlan 10
interface eth-trunk1
Description: To 5g-6
port link-type trunk
port trunk allow-pass vlan 10
mode lacp-dynamic
interface eth-trunk2
Description: To 5g-7q
port link-type trunk
port trunk allow-pass vlan 10
mode lacp-dynamic
interface eth-trunk21
Description: To Optical Node
port link-type trunk
port trunk allow-pass vlan 10
mode lacp-dynamic
A small sub-sample of some of the required commands to setup one slice in one C-RAN (non Radio parts) i.e. its very complex.
Transport network, radio and EPC attributes
not shown

## Slide 13: Outline
Background
Architecture
Prototype

## Slide 14: Slicing create/control hierarchical orchestration infrastructure
CTRL
MGMT
SOFT
ANT/freq
CTRL
MGMT
SOFT
FH
CTRL
MGMT
SOFT
DSP
S
P
L
CTRL
MGMT
SOFT
Fabric
CTRL
MGMT
SOFT
CUS
CTRL
MGMT
SOFT
NFs
F() G() H()
CTRL
MGMT
SOFT
Fabric
CTRL
MGMT
SOFT
CPUS
CTRL
MGMT
SOFT
NFs
F() G() H()
CONTROL
ORCHESTRATION
SOFTWARIZATION(APIs)
CONTROL
ORCHESTRATION
SOFTWARIZATION(APIs)
CTRL
MGMT
SOFT
NW
CONTROL
ORCHESTRATION
SOFTWARIZATION(APIs)
TAPI
F()
G()
H()
S
F()
G()
H()
I()
I()
((
((
URLLC
eMBB
URLLC Slice-B
eMBB Slice-A
f
(G)MPLS
Docker
Op-NFV
ODL
ODL
PCE
Container LXD
Container LXD
CTRL
MGMT
SOFT
NW
TAPI
(G)MPLS
PCE
NG(R)AN
UE
NG-UP
FW
NG-CP
UDM
AF
Data Network
NG1
NG3
NG2
NG4
NG7
NG6
NG5
SliceTemplate(eMBB-A)
F()
G()
H()
I()
L2VPN
L3VPN
A
B
C
INPUT
MACHINE
OUTUT

## Slide 15: High Level Events – Capability Exposure & Abstraction
CTRL
MGMT
SOFT
ANT/freq
CTRL
MGMT
SOFT
FH
CTRL
MGMT
SOFT
DSP
S
P
L
CTRL
MGMT
SOFT
Fabric
CTRL
MGMT
SOFT
CUS
CTRL
MGMT
SOFT
NFs
F() G() H()
CTRL
MGMT
SOFT
Fabric
CTRL
MGMT
SOFT
CPUS
CTRL
MGMT
SOFT
NFs
F() G() H()
CONTROL
ORCHESTRATION
SOFTWARIZATION(APIs)
CONTROL
ORCHESTRATION
SOFTWARIZATION(APIs)
CTRL
MGMT
SOFT
NW
CONTROL
ORCHESTRATION
SOFTWARIZATION(APIs)
TAPI
G()
H()
S
F()
I()
((
((
URLLC
URLLC Slice-B
f
(G)MPLS
Docker
Op-NFV
ODL
ODL
PCE
Container LXD
Container LXD
CTRL
MGMT
SOFT
NW
TAPI
(G)MPLS
PCE
NG(R)AN
UE
NG-UP
FW
NG-CP
UDM
AF
Data Network
NG1
NG3
NG2
NG4
NG7
NG6
NG5
SliceTemplate(eMBB-A)
F()
G()
H()
I()
L3VPN
A
B
C
INPUT
MACHINE
OUTUT

## Slide 16: High Level Events – Import Slice Delta & compute resource allocation
CTRL
MGMT
SOFT
ANT/freq
CTRL
MGMT
SOFT
FH
CTRL
MGMT
SOFT
DSP
S
P
L
CTRL
MGMT
SOFT
Fabric
CTRL
MGMT
SOFT
CUS
CTRL
MGMT
SOFT
NFs
F() G() H()
CTRL
MGMT
SOFT
Fabric
CTRL
MGMT
SOFT
CPUS
CTRL
MGMT
SOFT
NFs
F() G() H()
CONTROL
ORCHESTRATION
SOFTWARIZATION(APIs)
CONTROL
ORCHESTRATION
SOFTWARIZATION(APIs)
CTRL
MGMT
SOFT
NW
CONTROL
ORCHESTRATION
SOFTWARIZATION(APIs)
TAPI
(G)MPLS
Docker
Op-NFV
ODL
ODL
PCE
Container LXD
Container LXD
CTRL
MGMT
SOFT
NW
TAPI
(G)MPLS
PCE
NG(R)AN
UE
NG-UP
FW
NG-CP
UDM
AF
Data Network
NG1
NG3
NG2
NG4
NG7
NG6
NG5
SliceTemplate(eMBB-A)
F()
G()
H()
I()
A
B
INPUT
MACHINE
G()
H()
S
F()
I()
((
((
URLLC
URLLC Slice-B
f
L3VPN
OUTUT

## Slide 17: High Level Events – Sub divide problem by region/domain
CTRL
MGMT
SOFT
ANT/freq
CTRL
MGMT
SOFT
FH
CTRL
MGMT
SOFT
DSP
S
P
L
CTRL
MGMT
SOFT
Fabric
CTRL
MGMT
SOFT
CUS
CTRL
MGMT
SOFT
NFs
F() G() H()
CTRL
MGMT
SOFT
Fabric
CTRL
MGMT
SOFT
CPUS
CTRL
MGMT
SOFT
NFs
F() G() H()
CONTROL
ORCHESTRATION
SOFTWARIZATION(APIs)
CONTROL
ORCHESTRATION
SOFTWARIZATION(APIs)
CTRL
MGMT
SOFT
NW
CONTROL
ORCHESTRATION
SOFTWARIZATION(APIs)
TAPI
(G)MPLS
Docker
Op-NFV
ODL
ODL
PCE
Container LXD
Container LXD
CTRL
MGMT
SOFT
NW
TAPI
(G)MPLS
PCE
NG(R)AN
UE
NG-UP
FW
NG-CP
UDM
AF
Data Network
NG1
NG3
NG2
NG4
NG7
NG6
NG5
SliceTemplate(eMBB-A)
F()
G()
H()
I()
A
INPUT
MACHINE
G()
H()
S
F()
I()
((
((
URLLC
URLLC Slice-B
f
L3VPN
OUTUT
((
((

## Slide 18: High Level Events – Recursive.. divide problem by region/domain
CTRL
MGMT
SOFT
ANT/freq
CTRL
MGMT
SOFT
FH
CTRL
MGMT
SOFT
DSP
S
P
L
CTRL
MGMT
SOFT
Fabric
CTRL
MGMT
SOFT
CUS
CTRL
MGMT
SOFT
NFs
F() G() H()
CTRL
MGMT
SOFT
Fabric
CTRL
MGMT
SOFT
CPUS
CTRL
MGMT
SOFT
NFs
F() G() H()
CONTROL
ORCHESTRATION
SOFTWARIZATION(APIs)
CONTROL
ORCHESTRATION
SOFTWARIZATION(APIs)
CTRL
MGMT
SOFT
NW
CONTROL
ORCHESTRATION
SOFTWARIZATION(APIs)
TAPI
(G)MPLS
Docker
Op-NFV
ODL
ODL
PCE
Container LXD
Container LXD
CTRL
MGMT
SOFT
NW
TAPI
(G)MPLS
PCE
NG(R)AN
UE
NG-UP
FW
NG-CP
UDM
AF
Data Network
NG1
NG3
NG2
NG4
NG7
NG6
NG5
SliceTemplate(eMBB-A)
F()
G()
H()
I()
A
INPUT
MACHINE
G()
H()
S
F()
I()
((
((
URLLC
URLLC Slice-B
f
L3VPN
OUTUT
((
((

## Slide 19: High Level Events – Leaf (Physical) instantiation
CTRL
MGMT
SOFT
ANT/freq
CTRL
MGMT
SOFT
FH
CTRL
MGMT
SOFT
DSP
S
P
L
CTRL
MGMT
SOFT
Fabric
CTRL
MGMT
SOFT
CUS
CTRL
MGMT
SOFT
NFs
F() G() H()
CTRL
MGMT
SOFT
Fabric
CTRL
MGMT
SOFT
CPUS
CTRL
MGMT
SOFT
NFs
F() G() H()
CONTROL
ORCHESTRATION
SOFTWARIZATION(APIs)
CONTROL
ORCHESTRATION
SOFTWARIZATION(APIs)
CTRL
MGMT
SOFT
NW
CONTROL
ORCHESTRATION
SOFTWARIZATION(APIs)
TAPI
(G)MPLS
Docker
Op-NFV
ODL
ODL
PCE
Container LXD
Container LXD
CTRL
MGMT
SOFT
NW
TAPI
(G)MPLS
PCE
NG(R)AN
UE
NG-UP
FW
NG-CP
UDM
AF
Data Network
NG1
NG3
NG2
NG4
NG7
NG6
NG5
SliceTemplate(eMBB-A)
F()
G()
H()
I()
A
INPUT
MACHINE
G()
H()
S
F()
I()
((
((
URLLC
URLLC Slice-B
f
L3VPN
OUTUT
((
((
F()
G()
H()
I()
eMBB Slice-A
L2VPN
eMBB

## Slide 20: Outline
Background
Architecture
Prototype

## Slide 21: Basic Setup & Reaction Capability {create, delete, adjust of multiple slice types}
5G RADIO PHY
10GE SWITCH-A
DWDM A
DWDM B
10GE SWITCH-B
DWDM Emulator
Server DC A/1
Server DC A/2
T-SDN CTRL
5G ORCH
Server DC B/1
Server DC B/2
DWDM C
Hitless spectrum changes. Take from slice 1, Give to slice 2 etc.
Hitless 10G DWDM bandwidth adjustment hard or soft per slice
1 x 2xGE LAG per slice
NF
NF
NF
NF
NF
NF
NF
NF
NF
NF
NF
NF
NF
NF
NF
NF
NF
NF
Thousands of possible NF placements. Chosen by global optimizer. Hitless changes.
State 1
State n
State 2
1
2
3
1
3
2
Interrelated Dimensions

## Slide 22: Logical Demo and Physical Hardware
5G RADIO PHY
10GE SWITCH-A
DWDM A
DWDM B
10GE SWITCH-B
DWDM Emulator
Server DC A/1
Server DC A/2
TSDN
SONAC
5G ORCH
Server DC B/1
Server DC B/2
DWDM C
Load Generator
B-CUBE (FPGA)
OPTIX 9800(DWDM)
2288
Servers
6850(switch)
RFU
RFU
RFU
6800 Servers
2288
Servers
2288
Servers
OPTIX 9800(DWDM)
OPTIX 9800(DWDM)
eMBB
URRLC
MMTC
1000Mhz (5 x 20Mhz) @ 4.6Ghz
F-OFDM
F-OFDM
F-OFDM
15Khz
30Khz
30Khz
0.5ms 7 symbol
0.25ms 7 symbol SCMA
0.25ms 7 symbol
SUB FRAME
FRAME
UE-Server
UE-Radio (FPGA)
UE-Server
UE-Radio (FPGA)
: :
cv
Spectrum
Analyzer
6850(switch)
MUX
MUX
SUB FRAME
SUB FRAME

## Slide 23
BONN/GERMANY
SHANGHAI/CHINA
OTTAWA/CANADA

## Slide 24
DWDM NETWORK + ROADMS
General purpose compute in DC and C-RAN including 40GE High Density Switches LAG’ed over DWDM network.
5G Radio real time logic in BEE-7 FPGAs.
5G UE Radios real time FPGAs and test servers.

## Slide 25
SONAC DEMO GUI
IMPORTANT KPIS FOR EACH SLICE
TRANSPORT BANDWIDTH CRAN-DC
100 Mhz as 5x20Mhz F-OFDM blocks colored to show slice assignment
High level
view of what’s happening
View of Messaging data flow

## Slide 26: Resource allocation by mixed integer/linear program
System Resources =
Server resources
CPU
Memory
IO
OTN Resources
Bandwidth
System Costs =
Resource costs
Server-server cost
Server delays
Server-server delays
Optimization program:
Minimize selected costs/delays while:
Placing network functions(slices) and
Respecting system resource limitations.
≤
CPU cores
CPU I/O
DWDM link
Routing
Delay
Slice 1
Slice 2
Slice 3
Delay
NP-hard combinatorial problem
Randomized algorithms - approximate solutions but:
Good scalability
Parallelizable
Continuous optimization tracks requirement changes
Start at LP solution and branch-and-bound
MILP is a well known method, but:
Poor scalability
Problem changes before you compute solution
constraints
variables
Embb-MME
Embb-HSS
Mmtc-PHY
Embb-nb
Embb-gw
Embb-content
Ordering Constraint
BW(demand)
Resources(demand)
Slice ~= Graph of network functions (creates ordering constraints)
Resource utilization = fnetwork-function(slice demand)
Notes: If we look at some of the goals of 5G vs where we are today we an see the gap that has to be bridged over the next few years. The goal of 1ms latency is nearly 50x better than current LTE systems, to get from 100Mbps per user to 10G we need 100x the throughput per connection. The current 10,000 connections per square kilometer needs to increase to 1Million connetions so a 100x increase in density. Reliabile communications today with LTE top out about 350km/h and we expect to bring that up by 1.5x to 500km/h . Finally the current core networks and backhaul/front haul are inflexible with wasted pools of bandwidth. The introduction of SDN/NFV will allow much better ability to chop up and virtualize the network resources for lower operational costs and capital costs and much greater flexibility.

## Slide 27: STATE-0 – idle, no slices, NFs, min BW
5G RADIO PHY
10GE SWITCH-A
DWDM A
DWDM B
10GE SWITCH-B
9800 Emulator
Server DC A/1
Server DC A/2
T-SDN CTRL
5G ORCH
Server DC B/1
Server DC B/2
DWDM C
NF
NF
NF
NF
NF
No network functions present in either CRAN
/EDGE or DC.
1
2
3
Test UE’s are all idle
Minimum B/W up between DC’s.
4G RADIO PHY
Real LTE UE’s are disconnected

## Slide 28
10GE SWITCH-A
DWDM A
DWDM B
10GE SWITCH-B
DWDM Emulator
Server DC A/1
Server DC A/2
T-SDN CTRL
5G ORCH
Server DC B/1
Server DC B/2
DWDM C
NF
NF
NF
NF
1
Operator !! requests LTE slices
EPC NF’containers placed in C-RAN
2
Global Optimizer assigns resources
3
LTE MME&HSS NFs placed in DC, cores assigned, started,
configured.
3
LTE Phy H/W instantiated.
E-2-E network configured and sized.
5a-OVS bridges, 5b-phys switches. 5c-TSDN allocates and brings up lambdas into switch LAG for this slice.
5
LTE in slice – create two LTE slices
4
6
Two smartphones connect, one per slice.
Skype initiated.
LTE-gw containers
moved.
Skype
4G
PHY
Lte-eNB
LTE-mme
LTE-PHY
LTE-gw
LTE- hss
Lte-eNB
LTE-mme
LTE-PHY
LTE-gw
LTE- hss

## Slide 29
5G RADIO PHY
10GE SWITCH-A
DWDM A
DWDM B
10GE SWITCH-B
DWDM Emulator
Server DC A/1
Server DC A/2
T-SDN CTRL
5G ORCH
Server DC B/1
Server DC B/2
DWDM C
NF
Embb-nb
NF
NF
NF
1
Operator !! requests eMBB slice
eMBB NF’containers placed in C-RAN
  1-eMBB NB protocol
  2-eMBB gateways, 3-some content
  Cores assigned, started, configured.
Embb mme
Mmtc-PHY
2
Global Optimizer assigns resources
3
eMBB MME&HSS NFs placed in DC, cores assigned, started,
configured.
3
eMBB PHY instantiated.
Spectrum/OFDM etc.
attributes configured.
E-2-E network configured and sized.
5a-OVS bridges, 5b-phys switches. 5c-TSDN allocates and brings up lambdas into switch LAG for this slice.
5
STATE-1 – eMBB slice created
4
5
Test-UE’s start generating traffic into this slice for the content.
>display stats
30,30303
30303.
>display stats
30,30303
30303.
6
KPI displays Spectrum Analyzer etc.
Embb-gw
Embb hss
Embb-content

## Slide 30
5G RADIO PHY
10GE SWITCH-A
DWDM A
DWDM B
10GE SWITCH-B
DWDM Emulator
Server DC A/1
Server DC A/2
T-SDN CTRL
5G ORCH
Server DC B/1
Server DC B/2
DWDM C
NF
Mmtc-prot Mmtf-agg
NF
NF
NF
1
Operator !! requests MMTC slice
MMTc NF’ containers placed in C-RAN
  1-MMTc NB protocol
  2-MTc small packet aggregator
  Cores assigned, started, configured.
Mmtc-split
Mmtc-PHY
2
Global Optimizer assigns resources
3
MMTc small packet disaggregator NF placed in DC, cores assigned, started,
configured.
3
MMTc PHY instantiated.
Spectrum/OFDM etc.
attributes configured.
E-2-E network configured and sized.
5a-OVS bridges, 5b-phys switches. 5c-TSDN allocates and brings up lambdas into switch LAG for this slice.
5
STATE-2 – mMTC slice created
4
5
Test-UE’s generate 10,000 different UE IDs.
>display stats
30,30303
30303.
>display stats
30,30303
30303.
6
KPI displays packet loss etc. Spectrum Analyzer etc.

## Slide 31
5G RADIO PHY
10GE SWITCH-A
DWDM A
DWDM B
10GE SWITCH-B
DWDM Emulator
Server DC A/1
Server DC A/2
T-SDN CTRL
5G ORCH
Server DC B/1
Server DC B/2
DWDM C
NF
Urrrlc-nb
NF
NF
NF
1
Operator !! requests URRLC slice
URRLC-NB NF container placed in C-RAN
  1-URRLC NB protocol
urrrlc-PHY
2
Global Optimizer assigns resources
3
URRLC PHY instantiated.
Spectrum/OFDM etc.
attributes configured.
STATE-3 – URRLC slice created
4
5
Test-UE’s A generates urgent vehicle to vehicle message to Test-UE-B
Round trip delay displayed on related laptop.
>display stats
30,30303
30303.
>display stats
30,30303
30303.
6
Three slices running.
6
KPI displays packet loss etc. Spectrum Analyzer etc.

## Slide 32
5G RADIO PHY
10GE SWITCH-A
DWDM A
DWDM B
10GE SWITCH-B
DWDM Emulator
Server DC A/1
Server DC A/2
T-SDN CTRL
5G ORCH
Server DC B/1
Server DC B/2
DWDM C
NF
Urrrlc-nb
NF
NF
NF
1
Operator !! requests URRLC slice spectrum growth by reducing MMTC spectrum
MMTc NF container moved out of C-to DC because URRLC needs the compute resources.
urrrlc-PHY
2
Global Optimizer has to move MMTC to DC for URRLC performance increase. Also more DC/CRAN B/W required for MMTC-protocol to PHY
3
URRLC PHY hitless spectrum increase. MMTC hitless spectrum decrease.
STATE-4 – Breath- increase URLLC
4
6
Test-UE’s for all three slices continue
Uninterrupted.
eMBB not shown for
clarity.
>display stats
30,30303
30303.
>display stats
30,30303
30303.
6
Three slices running after spectrum change
6
KPI displays all slices still working.
Mmtc-prot Mmtf-agg
Mmtc-split
Mmtc-PHY
5
Fronthaul B/W increased for MMTC since its moved out of C-RAN. New 10G lambda created added to LAG.

## Slide 33
5G RADIO PHY
10GE SWITCH-A
DWDM A
DWDM B
10GE SWITCH-B
DWDM Emulator
Server DC A/1
Server DC A/2
T-SDN CTRL
5G ORCH
Server DC B/1
Server DC B/2
DWDM C
NF
Embb-nb
NF
NF
NF
1
Operator !! requests eMBB ICN slice
ICN-ROUTER container placed in C-RAN
  eMBB NB Slice Selection Function SSF configured to forward ICN packets direct ICN-router NF.
Mmtc-PHY
2
Global Optimizer assigns resources
3
ICN-ROUTER , MANAGER, VIDEO CONF APP containers placed in DC
4
Due to increase in MBB traffic on the ICN slice TSDN configures extra 10GE lambda to the MBB slice LAG.
5
STATE-5 – eMBB/ICN slice created
>display stats
30,30303
30303.
>display stats
30,30303
30303.
6
KPI displays Spectrum Analyzer etc.
ICN-ROUTER
ICN-ROUTER
ICN-MGR
ICN-Video
SSF
6

## Slide 34
5G RADIO PHY
10GE SWITCH-A
DWDM A
DWDM B
10GE SWITCH-B
DWDM Emulator
Server DC A/1
Server DC A/2
T-SDN CTRL
5G ORCH
Server DC B/1
Server DC B/2
DWDM C
Embb-nb
Mmtc-PHY
STATE-6 – eMBB/ICN slice operation
3
ICN UEs register interest
In SOURCE’s content.
>display stats
30,30303
30303.
>display stats
30,30303
30303.
6
ICN Manager
Displays KPIs.
ICN-ROUTER
ICN-ROUTER
ICN-MGR
ICN-Video
(((((((
ICN-SOURCE
SSF
1
ICN Source content follows interest ‘tree’
2
2
(((((((
3
ICN replicates at a fork in interest directly to eMBB-NB
In same C-RAN DC.
4
eMMB-NB SSF sends
To ICN ROUTER(s)
Bypassing eMBB G/Ws.
5
ICN UE-s receive content of interest.

## Slide 35: State-7 Breathing response to B/W
5G RADIO PHY
10GE SWITCH-A
DWDM A
DWDM B
10GE SWITCH-B
Server DC A/1
Server DC A/2
T-SDN CTRL
5G ORCH
DWDM C
Generate 9.5 G worth of background eMBB traffic into eMBB slice LAG.
1
2
5G Orchestrator notes increased B/W in slice at critical link and asks TSDN for additional 10G lambda which it then add to the LAG in a
make-before-break manner (no hit).
+l
SPIRENT TESTER

## Slide 36: Thank-You