## Slide 1: Information Centric Networking (ICN) in IMT-2020
Marc Mosko
marc.mosko@parc.com
2016-12-07

## Slide 2
Today’s host-based networking and
server-based security.

## Slide 3: The future Internet architecture
Naming all data, securing all data and communicating based on name
Is secure
Provides high availability
Transfers data independent of location
Takes advantage of storage and processing
An architecture proposal that
It does this by

## Slide 4
Information Centric Networking (ICN)
Transfer data based on its properties not opaque bytes and addresses
Content Centric Networking (CCNx)
Seminal and popular ICN protocol

## Slide 5
CCNx Operation in a Nutshell
Uniquely name network objects (like a URI)
Request a name from the network (not from a host)
Security is bound to the network object not a host
Network objects can come from any location
As an overlay over IP, IPv6, UDP, MPLS, etc.
Native over GTP, Ethernet, PPP, OTN, etc.
As an underlay for IP, IPv6, SCTP, HTTP, etc.

## Slide 6
Using named content with content-level
security maps well to core 5G principles
Simplification — Loose-coupling
— Intrinsic Mobility — Security —
Orchestration & Virtualization

## Slide 7: Network abstraction
CCN Portal
Key-Value
Messaging
Streaming
K
V
K
V
K
V
I
C
Flow Control
Sign / Verify
Encoder / Decoder
Transport
Framework
Assembly
Framework
Posix
Notes: Storage and network looks the same
Apps don’t need to be aware of network specifics
We need the right set of APIs.

## Slide 8: CCNx names
/parc/ccnx/presentation/slide17/v=2/c=0
globally routable
name segments
system / application
dependent name segments
protocol dependent
name segments
Hierarchical
Everything has a name
Replaces IP addresses and ports
Don’t have to be human readable

## Slide 9: Network data structures
Content Manifest Message
Name
Publisher Signature
Content Messages Catalog
Optionally encrypted
Aggregate Metadata
Optionally encrypted
Notes: Not everything fits in a single packet.
We use manifests (basically a catalog)
Benefits/features of manifests:
Give information about the whole object (don’t have to be repeated by each object)
Seek
Overarching security context don’t need to repeat security in each packet
Data structures that the network knows about

## Slide 10: Unifying network and storage
A
B
Messages are secure
(in motion and at rest)
Messages are the same
(in network and in storage)
Notes: A- Messages are secure, in motion and at rest
B- Messages are the same, in network and in storage
Storage is part of the network
Storage systems can integrate with the network
The network can take advantage of raw storage
Disk blocks become message caches, message caches become disk blocks.
Storage data structures can merge with disk data structures.
No coincidence that manifests look like inodes

## Slide 11
ICN in Standards
Several Internet Drafts in IRTF research group (proposed Experimental status)
Data Aware Networking in ITU-T (Y.3033)

## Slide 12
ICN in IMT-2020 Focus Group
Identify ICN as important non-IP protocol for IMT-2020
Identify existing standardization gaps
Perform Proof-of-Concepts and studies in important gap areas

## Slide 13
Gap |  | POC #1 | POC #2 | POC #3 | POC #4 | POC #5 | Study #1 | Study #2
E.1 | ICN in IMT2020 | ✓ | ✓ | ✓ | ✓ | ✓ |  | ✓
E.2 | ROHC |  |  |  |  |  | ✓ | 
E.3 | ICN S-GW |  |  |  |  |  |  | ✓
E.4 | ICN MME |  |  |  |  |  |  | 
E.5 | ICN P-GW |  |  |  |  |  |  | ✓
E.6 | ICN Slice | ✓ |  |  |  |  |  | 
E.7 | Lawful Intercept |  |  |  |  |  |  | 
E.8 | Mobility & Routing | ✓ | ✓ | ✓ | ✓ | ✓ |  | ✓
E.9 | UE Provision | ✓ |  |  |  |  |  | ✓
E.10 | ICN mgmt SON |  |  |  |  |  |  | 
E.11 | OAM |  |  |  |  |  |  | 
E.12 | SDN & Openflow |  |  | ✓ |  |  |  | 
E.13 | Auth & Encrypt |  | ✓ |  | ✓ |  |  | 
E.14 | Encrypt |  |  |  |  |  |  | 
E.15 | QoS |  |  |  |  |  |  | 

## Slide 14
Cost efficient and low latency delivery of IP-based services (InterDigital)
Using ICN to simplify data delivery, mobility management and secure transmission over an heterogeneous network access (Cisco Systems)
Using ICN to meet the IMT-2020 goals (Fujitsu Labs)
Interplay of mmWave based wireless access and ICN (KDDI)
ICN seamless mobility (Huawei Technologies)
Proofs of Concepts

## Slide 15
marc.mosko@parc.com
http://www.ccnx.org/