## Slide 1
ITU-T Information & Data Modeling and Status
Joint IEEE 802 and ITU-T Study Group 15 Workshop
Kam LAM (CICT) Q14/15 Rapporteur

## Slide 2: ITU-T Q14/15 Modeling Work
Mandate & Scope
Modeling Methodology
Evolution
Pruning/Refactoring & Augmentation
UML to YANG Generation
Status

## Slide 3: Q14/15 Mandate & Scope
Management and control of transport systems and equipment
  Technology architecture & function  Management/Control
    requirement, information model, data model
 | Generic | SDH | OTN (L1) | Carrier Ethernet | MPLS-TP | MTN | Media (L0) | Sync
Transport Architecture | G.800 G.805 G.807 | G.803 | G.872 | G.8010 | G.8110.1 | G.media-arch | G.807 | G.8265.1 G.8275.1 G.8275.2
Interface |  |  | G.709 | G.8013 | G.8113.x | G.mtn | G.698.1..4 | 
Equipment Function | G.806 | G.783 | G.798 | G.8021 | G.8121.x | G.mtn-eqpt G.mtn-prot |  | 
Mgmt/Control Requirement | G.7710 | G.784 | G.874 | G.8051 | G.8151 | G.mtn-mgmt | G.876 | G.7721
Information Model | G.7711 | G.774.1-10 (CMISE) | G.875 | G.8052 | G.8152 |  |  | 
Data Model |  |  |  | G.8052.1/2 | G.8152.1/2 |  |  | G.7721.1
Q14
Q10,
Q11,
Q12,
Q13

## Slide 4: Model Development Methodology
Core Model G.7711 / ONF TR-512
  Forwarding & Termination
  Foundation
  Topology
  Resilience
  Physical
  ….
Data schema
for interface 1
Application specific models (e.g. storage)
Technology specific models, e.g.,
  G.875 OTN
  G.8052 Transport ETH
Guidelines
Interface specific
Common process
Common Information Model
Interface specific
xxx model
Map
Prune/refactor
View of the common IM for a particular purpose
Papyrus tool and GitHub
Model structure
UML
Common Guidelines
Map
Interface
instance 1
Map
Interface instance 2
Interface specific
Interface Creation Process

## Slide 5: UML Modelling Guidelines evolution
NGCOR Modelling Requirements
ITU-T SG15 Modelling Guidelines
UML Modeling Guidelines ONF TR-514
JWG MA Model Repertoire
multi SDO
UML Modeling Guidelines IISOMI 514
Other candidates:
ONAP
OIF
…

## Slide 6: Information Model evolution

## Slide 7: Influence Across Standards and Open Source
TAPI FRS
Use cases & Requirements
TAPI UML Information Model
TAPI YANG
Data Schema
SWAGGER/REST APIs
ONF Core Information Model
ONF Technology Specification Models
UML-YANG
Generation Tool
YANG-SWAGGER Generation Tool
SNOWMASS TAPI SDK
EAGLE Modeling Tools
Open Model Profile
Code
OTN
(ITU-T G.874.1)
ETH
(ITU-T G.8052)
MPLS-TP
(ITU-T G.8152)
Python Reference Implementation
Python Stub Generation Tool
Optical Transport
MEF
Open CS Implementations
Packet WAN
Multi-carrier
T-SDN Interop
Implementation Agreements & Certification
OIF
Interop Implementations
NRM
MEF Models
NRP
ONF OIMT
ONF OTCC
ITU-T SG15
Technology Generic Core Model
(ITU-T G.7711)
ONF OIMT

## Slide 8: Pruning/Refactoring example
OTN
(G.875)
ETH
(G.8052)
MPLS-TP
(G.8152)
TAPI UML Information Model
Core Information Model
(TR-512 / G.7711)
ONF Technology Specification Models
ONF OIMT
ITU-T SG15
Technology IMs
SYNC
(G.7721)
Media
(G.876)
ONF OTCC TAPI
Pruning & Refactoring (P&R)
How: Spec model approach (TR-512.7 / G.7711 Annex G)
What: Technology IMs

## Slide 9: UML Modelling
UML Modeling Guidelines
  ONF TR-514 v1.3 (IISOMI-514 v1.3)
    https://www.opennetworking.org/software-defined-standards/models-apis/

## Slide 10: UML Modelling Tools
Papyrus & Github Guidelines
  ONF TR-515 v1.3 (IISOMI-515 v1.3)
    https://www.opennetworking.org/software-defined-standards/models-apis/

## Slide 11: UML to YANG Mapping
Mapping Guidelines
  ONF TR-531 v1.1 (IISOM-531 v1.1)
    https://www.opennetworking.org/software-defined-standards/models-apis/
Mapping Tool
  xmi2yang
    https://github.com/OpenNetworkingFoundation/EagleUmlYang
  To download the tool:
    Go to https://github.com/OpenNetworkingFoundation/EagleUmlYang,
    click , select “Download ZIP”
    Extract the zip file
    Put the “xmi2yang” folder anywhere you like in your explore.

## Slide 12: UML to YANG Mapping Tool
Open Source Tool: https://github.com/OpenNetworkingFoundation/EagleUmlYang
  Background:
    Initially developed by the ONF open source project “EAGLE”
    Now run by the Informal Inter SDO Open Model Initiative (IISOMI), including active participants from ONF, ITU-T SG15, MEF, TMF, …
  Mapping Guidelines (rules): IISOMI-531 v1.3
  Mapping Tool: xmi2yang
    Programming language: JavaScript
    Set up the running environment: node.js (download from https://nodejs.org/en/ the node-v8.9.4-x64.exe and run it once)
      Also, from time to time, update the environment by running the command “npm install” in the folder xmi2yang
    How to run:
      Copy the UML file of the UML model into the “project” sub-folder of the xmi2yang directory
      Run the command “node main.js” at the xmi2yang directory
      The YANG file will be generated in the “project” sub-folder
      Validate the YANG file at http://www.yangvalidator.com/ and get also the YANG Tree.

## Slide 13: UML to YANG Mapping Tool - Demo
The output
The model
The tool
Run!

## Slide 14: Status of ITU-T Technology-specific and Generic Information Models
G.7711 – Core information model, generic to transport technology; same model as ONF TR-512
  v3.05 in TD370r1/3 (7/2019); to align with ONF TR-512 v1.4.1-info and consent in 9/2020
G.875 – OTN (L1)
  v4.06 in TD439/P(1/2020); is planned for consent at this 2/2020 SG15 plenary meeting
G.876 – Photonic media (L0); requirements and information model
  v0.09 in TD476/3 (1/2020); is progressing and planned for consent in 09/2020
G.7719 – Management/Control components IM; revision to ex. G.7718.1; v1.02 in TD373r1/3 (7/2019);
G.7721 – Synchronization IM; management requirements and information model; v1.0 approved in 11/2018;
G.7721.1 – Synchronization management data model; v0.01, Just started
G.8052 – Carrier Ethernet; v3.02 in TD484/3 (1/2020);
G.8052.1 – OAM information/data model for Carrier Ethernet; v0.12 in TD521/3 (1/2020);
G.8052.2 – Resilience information/data for Carrier Ethernet; v0.12 in TD521/3 (1/2020);
G.8152 – MPLS-TP; V1 (12/2016);
G.8152.1 – OAM information/data model for MPLS-TP; v0.04 in TD486/3 (1/20202)
G.8152.2 – Resilience information/data model for MPLS-TP; v0.04 in TD487/3 (1/20202)
G.mtn-mgmt – MTN management requirements and information model; just started

## Slide 15: THANK YOU