## Slide 1: Time-Sensitive Networking Horizons Possibilities for Achieving Bounded Low Latency
Norman Finn
Huawei Technologies Co. Ltd
Joint IEEE 802 and ITU-T Study Group 15 Workshop, Geneva, Switzerland,
25 January, 2020

## Slide 2: The TSN Toolbox
TSN Components (Tools of the TSN toolbox)
2
Latency
Bounded low latency: Credit Based Shaper (802.1Qav) Frame preemption (802.3br & 802.1Qbu) Scheduled Traffic (802.1Qbv) Cyclic Queuing and Forwarding (802.1Qch) Asynchronous Traffic Shaping (P802.1Qcr)
QoS Provisions (P802.1DC)
High Availability / Ultra reliability: Frame Replication and Elimination (802.1CB) Path Control and Reservation (802.1Qca) Per-Stream Filtering and Policing (802.1Qci) Reliability for time sync (802.1AS-2020)
Time synchronization: Timing and Synchronization (802.1AS) includes a profile of IEEE 1588 (revision: P802.1AS-Rev  802.1AS-2020
sent to IEEE SA RevCom approval)
Zero congestion loss =
Bounded latency
Resource Mgmt
Dedicated resources & API Stream Reservation Protocol (802.1Qat) TSN configuration (802.1Qcc) Basic YANG (802.1Qcp)
YANG for CFM (P802.1Qcx) YANG for LLDP (P802.1ABcu)
YANG for Qbv, Qbu, and Qci (P802.1Qcw)
YANG & MIB for FRER (P802.1CBcv)
Extended Stream Identification (P802.1CBdb) Link-local Registration Protocol (P802.1CS)
Resource Allocation Protocol (P802.1Qdd) Configuration Enhancements (P802.1Qdj)
LLDPv2 (P802.1ABdh)
Reliability
Synchronization
Resource Mgmt
Note: P upfront of an ID indicates ongoing Project
From János Farkas’s presentation

## Slide 3: The TSN Toolbox
TSN Components (Tools of the TSN toolbox)
3
Latency
Bounded low latency: Credit Based Shaper (802.1Qav) Frame preemption (802.3br & 802.1Qbu) Scheduled Traffic (802.1Qbv) Cyclic Queuing and Forwarding (802.1Qch) Asynchronous Traffic Shaping (P802.1Qcr)
QoS Provisions (P802.1DC)
High Availability / Ultra reliability: Frame Replication and Elimination (802.1CB) Path Control and Reservation (802.1Qca) Per-Stream Filtering and Policing (802.1Qci) Reliability for time sync (802.1AS-2020)
Time synchronization: Timing and Synchronization (802.1AS) includes a profile of IEEE 1588 (revision: P802.1AS-Rev  802.1AS-2020
sent to IEEE SA RevCom approval)
Zero congestion loss =
Bounded latency
Resource Mgmt
Dedicated resources & API Stream Reservation Protocol (802.1Qat) TSN configuration (802.1Qcc) Basic YANG (802.1Qcp)
YANG for CFM (P802.1Qcx) YANG for LLDP (P802.1ABcu)
YANG for Qbv, Qbu, and Qci (P802.1Qcw)
YANG & MIB for FRER (P802.1CBcv)
Extended Stream Identification (P802.1CBdb) Link-local Registration Protocol (P802.1CS)
Resource Allocation Protocol (P802.1Qdd) Configuration Enhancements (P802.1Qdj)
LLDPv2 (P802.1ABdh)
Reliability
Synchronization
Resource Mgmt
Note: P upfront of an ID indicates ongoing Project
From János Farkas’s presentation

## Slide 4: Outline
  Disclaimer
  Two kinds of traffic: time-shared (not here) and continuous (here).
  Several queuing methods are available and/or proposed
    Asynchronous Traffic Shaper
    Two-buffer CQF
    Three-buffer CQF
    Multilevel CQF
    Paternoster
  Summary

## Slide 5: Disclaimer
This presentation is the personal opinion of a long-time contributor to the IEEE 802.1 process. It does not claim to represent the opinions of IEEE 802.1 as a whole, or of any of the other participants in that Working Group.
Some of the methods described are in published standards. Some are work in progress. Some are simply proposals presented publicly in IEEE 802.1.
Some people may disagree with this author’s characterization of either the standards, the work in progress, or the proposals.

## Slide 6: Two kinds of traffic
Scheduled (bursty) traffic, characterized by:
  Regularly-scheduled transmission bursts, the phases of which may be adjustable to meet network needs.
  Predictable patterns of frame sizes, sources, and destinations.
Maximally interfering (continuous) traffic, characterized by:
  Maximum bandwidth
  Frame size limitations
Both have in common:
  Sender promises not to exceed the flow characterization.
  Network promises zero congestion loss and a firm maximum end-to-end latency.

## Slide 7: Two kinds of traffic
Scheduled (bursty) traffic, characterized by:
  Regularly-scheduled transmission bursts, the phases of which may be adjustable to meet network needs.
  Predictable patterns of frame sizes, sources, and destinations.
Maximally interfering (continuous) traffic, characterized by:
  Maximum bandwidth
  Frame size limitations
Both have in common:
  Sender promises not to exceed the flow characterization.
  Network promises zero congestion loss and a firm maximum end-to-end latency.
We will talk only about continuous traffic

## Slide 8: Scheduled traffic
Each frame has a latency of only 2 ticks, but only because each frame is sent on a schedule.
Total time: 6 ticks

## Slide 9: Continuous (maximally interfering) traffic
All sources can transmit at the same time. Latency is 2-6 ticks, depending on luck.
Total time: 6 ticks  (the same)

## Slide 10: ATS P802.1Qcr Asynchronous Traffic Shaping
Asynchronous Traffic Shaping is a work in progress.
In its net effect, it can be understood as a significantly improved version of RFC1633 Integrated Services. It has per-flow regulators and methods for selecting among them for output.
It will not be described in detail, here, but will be compared to other techniques.
IN PROGRESS

## Slide 11: CQF2 2-buffer Cyclic Queuing and Forwarding
IEEE Std 802.1Qch. All forwarding nodes are synchronized. Link delays should be less than the cycle time. No per-flow state. End-to-end delay = one cycle per hop.
sTANDARD

## Slide 12: CQF3 3-buffer Cyclic Queuing and Forwarding
Permitted* by, but not described in, IEEE Std 802.1Qch. Three buffers allow for input and output switching at different times so that link delay does not lengthen cycle time.
INPUT CLOCK
OUTPUT CLOCK
“Standard”
* There is no open project in IEEE 802.1 to describe this use case.

## Slide 13: Multi-CQF Multiple cycle periods on one port
Proposed by this author. Permitted* by, but not described in, IEEE Std 802.1Qch. Multiple cycle times support classes of service at different throughput rates and latencies on one port.
Fast cycle at higher priority
* 802.1Qch imposes significant limitations to multi-CQF. There is no open project in IEEE 802.1 to remove these limitations.
SPECULATION
High-priority clock
Low-priority clock

## Slide 14: Paternoster*
Proposed by Mick Seaman. Each flow has a limiting function to ensure that it does not exceed its per-cycle byte count; overflow goes into next CQF buffer. Cycle times not synchronized over network.
* There is no project in IEEE 802.1 to standardize the Paternoster algorithm.
Limiters/ policers
SPECULATION

## Slide 15: Disclaimer - again
This presentation is the personal opinion of a long-time contributor to the IEEE 802.1 process. It does not claim to represent the opinions of IEEE 802.1 as a whole, or of any of the other participants in that Working Group.
Some of the methods described are in published standards. Some are work in progress. Some are simply proposals presented publicly in IEEE 802.1.
Some people may disagree with this author’s characterization of either the standards, the work in progress, or the proposals.

## Slide 16: All methods offer valuable trade-offs
Let’s look at several performance criteria:
  Efficient use of reserved bandwidth (lack of overprovisioning)
  Need for clock and/or frequency synchronization
  Scaling issues:
    Per-flow, per-node state machine configuration required
    Difficulty of computing actual latency and required buffers
  Variability in end-to-end latency delivered
  Different target use cases
OPINION

## Slide 17: Efficient use of available bandwidth
ATS can make use of every byte and every nanosecond, subject only to clock frequency inaccuracies, for flows with a wide range of characteristics in one network. It provides the lowest latency and uses the least buffer space.
The other schemes pack data into fixed-sized buffers, and require margins for packing waste. A limited number of cycle frequencies can be offered, resulting in much higher latency for flows that fit the available frequencies poorly. These can be made less relevant by offering only a few selections of flow characteristics, rather than an infinite variety.
OPINION

## Slide 18: Clock and frequency synchronization
ATS requires no clock synchronization. Slight overprovisioning takes care of small clock frequency differences.
Paternoster requires no clock synchronization. It requires a little overprovisioning for clock inaccuracy.
CQF2/3 and multi-CQF require frequency locking, meaning bounded variation in the phase differences among nodes. This is because they use reception time to direct frames to the right buffer.
OPINION

## Slide 19: Scaling issues
CQF2/3 or multi-CQF require no per-flow, per-node state, so provisioning a new flow is limited to configuring ingress protection, if necessary.
Paternoster requires allocating and configuring a simple state machine at each hop for each flow.
ATS requires allocating and configuring a more complex state machine at each hop for each flow.
  The latency calculation is complex only for ATS, because adding a flow to the network affects the latency of any existing flow whose path it crosses. For the other methods, the addition of a new flow does not affect the latency of other flows. For the CQF methods, the latency calculation is a trivial sum.
OPINION

## Slide 20: End-to-end latency variability
  CQF2/3 and multi-CQF deliver all frames with a variability of one cycle-sized window.
  The latency of a flow using ATS or Paternoster varies with network load, although it never exceeds the calculated maximum.
OPINION

## Slide 21: Combinations
The possibilities are not limited to those shown, so far.
  ATS can serve multiple classes of service, with differential treatment for different classes, and fairness within a class.
  Paternoster can be operated, like multi-CQF, with multiple classes of service at multiple cycle times on the same port.
  Paternoster can provide ingress traffic conditioning for any CQF, and is required at boundaries where CQF changes cycle time.
  Techniques can be combined on one port with deterministic results. ATS or Paternoster can be used for a few low-latency flows, and multi-CQF for large numbers of higher-latency flows.
OPINION

## Slide 22: SUMMARY Ideal target use cases
  ATS: Best in small networks, or where most flows are known beforehand, where optimum performance over a wide range of flow requirements is required.
  CQF2, CQF3: Best in large, dynamic networks with changing flows, where flow requirements are not severe.
  Paternoster: Works well in networks intermediate in dynamics. Similar to CQF, but extends to higher-throughput, lower-latency flows, and does not require frequency locking.
  Combinations: Allow one to tailor the tradeoffs between performance and cost.
OPINION

## Slide 23: Thank you