## Slide 1: ITU Workshop on "Future Trust and Knowledge Infrastructure", Phase 1 Geneva, Switzerland, 24 April 2015
Session 4 – IoT data platform based on oneM2M
Dr. Omar Elloumi,
Technical Plenary Chair,
Alcatel-Lucent (oneM2M member)
oneM2M www.oneM2M.org

## Slide 2: The Partnership Project
Over 200 member organizations in oneM2M

## Slide 3: Purpose & Deliverables
Purpose To specify and promote an M2M Common Service Layer
Deliverables
Technical Reports and Technical Specifications

## Slide 4: M2M Common Service Layer in a nutshell
It is a software layer
It sits between M2M applications and communication HW/SW that provides data transport
It normally rides on top of IP
It provides functions that M2M applications across different industry segments commonly need. Those functions are exposed to Applications via IT-friendly APIs.
It allows for distributed intelligence (device, gateway, cloud apps)

## Slide 5: Standardization approach
Use cases
Requirements
Architecture
APIs and protocols
Test and Interop
Automotive
Home
Energy
E-Health
Security & privacy
Device Management
Data exchange
Interworking
IP communications
Restful webservices APIs
Reuse of existing protocols
Semantics framework (future)
Reference points
Device certification
Open source

## Slide 6: oneM2M Architecture approach
Horizontal framework, Restful API
Objects represented as resource
Access control policy to access resource
IoT will be based on ontologies (formal description of concepts and relationships, e.g. W3C Semantic Sensor Network) as well as big data frameworks
Currently developed solutions are similar are vertically integrated, with limited integration of data models (Zigbee, DLMS for smart meters, etc.).
Automotive Application
Energy Application
Home Application
Automotive Application
Energy Application
Home Application
Communication Technologies & Protocols
Communication Networks
Common Service Layer
Communication Devices & Hardware
TOMORROW
IoT enabled
IoT ready

## Slide 7: Common Service Functions
Registration
Group Management
Security
Discovery
Data Management & Repository
Application & Service Management
Device Management
Subscription & Notification
Communication Management
Service Charging & Accounting
Location
Network Service Exposure

## Slide 8: Why does it matter
Healthy eco-system with economies of scale
More partnering choices and opportunities for M2M/IOT industry stakeholders
Combat fragmentation
Standardized protocols / APIs -> simplifies application development/deployment
Cross-vertical standards -> same devices and back-ends in different industries
Lower CAPEX
Standard features to use networks more efficiently -> get better tariffs
Flexibility for verticals -> utilize best transport network meeting business needs
Lower OPEX
Reduced development, test and deployment lifecycles through focusing on core business (application logic)
Time to Market
oneM2M is IoT ready

## Slide 9: Technical Specifications
Service Components
TS-0007 (WI-0011)
Security Solutions TS-0003 (WI-0007)
MQTT Protocol Binding TS-0010 (WI-0014)
Service Layer
Core Protocols
TS-0004 (WI-0009)
Functional
Architecture
TS-0001 (WI-0002)
Definitions & Acronyms
TS-0011 (WI-0003)
Requirements TS-0002 (WI-0001)
ftp://ftp.onem2m.org/Work Programme/
Management Enablnt - BBF TS-0006 (WI-0010)
Management Enablnt - OMA TS-0005 (WI-0010)
CoAP Protocol Binding TS-0008 (WI-0012)
HTTP Protocol Binding TS-0009 (WI-0013)

## Slide 10: Example Scenario – E-Health
Patient
E-Health Web-application
Medicalized support
M2M Platform
Blood Pressure Meter
Scales
Bluetooth Smart Network
Tech support Application
Doctor
Cellular Network
Pill dispenser with integrated comm. gateway

## Slide 11: Design principles
IP-based, but interworks with specific IP and non IP technologies in the M2M Area networks
RESTful resource oriented APIs, resources are representations of devices, applications, things and related descriptions, etc.
Distributed intelligence (device, gateway, edge, cloud)
Reuse of existing device management frameworks
Reuse of existing data exchange protocols
Reuse of existing security
Reuse of underlying network capabilities such as location, triggering, etc.
Resource access control policies allows many to many communications framework
Future proof – ready to add semantics support
No mandated implementation (Database choice, intelligence location, etc.)

## Slide 12: Architecture
Underlying Network
Underlying Network
AE
NSE
AE
NSE
NSE
NSE
Application Service Node
Middle Node
Infrastructure Node
Application Layer
Network Layer
AE
Application Entity Provides application logic for the end-to-end M2M solutions
Network Services Entity Provides services to the CSEs besides the pure data transport
Node Logical equivalent of a physical (or possibly virtualized, especially on the server side) device

## Slide 13: Architecture
Underlying Network
Underlying Network
CSE
AE
NSE
CSE
AE
NSE
CSE
AE
NSE
NSE
Application Service Node
Middle Node
Infrastructure Node
Application Layer
Service Layer
Network Layer
Mca
Mcn
Mca
Mca
Mcn
Mcn
Mcn
Mcc
Mcc
Reference Point One or more interfaces - Mca, Mcn, Mcc and Mcc’ (between 2 service providers)
Common Services Entity Provides the set of "service functions" that are common to the M2M environments
Application Entity Provides application logic for the end-to-end M2M solutions
Network Services Entity Provides services to the CSEs besides the pure data transport
Node Logical equivalent of a physical (or possibly virtualized, especially on the server side) device
CSE
Mcc’
Inf. Node

## Slide 14: Concrete example
New measurement value available
Write to //MN-CSE/A
MN-CSE notifies aggregation app about new data, MN-CSE keep a copy of the data
for subsequent use
New measurement value available
Write to //MN-CSE/A
MN-CSE notifies aggregation app about new data, MN-CSE keep a copy of the data
for subsequent use
… etc, etc …
Ask MN-CSE to write aggregated/transformed data to //IN-CSE/B…. and BTW, this is low priority and you got 12 h time for that!
MN-CSE checks with policies and when time is good gets connected…
..and writes aggregated data to //IN-CSE/B
IN-CSE notifies network app (DB, HRN) about new data.
Measurement app can simply keep on delivering its data to the MN-CSE Aggregation app gets always notified about the new bits coming in
MN-CSE will store-and-forward aggregated/transformed data at a good time IN-CSE will notify DB app when new data arrived
=> Very little effort to synch the different apps
M2M Gateway
MN-CSE
Aggregation & format conversion
IN-CSE
M2M Device
Local Connectivity
3G Network
Measurement App.
M2M customer’s application
A
B
Resources
Starting assumptions: - Bootstrapping / DM is done (provisioning of credentials/apps) - MN-CSE and IN-CSE have logically connected (authentication, binding, encryption)
- Apps have authenticated to xCSE and access right were established

## Slide 15: Information Modelling
Resource-based information model
Information is stored in the system as Resources
A given Resource can be identified with a Uniform Resource Identifier
  A given Resource is of one of the defined Resource Types
  The Resource Type determines the semantics of the information in the Resource
  Resources can be Created, Read, Updated or Deleted to manipulate the information
  Resources are organized in a tree-like structure and connected by links

## Slide 16: Communication Protocols
  Reuse IP-based existing protocols
Service Layer
Core Protocols
TS-0004
CoAP Binding TS-0008
MQTT Binding TS-0010
HTTP Binding TS-0009
  XML or JSON Content serialization
  HTTP Example
REQUEST
GET http://provider.net/home/temperature HTTP/1.1 Host: provider.net From: //provider.net/CSE-1234/WeatherApp42 X-M2M-RI: 56398096 Accept: application/onem2m-resource+json
RESPONSE
HTTP/1.1 200 OK X-M2M-RI: 56398096 Content-Type: application/onem2m-resource+json Content-Length: 107 {"typeOfContent":"application/json", "encoding":1, "content": "{'timestamp':1413405177000,'value':25.32}" }

## Slide 17: Security Challenges & Solutions
Large variety of scenarios
Any device in any deployment
A device cannot make “judgment calls” on privacy
Secure communication
    various authentication options
Remote provisioning
    various authentication options
Access Control Policy
    express wide variety of rules

## Slide 18: Interworking – OMA & BBF
oneM2M
Domain
DM
Domain
  Reuse existing Device Management technologies
Application Entity
IN-CSE
Mca
OMA DM 2.0
OMA DM 1.3
OMA LWM2M
BBF TR-069
BBF Server
BBF CPE
BBF Device
DM Server
DM Client

## Slide 19: Privacy principles
System allows tracing and history of all interactions
Accountability
Each resource has an Access Control Policy (ACP) which specifies who (which entity) can access the resource, R/W permissions and under which context (time of the day, etc)
Applications link published data to ACP according to user consented purpose
Use limitation
Collected data is assigned a time-stamp and linked to a producer entity
Expiration time ensures old data is removed – could be used to enforce data retention policy
Data quality
Authentication and authorization, secure communications
Security safeguards
PI owner provides prior consent about the intended use of data – applications set Access Control Policy accordingly
Participation
oneM2M technology answer examples

## Slide 20: Thank You!
Q&A