## Slide 1
Wet Demonstrator Objectives

## Slide 2: A Brief History
Functional Requirements First Draft July 2014
Wet Demonstrator Scope First Draft July 2014
Singapore Workshop Discussions Oct 2014
General Requirements Draft to ITU Feb 2016

## Slide 3: Submission to ITU SG15
Establishes criteria for
  Sensor performance
  General capabilities: reliability, design life, environment, repair
  Operational requirements: error rate, latency, calibration, management
Does NOT impose requirements on:
  Power delivery
  Communications
  How to build it
“Compliance with this Recommendation is voluntary.”

## Slide 4: Features of a sensor-enabled submarine cable system
A sensor-enabled submarine cable system incorporates temperature, pressure and three-axis acceleration sensors at regular intervals along the cable. Sensor sets are nominally located once per repeater span, however other arrangements may be considered. Sensor sets shall be no more than 150 km apart.
The system shall provide continuous power for the sensors and a means of transmitting data to one or more shore stations.
The presence of sensors shall not preclude the use of branches, fixed OADM or ROADM. To the extent feasible, branch cable segments should also be equipped with sensors.

## Slide 5: Capabilities of a sensor-enabled cable system
The presence of sensors and the sensor subsystem shall have no net impact on the performance of telecommunications functions. Any allocation to the system performance budget resulting from the sensors or sensor subsystem shall be identified.
The addition of sensors and the sensor subsystem shall have negligible impact on the availability of telecommunications functions. Any unavailability resulting from the presence of the sensors and sensor subsystem shall be identified.
The design life of the sensor subsystem shall be ten years or greater.
Sensor failures or sensor subsystem failures that have no affect on telecommunications functions will not be repaired.
The sensors and sensor subsystem shall be compatible with conventional installation methods including, but not limited to, cable transport, cable and repeater storage on vessels, linear cable engines, three meter sheaves, plough burial, ROV burial and jetting.

## Slide 6: Wet Demonstrator Objectives - Science
Demonstrate the ability of sensors to be installed as part of a submarine telecommunications system
Demonstrate the accuracy and usefulness of the sensor data when the sensors are deployed in a realistic manner
Prove the assumptions related to sensor orientation and direction when laid as part of a cable system

## Slide 7: Wet Demonstrator Objectives - JTF
Provide baseline requirements that will facilitate continued discussion
Maintain and strengthen interaction between interested parties
Establish credibility needed to solicit more substantial resources from governments, NGOs, and industry

## Slide 8: Wet Demonstrator Objectives - Suppliers
Encourage system suppliers to allocate modest resources to early development stages
Allow system suppliers to consider suitability of existing product lines

## Slide 9: Wet Demonstrator Engineering Goals
Sensors can be integrated into the cable system;
Sensors can survive deployment stresses;
Data can be collected and transmitted to shore;
Data will provide value to science, and
The system can continue to operate for months or years.

## Slide 10: Configuration Requirements
Each sensor set shall consist of one temperature sensor, one pressure sensor, and one three-axis accelerometer meeting the performance parameters provided in the Functional Requirements.
Sensors shall be housed in or placed adjacent to a cable body that matches the physical and mechanical characteristics of a repeater housing.
The submarine cable shall be a conventional [12mm], 17mm, 20mm or 21mm type suitable for the expected deployment conditions such as Lightweight (LW) or Lightweight Protected (LWP), or a cable armor type that is typically used for repeater tails.
Power and communications shall be provided to the sensors. Note, however, that the power feeding and communications methods are not required to be similar to a conventional cable system and may be specific to the wet test.
Note: It is expected that each supplier will demonstrate full integration of the sensors into their repeaters through appropriate qualification and sea trials at a later stage of development.

## Slide 11: Basic Configuration

## Slide 12: Connection to Observatory
The wet test will be laid in an area of seabed supported by a cabled observatory
The observatory shall agree to make the data from the wet test available to interested parties for review and verification
The wet test shall include a suitable wet-mate connector for connection to a cable observatory.
The wet test shall include any necessary adaptation to convert power received from the cabled observatory to power needed for the sensors.
The wet test shall include any necessary adaptation to connect the sensors and the wet test system to the communications interface provided by the cabled observatory.

## Slide 13: Installation
The wet test shall be laid using conventional cable lay equipment
At least one sensor location shall be visually inspected by ROV after installation.
The wet test cable will be laid at typical speed for repeater installation. No attempt will be made to reduce loads on the instrument housing.

## Slide 14: Criteria for Success
All sensors operational following installation
99.99% availability of sensor data over test period
No more than one sensor of each type failing over a six month period
Successful validation of sensor data based on agreed qualitative and quantitative criteria

## Slide 15: Summary
Representative Mechanical Design
  Real repeater housing
  Sensor attachment to housing or cable
No Specific Electrical Power Requirements
  Does not require repeater power supply
  Any convenient method can be used
No Specific Communications Requirements
  Does not require integration to optical line
  Any convenient method can be used

## Slide 16: Criteria for Success
All sensors operational following installation
99.99% availability of sensor data over test period
No more than one sensor of each type failing over a six month period
Successful validation of sensor data based on agreed qualitative and quantitative criteria

## Slide 17: Do requirements need to be modified?
First two requirements for the wet demonstrator are intended to simulate a repeatered telecom system
A repeater or repeater-like housing is required, as is the ability to terminate the cable onto this housing
Relaxing or removing the first two requirements would allow alternative mechanical designs

## Slide 18: Revised Requirements
Sensors can be deployed on an instrument platform of any convenient design
Deployment assumes good weather, careful handling
Data can be collected and transmitted to shore
Data will provide value to science, and
The system can continue to operate for months or years.

## Slide 19: Revised Development Effort
Off-the-Shelf
  Sensors
  Serial converters
  Optical ethernet links
  Housings
Re-use Existing Bespoke Designs
  DC-DC converters
  Cable termination
Potential Suppliers
  Telecom system suppliers
  Systems integrators
  Ocean observatory engineering teams

## Slide 20: Revised Engineering Goals
Sensors can be integrated into the cable system;
Sensors can survive deployment stresses;
Data can be collected and transmitted to shore;
Data will provide value to science, and
The system can continue to operate for months or years.

## Slide 21: Conclusions
Wet demonstrator requires development of mechanical interface to a repeater
Wet demonstrator does not require electrical or optical integration
Efforts to engage industry are ongoing
Alternative approaches would diminish the value of the Wet Demonstrator