## Slide 1: Typology and Benchmark of Tools for Assessing the Mobile Networks QoS and QoE
Session 4: Tools and Methodologies for Testing the Quality of Service for Mlutimedia Services over Internet/Broadband Networks (Mobile and Fixed)
ITU Regional Standardization Forum, SG 5 and SG 12 Regional Group for Africa
Dakar, Sénégal, 24 -25 March 2015
Speaker: Prof. Sami TABBANE

## Slide 2
Quality KPIs: Measured and Perceived
1
Processes and Tools
2
4G Innovations
3
Annex: SFM Presentation and Tools
4
Agenda

## Slide 3: Impact Indexes of QoE

## Slide 4
QoS KPIs
Call Blocking Rate
Call Success Rate
Call Drop Rate
Voice quality
MSC/BSC/Network Availability
International Availability
Network Efficiency Ratio
SMS Access Success Rate
Received SMS Rate
MMS Access Success Rate
Received MMS Rate
Internet Connection Success Rate
Data Transmission Throughput
Internet Session Maintain
Data Connection Establishment Duration
Web Service Unsuccessful Rate
Apparent Web Service Throughput
FTP Data Service Connection Failure Rate
Apparent Throughput of the FTP Service
Coverage

## Slide 5
Which quality indicators are important for the user?
Results of a survey conducted in Tunisia (2014)

## Slide 6
Telephony service reliability
Base : 286 répondants
Chart: 
| Très important | Plutôt important | Plutôt pas important | Pas important du tout
% | 0.6958 | 0.22028 | 0.08042 | 0.0034965
91,6%
8,3%
Moyenne / 100
90,2

## Slide 7
SMS service reliability
Base : 286 répondants
Chart: 
| Très important | Plutôt important | Plutôt pas important | Pas important du tout | NSP
% | 0.3042 | 0.3007 | 0.17483 | 0.1958 | 0.024476
60,5%
37,1%
Moyenne / 100
68,2

## Slide 8
MMS service reliability
Base : 286 répondants
Chart: 
| Très important | Plutôt important | Plutôt pas important | Pas important du tout | NSP
% | 0.11189 | 0.12587 | 0.15385 | 0.55245 | 0.056
23,8%
70,6%
Moyenne / 100
44,6

## Slide 9
Internet service reliability
Base : 286 répondants
Chart: 
| Très important | Plutôt important | Plutôt pas important | Pas important du tout | NSP
% | 0.49301 | 0.15035 | 0.062937 | 0.25874 | 0.034965
64,3%
32,2%
Moyenne / 100
72,7

## Slide 10
Call success rate importance
Base : 286 répondants
Chart: 
| Très important | Plutôt important | Plutôt pas important | Pas important du tout | NSP
% | 0.83916 | 0.11888 | 0.027972 | 0.01049 | 0.003
95,8%
3,8%
Moyenne / 100
94,8

## Slide 11
Communications quality importance
Base : 286 répondants
Chart: 
| Très important | Plutôt important | Plutôt pas important | Pas important du tout
% | 0.87762 | 0.094406 | 0.020979 | 0.006993
97,2%
2,8%
Moyenne / 100
96,1

## Slide 12
City indoor coverage importance
Base : 286 répondants
Chart: 
| Très important | Plutôt important | Plutôt pas important | Pas important du tout | NSP
% | 0.8986 | 0.073427 | 0.017483 | 0.006993 | 0.003
97,2%
2,4%
Moyenne / 100
96,7

## Slide 13
Outdoor coverage outside cities
Base : 286 répondants
Chart: 
| Très important | Plutôt important | Plutôt pas important | Pas important du tout | NSP
% | 0.8007 | 0.11538 | 0.055944 | 0.020979 | 0.007
91,6%
7,7%
Moyenne / 100
92,7

## Slide 14
Indoor coverage importance
Base : 286 répondants
Chart: 
| Très important | Plutôt important | Plutôt pas important | Pas important du tout | NSP
% | 0.87063 | 0.076923 | 0.041958 | 0.006993 | 0.003
94,8%
4,9%
Moyenne / 100
95,4

## Slide 15
Incar coverage importance
Base : 286 répondants
Chart: 
| Très important | Plutôt important | Plutôt pas important | Pas important du tout | NSP
% | 0.62937 | 0.17133 | 0.087413 | 0.1014 | 0.01049
80,1%
18,9%
Moyenne / 100
83,5

## Slide 16
Call continuity (no call drops for 100 calls)
Base : 286 répondants
Chart: 
| Très important | Plutôt important | Plutôt pas important | Pas important du tout | NSP
% | 0.36713 | 0.21678 | 0.24476 | 0.16084 | 0.01
40,6%
Moyenne / 100
69,9
58,4%

## Slide 17
Base : 286 répondants
Chart: 
| Très important | Plutôt important | Plutôt pas important | Pas important du tout | NSP
% | 0.38462 | 0.18182 | 0.3042 | 0.11888 | 0.01
56,6%
42,3%
Moyenne / 100
71,0
Call continuity (no call drops for 50 calls)

## Slide 18
Base : 286 répondants
Chart: 
| Très important | Plutôt important | Plutôt pas important | Pas important du tout | NSP
% | 0.52448 | 0.23077 | 0.17483 | 0.059441 | 0.01
75,5%
23,4%
Moyenne / 100
80,8
Call continuity (no call drops for 20 calls)

## Slide 19
The 5 most important criteria (by order of importance)
1st criteria
Base : 286 répondants
Chart: 
| La couverture à l'intérieur des bâtiments | La continuité de la communication, c'est à dire la non existence de coupures | L'aboutissement des appels composés | La couverture à l'extérieur tout en restant à l'intérieur de la ville | La qualité de la communication | La Couverture à l'extérieur sur les routes | La couverture à l'intérieur des véhicules
% | 0.25874 | 0.17832 | 0.17133 | 0.13287 | 0.11189 | 0.11189 | 0.034965

## Slide 20
Base : 286 répondants
Chart: 
| La couverture à l'intérieur des bâtiments | La qualité de la communication | La Couverture à l'extérieur sur les routes | L'aboutissement des appels composés | La couverture à l'extérieur tout en restant à l'intérieur de la ville | La continuité de la communication, c'est à dire la non existence de coupures | La couverture à l'intérieur des véhicules
% | 0.22581 | 0.18996 | 0.17563 | 0.12545 | 0.12545 | 0.09319 | 0.064516
The 5 most important criteria (by order of importance)
2nd criteria

## Slide 21
Base : 279 répondants
Chart: 
| La qualité de la communication | La couverture à l'intérieur des bâtiments | La couverture à l'intérieur des véhicules | La Couverture à l'extérieur sur les routes | La couverture à l'extérieur tout en restant à l'intérieur de la ville | La continuité de la communication, c'est à dire la non existence de coupures | L'aboutissement des appels composés
% | 0.20073 | 0.17153 | 0.15328 | 0.14599 | 0.12774 | 0.10219 | 0.09854
The 5 most important criteria (by order of importance)
3rd criteria

## Slide 22
Base : 274 répondants
Chart: 
| La qualité de la communication | La continuité de la communication, c'est à dire la non existence de coupures | La couverture à l'extérieur tout en restant à l'intérieur de la ville | La Couverture à l'extérieur sur les routes | La couverture à l'intérieur des bâtiments | La couverture à l'intérieur des véhicules | L'aboutissement des appels composés
% | 0.18251 | 0.1597 | 0.14449 | 0.14068 | 0.14068 | 0.12548 | 0.10646
The 5 most important criteria (by order of importance)
4th criteria

## Slide 23
Base : 263 répondants
Chart: 
| La continuité de la communication, c'est à dire la non existence de coupures | La couverture à l'extérieur tout en restant à l'intérieur de la ville | L'aboutissement des appels composés | La Couverture à l'extérieur sur les routes | La couverture à l'intérieur des véhicules | La qualité de la communication | La couverture à l'intérieur des bâtiments
% | 0.20307 | 0.16475 | 0.15709 | 0.15326 | 0.13027 | 0.11494 | 0.076628
The 5 most important criteria (by order of importance)
5th criteria

## Slide 24
Quality KPIs: Measured and Perceived
1
Processes and Tools
2
4G Innovations
3
Annex: SFM Presentation and Tools
4
Agenda

## Slide 25: QoS and QoE measurements tools
Measurement techniques
Measurements
Field
System
Surveys
Measurement tools
Surveyors
OMC raw data
Passive probes
Calls and sessions generators
Generic/
Specific
Manual/ Automatic
Tools: no tool or technique is able to catch all the QoS of a network.
 Operators are using several tools (specific or not) on different interfaces (complementary or not)
Passive
Active

## Slide 26
Solution | Advantages | Drawbacks
Drive tests | Track the events at a geographical level and step by step | Not exhaustive (geographical and temporal) Heavy costs and logistics
OMC raw data analysis | Geographically (all the cells) and timely exhaustive (all the network) Reduced cost | Lacks the tracking of the events linked to a particular call or a session Lacks of measurements in coverage holes
Subscribers service perception surveys | Reflects the QoE as actually perceived by the users | Costly (surveys) Subjective
Field surveys | Voice quality measurements more objective | Costly (logistic and surveyors) Limited in time and space
Subscriber’s mobile based applications | Low cost Geographical and temporal representative, from the services usage | Lack of some parameters non available May have an impact on the mobile phone of the user
Main tools for measuring QoS and QoE parameters

## Slide 27
Subs. A | Subs. B | Dropped Call
+33 6 XXXX XXXX | +33 1 XXXX XXXX | No
+33 6 XXXX XXXX | +33 4 XXXX XXXX | Yes
CDR: Call Data Record
Measurement field
Call | SpQ
X Y Z | Bad Excellent Good
BTS
BSC
MSC
Raw data | Value
A | 3.15
B | 1.05
C | 0.95
NE counters
Drive tests
OMC counters
Capture tool
Measurement types
QoS parameters measurements

## Slide 28
RNC
3G GGSN
3G SGSN
Server
application
Node B
UTRAN
Core nw
External nw
E2E
service
quality,
QoE
Performance
statistics
Statistics from different counters and interfaces
Back to
user
Control of network performance
 Optimization
Measurements of network performance
QoS parameters measurements

## Slide 29
Different services  different QoS needs
  KPIs should be defined separately for each service
Example: voice services - CS
KPI categories | Indicators | Measurements
Service accessability | Coverage availability Call blockage rate Call establishment delay | Ec/No, RSCP Admission control RAB assignment
Service integrity | Voice quality | Noisy frames (FER), MOS
Service retainability | Dropped calls | Handover failure No coverage Interference
QoS parameters measurements

## Slide 30
Service FTP: FTP start-up failure rate, FTP abort rate, FTP throughput, …
Service HTTP: HTTP access failure rate, HTTP abort rate, HTTP access time, HTTP access time to text, HTTP throughput/delay, ...
Pusk-to-Talk over Cellular (PoC): PoC service availability, PoC service accessibility, PoC voice quality, PoC timely delivery of voice.
MMS: MMS send/retrieve failure rate, MMS send/receive throughput, MMS send/receive delay, MMS end-to-end delay, MMS notification delay.
WAP: WAP failure rate, WAP access time.
Ping: RTT
QoS parameters measurements
Service KPI

## Slide 31
 Manufactured for pedestrian measures.
It consists of:
  A portable equipment, installed in the backpack (based on HTC smartphones),
  An application XGMA controlled via a digital tablet allow auditing wireless networks in urban area, in shopping centers and public buildings.
This tool can also during the measurement campaign audit the service quality of mobile networks in car, when the vehicular is mobile.
Field measurements
Example of Net check tool (Infocom)

## Slide 32
Network Optimization Tools Used are as the following:
  TEMS Investigation
  Agilent E6474A
  Neptune
  CDMA Air Interface Tester (CAIT)
  TEMS DeskCat
  Actix Analyzer
  NEMO
  Gladiator
  NetAct
  Mentum
Field measurements

## Slide 33
Measurements
and
softwares
Controler
GPS
Energy
Man to machine interface
Processing
External antennas
Mobile QoS test equipment
Field measurements

## Slide 34
Voice quality measurement principle
voice quality Analysis

## Slide 35
Principle | Harvest from OMC (radio and network) events (counters) report from equipment Treatment of this counters ( with formula elaborated by the operating team or by treatment software)
Advantages | Global statistics: related to an BSC/ MSC/ SGSN/… area Less expensive than field measurements: distant measurements , no necessary to engage a team for measurements , …
Drawback | No localization of problems identified in radio level des (area with no coverage or interference area ) No follow up of one or multiple calls in particularly
Measurements | Radio measurements (KPI « classics »: QoS, traffic, performances, …)Network measurements (KPI « classics »: localization, attachment, calls, …)
OMC measurements

## Slide 36
Proprietaries
Alcatel: RNO
Siemens: SPOTS (Fair interest for statistic reports)
Ericsson: TEMS Analyzer
…
Generic (multi-manufacturer)
APIC of Metrica: Evolution problem
MyCom of MyCom: equivalent to Metrica but less adapted to sophisticated reporting
AirCom: generally preferment for classic statistics
NetAct SQM: Nokia
OVPI: HP (for IP equipment)
OMC measurements
Tools

## Slide 37
Principle | Collect in a network equipment (nodes) and/or in an interface the exchanged messages between the network and multiple mobiles (files typically .log)
Advantages | More global than field measurements: related (in function of the used interface) to a cell, to an area BSC/MSC/SGSN, … Less expensive than field measurements: distant measurements , no necessary to engage a team for measurements , …
Drawback | No localization of problems identified in radio level des (area with no coverage or interference area )
Measurements | Radio measurements (Signal power level in broadcast or point to point, interferences level , power of neighbor cells, cell parameters, …) Exchanged messages and occurred problems during a connection (LU/RU, call/session, HO, …) for all levels les (layers 1, 2, 3 and highest in function of interfaces).
Passive probes

## Slide 38
    Tektronics: K12/15XX (Failed statistics, …, simple and recently improved in term of ergonomic)
    Network General: Sniffer Pro + NPO (IP interfaces and analyzes via NPO)
    MyCom: NIMS-PrOptima (possibility of combination with drive tests in an SIG)
    Tekelec: Steleus 2.5 G (GPRS interfaces) and Steleus 3G (Iu interfaces ), multiple applicatives for de post-treatment. Preservation of data for few days. Supervision of the GPRS QoS on real time and production of QoS reports with alerts .
Passive probes

## Slide 39
    HP: Ovis (Test of data services, production of KPI of availability and of response delay).
    RadCom: Network Consultant (interfaces A, Gb, Gi, Gn, Iub, Iur, Iu, Gi et Gn): decoding frame , Very good in post-treatment ( mare richer in information than other products, as statistics on PDP liberation causes)
    Trafica (NetAct de Nokia)
    Ipanema: Ipanema (Fix probes for data traffic capture of 2,5 G et 3G).
    Cigale (Astellia): Probes for capturing traffic 2G and 3G
    Problems of update and maintenance comparing to other software manufacturer version
Passive probes

## Slide 40
Company | Product
Nethawk | 3G Analyzer
Agilent | Signaling analyzer
Tektronix | K15
Radcom | Performer analyzer
Acterna | Telecom Protocol Analyzer
Network interfaces analysis
Protocol analyzers

## Slide 41
Principle | Generation of serial calls and sessions, … according to predefined scenarios and harvest the ensemble of exchanged messages with detection of possible problems
Advantages | More exhaustive than probes Targeting procedures/mobiles/area/… with problems
Drawback | More expensive than probes Less « independents » than probes (because targeting in particular scenarios)
Measurements | Radio measurements (Power signal level in broadcast and in point to point, interference level, power of neighbor cells, cell parameters, …) Exchanged messages during a connection (LU/RU, call/session, HO, …) to all levels (layer 1, 2 et 3).
Calls generators

## Slide 42
Tools Benchmark
Vendors | DT measurement tools | DT post processing tools | OMC tools | Performance monitoring tools | Probes tools | Geolocation tools | Customer QoS surveys | Subjective voice quality evaluation | Customer QoE tool
Opticom |  |  |  |  |  |  |  | ✓ | 
Actix |  | ✓ | ✓ | ✓ |  |  |  |  | 
JDSU |  | ✓ | ✓ | ✓ |  |  |  |  | 
Xceed Tech |  | ✓ | ✓ | ✓ |  |  |  |  | 
Aircom |  |  | ✓ | ✓ |  |  |  |  | 
Ascom | ✓ | ✓ |  |  |  |  |  |  | ✓
Anite | ✓ | ✓ |  |  |  |  |  |  | ✓
Accuver | ✓ | ✓ |  |  |  |  |  |  | ✓
Accanto | ✓ | ✓ | ✓ |  |  |  |  |  | ✓
Net check | ✓ |  |  |  |  |  |  |  | 
Epitiro | ✓ |  |  |  |  |  |  |  | 
Ookla | ✓ |  |  |  |  |  |  |  | 
Dingli | ✓ | ✓ |  |  |  |  |  |  | ✓
Ericsson |  |  | ✓ |  |  | ✓ |  |  | 
Huawei |  |  | ✓ |  |  | ✓ |  |  | 
NSN |  |  | ✓ |  |  |  |  |  | 
Alcatel-Lucent |  |  | ✓ |  |  |  |  |  | 
QoS Tracker |  |  | ✓ |  |  |  |  |  | 
BI4T |  |  | ✓ |  |  |  |  |  | 
InfoVista |  |  | ✓ |  |  |  |  |  | 
Astellia |  |  | ✓ |  | ✓ |  |  |  | 
Pixipnet |  |  |  |  | ✓ |  |  |  | 
V3D |  |  |  |  |  |  |  |  | ✓
RTR-NetTest |  |  |  |  |  |  |  |  | ✓
Marketing institutes |  |  |  |  |  |  | ✓ |  | 
QoEntum |  |  |  |  |  |  |  |  | ✓

## Slide 43
Quality KPIs: Measured and Perceived
1
Processes and Tools
2
4G Innovations
3
Annex: SFM Presentation and Tools
4
Agenda

## Slide 44
Mobility: low mobility (0-15km/h) and high speeds
Latency: user plane < 5ms ; Control plane < 50 ms
Improved spectrum efficiency
Improved broadcasting
All IP
Scalable bandwidth
Carrier aggregation
Network sharing
Radio performance enhancement features
4G main features and the challenges for quality assessment
LTE performance requirements

## Slide 45: LTE releases evolutions and features

## Slide 46: Minimization of Drive Tests Principle
Defined in Rel-10 with the following objectives:
Ability of the UE to include location information as part of the UE radio measurement reporting
Ability of the UE to log radio measurements during the UE’s idle state
Reuse of radio measurements to those that have to be performed as part of normal RRM procedures, minimizing additional complexity and battery consumption by the UE.

## Slide 47: Conclusions
Drive testing was the very first type of tools for assessing the QoS,
System measurement tools (probes, OMC raw data, CDR based, …) used to get a wider picture of the network performance,
User experience focused measurements to be closer to user’s perception
Main issue so far in the transition to 4G and 5G
Trends in quality measurements

## Slide 48: Thank You!
Address: 81, Avenue Hédi Chaker – 1002 – Tunis – TUNISIA
Tel.: +216 71 845 248/ +216 98 377 887
Fax: +216 71 845 249
Contact: info@sfmtechnologies.com
Site Web: www.sfmtechnologies.com

## Slide 49
Quality KPIs: Measured and Perceived
1
Processes and Tools
2
4G Innovations
3
Agenda
Annex: SFM Presentation and Tools
4

## Slide 50
Services for Fixed and Mobile Telecommunications Network and Systems
Created: 1995 by an expert group of Engineers, consultants, specialists,
20+ Countries around the globe
40+ Cellular Networks
Activities: Strategic Consulting, Engineering, Technical Assistance and Training in Telecommunications
Customers: Telecom Ministry, Operators, Regulators, Consulting Company.
Synoptic

## Slide 51: SFM Group
SFM Telecom for local activities
SFM Technologies for consulting and expertise
SFM International for training
50+ Consultants and Experts
19+ Years of experience
40+ Cellular Networks
20+ Countries around the globe
Turn Over 2014: MUSD 1.8

## Slide 52
SFM
in 2014
50+Operators, Regulators
And Consulting Company
650+ Man-Days
Strategic Consulting
1800+ Man-Days of Technical
Assistance
550+ Man-Days Training
With 40% in site
SFM Group

## Slide 53: QoEntum: Automatic QoE for Network Performance Improvement And Business Monitoring
QoEntum Solution collects standard KPIs, including Voice and Data services from subscribers 'mobile Androïd smartphones. It reflects end-user experience and network performance perception. Information and measurements sent back to SFM server, where data are processed, stored, analyzed and immediately accessible via a secured web site.

## Slide 54
QoEntum: Sample screens

## Slide 55
Engineering and Optimization
Commercial and Marketing
CBR, CDR per area,
Mean call setup duration per area,
Signal level per user and per location,
Connected network (2G/3G/4G),
Real-time processing and display of the problems on maps
History of the measurements and comparison of networks performance (2G/3G/4G, region, …).
Data measurements: speed (UL, DL), setup success and delay,
HO rate,
Data activity rate,
Connection and sessions durations,
User information: UE type, location, activated services, used credit/SIM card and service, activity (sessions durations, calls, …), transmitted and received data volumes, …
Hotspots (density of test mobiles per area),
MOS and PESQ,
Mostly used application per subscribers,
Loss of revenues evaluation
User’s profile (behavior, …)
Perceived user quality
QoS and Legal Department
CDR, CBR, Call Setup Time etc. per region
Data services KPIs: speeds UL and DL per location,
White areas: coverage problems (holes, low signal level, indoor/incar/outdoor coverage),
Network performance tracking,
Compliance with license conditions
  Hotspots (density of test mobiles per area),
  MOS and PESQ,
  Mostly used application per subscribers,
  Loss of revenues evaluation
  User’s profile (behavior, …)
  Perceived user quality
USER
QoEntum: Indicators

## Slide 56
Central platform
Scenarios configuration,
Pricing formulas Setting,
Call generation,
Charging Information collecting,
Tariffs plans comparing,
Audit reports generation.
Backup
Collected Information Storage,
Databases,
Transaction History,
Generated reports.
SIM card platform for the generation of the calls, SMS and data sessions, and the collection of advice of charge.
Tariffs Tracker evaluates service tariffs as seen by the subscriber.
Tariffs Tracker: Automatic Control Tool of Telecommunications Services Tariffs

## Slide 57: Contact
Adresse: 8, Rue Ibn Sina – El Menzah VI – 2091 Ariana – TUNISIA
Tel.: +216 71 284 314/ +216 98 377 887
Fax: +216 71 284 314/ +216 71 754 842
Email: info@sfmtechnologies.com
Site Web : www.sfmtechnologies.com