## Slide 1: ITU Regional Standardization Forum For Africa Dakar, Senegal, 24-25 March 2015
Session 3 : Operational and Regulatory Aspects to Predict for a good QoS of the Internet Mobile in broadband networks
Hassan TALIB,
Vice-Chair ITU-T SG 12, Head DCT ANRT
Talib@anrt.ma // Htalib@ties.itu.int

## Slide 2: Plan of the Presentation
General Overview On QoS of the mobile Internet
Operational Aspects
Regulatory Aspects (ITU-T standards and recommendations)
  Regulatory Aspects at the national level
  Conclusions and recommendations
Senegal, Dakar, March 24-25, 2015

## Slide 3: General Overview on QoS of the Internet Mobile Perimeter of the Presentation
Networks concerned:
Mobile broadband networks, examples: 3G (UMTS and CDMA2000 ), 4G ( ), Wifi Outdoor (offloading ) ,...
Service concerned:
Mobile Internet on mobile broadband networks.
Senegal, Dakar, March 24-25, 2015

## Slide 4: General Overview on QoS of the Internet Mobile General Environment of the QoS
QoS And OTTs :
Services under Internet:
- Data *
- Videos *
- VoIP
...
* Concerned by this presentation
Internet QoS
Senegal, Dakar, March 24-25, 2015

## Slide 5: General Overview On QoS Of the Internet Mobile General Environment of the QoS
QoS Offered By The operator/Provider
QoS Issued By the operator/Provider
QoS Such that perceived By The subscriber
QoS Expected By the Users
Operator/Provider
Subscriber
(Theoretical/imaginary)
Difficult to deploy
(Operational/actual) a methodology for measuring and evaluation is necessary
Reference : The Recommendation Rec. G. 1000.
Senegal, Dakar, March 24-25, 2015

## Slide 6: General Overview On QoS Of the Internet Mobile Parameters of services "data"
Senegal, Dakar, March 24-25, 2015
Parameter | Example of Cause | Example of consequences | Example of influence QoS/QoE
Loss Of Packets | Errors Of transmission | Retransmission Of Packets | Delay In the navigation Flow low Download
Latency (End-to-end delay) | Files Of waiting, congestion | Delay In the real-time applications | Impossibility To play online Offset of a image of CCTV
Jitter | Use of different paths algorithms of different queuing in the nodes | The Stack do not arrive in the correct order | Delay In the navigation flow low download .

## Slide 7: General Overview On QoS Of the mobile Internet Parameters of services "video"
Senegal, Dakar, March 24-25, 2015
Parameter | Example Of cause | Example of consequences | Example of influence QoS/QoE
Time of onset of the first image slow | Bad Sizing the buffer | Great expectations before the start of the image | Great expectations before the start of the image
Availability of video | Server Congestion Link to slow transmissions | Flow of the non-continuous video | video stop offset of the video
The resolution and Frame-rate (Image by sec) | Bad Sizing of the resolution in relation to the user flow | Transmission Channel insufficient to route the video | Delays, stop of the Video
The Codec used | Bad compression therefore more data | Transmission Channel insufficient to route the video | Delays, stop of the video
Poor delivery of the video | The application of reading is poorly designed/configured | Bad synchronization of flows | Cut, stop of the video

## Slide 8: Plan of the presentation
General Overview On QoS Of the mobile Internet
Operational Aspects
Regulatory Aspects (ITU-T standards and recommendations)
  Regulatory Aspects at the national level
  Conclusions And recommendations
Senegal, Dakar, March 24-25, 2015

## Slide 9: Operational Aspects Services and classes of a UMTS network
The resources of the networks are allocated and managed according to the profile of QoS for each service.
Senegal, Dakar, March 24-25, 2015

## Slide 10: Operational Aspects Classes of a UMTS network
Senegal, Dakar, March 24-25, 2015

## Slide 11
Reference : The Recommendation Rec. ITU-T P. 1301.
Operational Aspects QoS Flow Chart of the Video Calling service
Senegal, Dakar, March 24-25, 2015
Telemeeting With texts and graphics
Telemeeting With the video only

## Slide 12
Reference : The Recommendation Rec. P. 1501.
Operational Aspects QoS Tests Architecture of Web service
Senegal, Dakar, March 24-25, 2015

## Slide 13: Operational Aspects QoS Architecture in a LTE network
Senegal, Dakar, March 24-25, 2015
A BEarer is a transmission medium of user traffic of signalling with the characteristics, transport attributions ,treatment of data and the resources allocated across the network: priority, flow, level of quality, ...
Two types of treatment have been defined.
Default BEarer :
-is established at the initial connection of the equipment to the network.
-remains established as long as the service has not changed. A subscriber may have multiple DefaultB each with an IP address.
Dedicated Bearer :
-is established when there is a need to ensure a level of QoS for a service: VoIP, Visio, Video,...
-This is the equivalent of a dedicated tunnel for one or several traffics. It is based on the IP of the Default Bearer.

## Slide 14
Operational Aspects Examples of QoS Indicators of Values in a LTE network
Senegal, Dakar, March 24-25, 2015
The Dedicated Bearers include two categories:
GBR: warranted debit
Non-GBR: unwarranted debit

## Slide 15: Operational Aspects Architecture of end to end QoS Evaluation in a broadband network
Gateway
NTP
End User
Internet Content Providers
Access Network
Public Internet
Physical Access
Transit
End-TB-End Service Quality
Download And Upload Speeds
Line Termination
Internet Service Provider Network
Local Switch
Senegal, Dakar, March 24-25, 2015

## Slide 16: Plan of the Presentation
General Overview On QoS Of the mobile Internet
Operational Aspects
Regulatory Aspects ITU-T (standards and recommendations)
  Regulatory Aspects at the national level
  Conclusions And recommendations
Senegal, Dakar, March 24-25, 2015

## Slide 17: Regulatory Aspects ITU-T General Framework The ITU-T recommendations under the SG12 dealing with the QoS/QoE
E. 420-E. 479, E. 800-E. 859
G. 100-series, Except G. 160-, G. 180- and G. 190-series
G. 1000-series
I. 350-series (Including Y. 1501/G. 820/I. 351), I. 371, I. 378, I. 381
P-Series, Except P. 900-series
Y. 1220-, Y. 1530-, Y. 1540-, Y. 1560-series

## Slide 18: Regulatory Aspects ITU-T General Framework The levels of the QoS
Senegal, Dakar, March 24-25, 2015

## Slide 19
Reference : The Recommendation Rec. G. 1000.
Methodology
E. 802 E. 803
QoS Model
Four Models of the Market
Performance Model
Universal Model
ACF Model
CSAT Model
Model of Satisfaction
QoS Such that perceived by the subscriber
QOP
Framework
ITU-T G. 1000
Subscriber
QoS issued by the operator/Provider
QoS
Operator/Provider
QoS Expected By the Users
QoR
SCAL (KQI)
Perception of the Subscriber
Waiting of the subscriber
Satisfaction Of
the subscriber
Non Satisfaction
Waiting
Waiting Review
QoS offered by The operator/provider
QoO
Regulatory Aspects ITU-T General Framework
Senegal, Dakar, March 24-25, 2015

## Slide 20
In implementation of the relevant recommendations of the ITU-T including the G. 1010 and G. 1050, we can establish guidelines concerning the requirements in terms of performance, the end user's point of view, about the different applications and aggregate them in a set of categories: numbering to (8). The categorization is based on the following parameters:
Regulatory Aspects ITU-T Categories of the QoS of Multimedia services/Internet
Reference : The Recommendations Rec. ITU-T G. 1010 and G. 1050.
The Delay and the losses of Packets ;
The variation of the delay (jitter).
Senegal, Dakar, March 24-25, 2015

## Slide 21
Regulatory Aspects ITU-T Categories of the QoS of Multimedia services/Internet
Reference : The Recommendations Rec. ITU-T G. 1010 and G. 1050.
Senegal, Dakar, March 24-25, 2015

## Slide 22
Regulatory Aspects ITU-T Categories of the QoS of Multimedia services/Internet
Reference : The Recommendations Rec. ITU-T G. 1010 and G. 1050.
Senegal, Dakar, March 24-25, 2015

## Slide 23
There are five types of objective evaluation models of the Multimedia/Internet quality:
Perceptual Models: The input to the model is the media itself (audio and video signals).
Parametric Models: The input to the model is the information from the flow of packets and the state of customer information. A parametric model also requires additional Information such as the type of codec and the binary debit.
Models of stream of bits: The input to the model is a piece of information derived from the flow and other information pertaining to the packets.
The hybrid models: The input to the model is the flow of the packets. Perhaps also information pertaining to the status of the client.
Planning Models: The input to the model includes the parameters for planning of the quality of Networks. It usually requires a prior knowledge of the testing.
Regulatory Aspects ITU-T Modeling of the QoS of Multimedia services/Internet
Senegal, Dakar, March 24-25, 2015

## Slide 24
Summary of the models of the ITU-T:
Application | Media | Through (CONV) /Non-Through (NONCONV) | Subjective Test methodology | Objective test methodology |  | 
 |  |  |  | Model | FR/RR/NR | Primary use
Telephony | Speech | NONCONV | (ITU-T P. 800] (ITU-T P. 830] (ITU-T P. 835] (ITU-T P. 1301] | (ITU-T P. 862) + (ITU-T P. 862.1 ] (NB) (ITU-T P. 862.2 ] (WB) (ITU-T P. 863] (NB/WB/SWB) | FR | LAB, MY
 |  |  |  | (ITU-T P. 563] (NB) (ITU-T P. 564] (NB/WB) | NR | MY
 |  | CONV | (ITU-T P. 800] (ITU-T P. 805] (ITU-T P. 1301] | (ITU-T G. 107] (NB) | NR | PLN
 |  |  |  | (ITU-T P. 561) + (ITU-T P. 562] (NB/WB) | NR | MY
Video telephony | Multimedia (Note) | CONV | (ITU-T P. 920] (ITU-T P. 1301] | (ITU-T G. 1070] (NB/WB) | NR | PLN
Regulatory Aspects ITU-T Modeling of the QoS of Multimedia services/Internet
Senegal, Dakar, March 24-25, 2015

## Slide 25
Summary of the models of the ITU-T:
Regulatory Aspects ITU-T Modeling of the QoS of Multimedia services/Internet
Application | Media | Through (CONV) /Non-Through (NONCONV) | Subjective test methodology | Objective test methodology |  | 
 |  |  |  | Model | FR/RR/NR | Primary use
Video streaming (Mobile TV/IPTV) | Video | NONCONV | (ITU-T P. 910] (ITU-T J. 140] [ITU-R BT.500-1 STANDARD3] | (ITU-T J. 144] (SD) (ITU-T J. 247] (QCIF, CIF, VGA) (ITU-T J. 341] (HD) | FR | LAB, MY
 |  |  |  | (ITU-T J. 249] (SD) (ITU-T J. 246) (QCIF, CIF, VGA) (ITU-T J. 342] (HD) | RR | MY
 | Audio | NONCONV | (ITU-T P. 830] [ITU-R BS.1116-1] [ITU-R BS.1285] [ITU-R BS.1534-1] | [ITU-R BS.1387] | FR/RR | MY/PLN
 | Multimedia | NONCONV | (ITU-T P. 911] | (ITU-T P. 1201.1 ] (QCIF, QVGA, HVGA) (ITU-T P. 1201.2 ] (SD, HD) (ITU-T P. 1202.1 ] (QCIF, QVGA, HVGA) (ITU-T P. 1202.2 ] (SD, HD) | NR | MY
Web browsing | Data |  |  | (ITU-T G. 1030] | NR | PLN
Senegal, Dakar, March 24-25, 2015

## Slide 26: Plan of the presentation
General Overview On QoS Of the mobile Internet
Operational Aspects
Regulatory Aspects (ITU-T standards and recommendations)
  Regulatory Aspects at the national level
  Conclusions And recommendations
Senegal, Dakar, March 24-25, 2015

## Slide 27
Examples of parameters for administrative QoS :
Regulatory Aspects at the national level
Provisions to provide by the regulator in the specifications/licensing of operators of broadband networks
Parameter (Unit) | Example of value (1Era Year) | Example of value (2Th Year)
Conformity of the network and the equipment to international standards (ITU) | -------------------- | --------------------
Permanence of Services (time and day) | 24/24 AND 7/7 | 24/24 AND 7/7
Cumulative Duration of unavailability of a base station must not exceed per year a duration (hour) | 24 | 12
Obligation of investment for more capacities to connect to the international (Gbps) | 200 | 400
Deadline for operating (in time) | 5 OR 7 | 4
Time of servicing failures (hour) | 24 | 12
Rate of litigation on invoices ( %) | 0.5 | 0.4
Senegal, Dakar, March 24-25, 2015

## Slide 28
Examples of parameters for technical QoS QoSQoS Techniques:
Regulatory Aspects at the national level Provisions to provide by the regulator in the specifications/licensing of operators of broadband networks
Parameter (Unit) | Example of value (1Era Year) | Example of value (2Th Year)
Success Rate of the first attempt ( %) | 95 | 98
Rate of successful connections in a fixed deadline (5 To 15s in relation to the network) ( %) | 96 OR 98 | 98 OR 99
The downflow average minimum required for 90% of the population covered (Mbps) | 2 Or 4 | 4 OR 7
Rate cut downloading or uploading ( %) | 5 | 3
Average time to start the video (s) | 10 | 15
Maximum number of stops of the video (figure) | 3 | 1
Senegal, Dakar, March 24-25, 2015

## Slide 29: Conclusions and Recommendations
  The requirement to establish a regulatory framework for the QoS for broadband networks at the national level.
  QoS for Internet in a context of mutation: NGN network all IP, IoT, IPv6, MTOM,...
  QoS for Internet at two speeds. Divergent Positions USA, Europe, ICANN,...
  OTTs And QoS : Problems of distributing the responsibilities?
Senegal, Dakar, March 24-25, 2015

## Slide 30
Thank you for your attention
Questions/Answers
Talib@anrt.ma // Htalib@ties.itu.int
Senegal, Dakar, March 24-25, 2015