## Slide 1: Regulatory aspects of quality of service From the standpoint of ITU-T E.800SerSup9: “Guidelines on regulatory aspects of QoS”
Hassan TALIB
Vice-Chair ITU-T SG 12, Head DCT ANRT
talib@anrt.ma // htalib@ties.itu.int
ITU Regional Standardization Forum for Africa
(Kampala, Uganda, 23-25 June 2014)

## Slide 2: Presentation outline
Presentation of ITU-T E.800SerSup9
QoS monitoring practices for the regulator
Measuring voice QoS on mobile networks
Measuring the QoS (data) of the mobile Internet
  Conclusions and recommendations

## Slide 3
Presentation of ITU-T E.800SerSup9
Guidelines on the regulatory aspects of QoS

## Slide 4: Presentation of ITU-T E.800SerSup9
Guidelines covering QoS measurements for practically all end-to-end services as perceived by the user. Non NP.
Main references are to the following ITU-T Recommendations:
  P.10/G.100 – General definitions
  E.800 – Definitions of terms related to QoS
  E. 803 – QoS parameters for supporting service aspects
  E.804 – QoS aspects for mobile services

## Slide 5: Presentation of ITU-T E.800SerSup9
Difference QoS and network performance, KPI and non-technical supports.
QoS and QoE.

## Slide 6: Presentation of ITU-T E.800SerSup9
Chain of influence end-to-end QoS:
  Standards development organizations
  Industry and equipment manufacturers
  Terminal device manufacturers
  Operators and service providers
  Regulators and administrations
  Consumers

## Slide 7: Presentation of ITU-T E.800SerSup9
The four basic elements of QoS regulation:
  Obtaining information on QoS levels and identifying problem areas (measurement and/or collection)
  Publishing information on QoS
  Make regulatory provision for minimum QoS thresholds to be observed by operators (with sanctions in case of non-observation)
  Maintain a constructive and ongoing dialogue with operators on the subject of QoS.

## Slide 8: Presentation of ITU-T E.800SerSup9
Objectives of QoS regulation (how to choose parameters and thresholds):
  Helping customers to make informed choices
  Checking complaints
  Understanding the state of the market
  Maintaining or improving quality in the presence or absence of competition
  Helping operators to achieve fair competition
  Making interconnected networks work well together

## Slide 9: Presentation of ITU-T E.800SerSup9
Activities in QoS regulation:

## Slide 10: Presentation of ITU-T E.800SerSup9
Approaches recommended under the guidelines:
  Make a good job of choosing, reviewing and updating QoS parameters and thresholds
  Adopt an encouragement and/or sanctions (penalties) approach
  Publish results on the website
  Maintain an ongoing and constructive dialogue between the regulator and operators
  Introduce SLAs into contracts between operators and users

## Slide 11
QoS monitoring practices for the regulator

## Slide 12: Basic principles for monitoring of QoS/QoE at ANRT
Regulator regularly monitors QoS
A national regulatory framework:
Duties
Operators’ QoS obligations
An international regulatory framework (standards):
ITU-T: series E, G, P, Y, QoS handbook, ...
Regional: ETSI
(series EG), IEEE, …
Benchmarking of best practices and technology watch
User feedback:
Complaints
Media
Consumer associations
…
Analysis of data received from operators in terms of performance, KPI and QoE measurements
Field measurements (campaigns) conducted by ANRT
QoE mechanism: QoE portal and downloadable applications
Kampala, Uganda, 24 June 2014
Adoption of a communication strategy (publications)

## Slide 13
Basic principles of QoS monitoring
Establishment of a global mechanism for receiving KPIs from operators: all networks and all services
Elaboration of reference documents, agreed by all players, setting out the QoS field measurements
Complete operational model of KPI data based on pre-established time intervals
Controlled externalization of measurements and use of results by operators
Kampala, Uganda, 24 June 2014

## Slide 14
Measuring voice QoS on mobile networks

## Slide 15: Protocol for voice QoS measurements
List and definitions of indicators
Rate |  | Indicator | Definition
TR |  | Rate of successful communications maintained during 2 minutes | A communication is considered as successful if the call launched succeeds at the first attempt and the communication is maintained for 2 minutes without being cut off. The rate (SR) is related to the number of successful communications and the total number of call attempts made.
TR | Perfect | Rate of successful communications maintained during 2 minutes with perfect audio quality | A communication is considered as successful and of perfect quality if it meets the indicator SR and the audio quality is considered by both parties as perfect (compared to the quality of direct communication).
 | Acceptable | Rate of successful communications maintained during 2 minutes with acceptable audio quality | A communication is considered as successful and of acceptable quality if it meets the indicator SR and the audio quality is considered by both parties as slightly degraded without disrupting the conversation.
 | Poor | Rate of successful communications maintained during 2 minutes with poor audio quality | A communication is considered as successful and of poor quality if it meets the indicator SR and the audio quality is considered by both parties as frequently degraded in the receiving channel by numerous disruptions on the line, but the conversation is still intelligible.
 | Bad | Rate of successful communications maintained during 2 minutes with bad audio quality | A communication is considered as successful but of degraded quality if it meets the indicator SR but it is very difficult for the parties to hear one another, such that the conversation is impossible.
RC |  | Rate of communications cut off | A communication is considered as cut off if, at the first attempt, it is established and maintained for more than 5 seconds, but cut off before 2 mins. The rate (CR) is the ratio between the number of cut- off communications and the total number of call attempts made.
RF |  | Rate of failed communications | A communication is considered as failed if, at the first attempt, it is not established or not maintained for more than 5 seconds. The Rate (FR) is the ratio between the number of failed communications and the total number of call attempts made.
SR + FR + CR = 100% and UR = FR + CR
SR
SR
CR
FR
15

## Slide 16: Protocol for voice QoS measurements
List and definitions of indicators
Evaluation of audio quality: Definitions of voice communication faults
Fault | Definition
Low voice level | Level received much lower than the normal level
Echo | Distinct return of transmitted sound during call
Metallic noise | Broken noises similar to metallic sounds
Crackling | Static noises
Micro-outages | Short breaks in sound giving an impression of broken speech
Silence | Fairly lengthy gap
Distorsion | Degradation of other party’s voice without other noise
16

## Slide 17: Protocol for voice QoS measurements
Measurement methodology
A QoS measurement has to be carried out within an area covered by all mobile networks concerned. QoS measurement is not the same thing as coverage measurement.
A voice QoS measurement consists in trying to establish a communication from the mobile testing station to the fixed testing station to verify the reception of the call (no failure) and the continuation of the communication for two minutes (no cutoff), and to assess the audio quality of the established communication.
Each network is tested by a “pair” of testing stations, one mobile and the other fixed.
17

## Slide 18: Protocol for voice QoS measurements
Measurement methodology
Precautions to be taken:
Force terminals on 2G in case of use of dual-mode sets.
Outdoor: Avoid taking measurements under trees.
Indoor: Well inside buildings and up to the 8th floor.
In-car: Use terminals without additional antennas and drive at a speed of less than 80km/h.
Every measurement point must be covered.
18

## Slide 19: Protocol for voice QoS measurements
Measurement methodology
    Sampling and statistical considerations:
  Average duration of a measurement: 7 min
  Average daily measurement time: 8 to 10 hours (e.g. 0900-1300 and 1400 to 2000 hours)
  Daily (per team): 85 measurements x number of operators, i.e. for 3 operators: 255 measurements per day
19

## Slide 20: Protocol for voice QoS measurements
Measurement methodology
    Sampling and statistical considerations:
  Breakdown: by operator, by site (cities, motorways, national highways, railways), by configuration (indoor, outdoor, in-car), by traffic destination (onNet and offNet)
  Large numbers to provide a significant sample (statistical error about 2%): elementary values after any breakdown shall be greater than 33
20

## Slide 21: Protocol for voice QoS measurements
Measurement methodology
    Organization and operation:
  Develop a guide for the investigator with templates to be used: Ref., weather, GPS coordinates, recipient, outcomes,…
  Use the codification principle: operator, site, configuration, traffic,…
21

## Slide 22: Protocol for voice QoS measurements
Measurement methodology
    Organization and operation:
  Guarantee all conditions so that each measurement is conducted under exactly the same conditions for every operator: weather, space, method,…
  Conduct a large number of dry-run tests in order to calibrate the whole testing system
22

## Slide 23: Protocol for voice QoS measurements
Measurement methodology
    Processing of outcomes (deliverables)
  Trend in “positive” indicator: SR
  Trend in “negative” indicator: USR
  = FR+CR
  Reports:
  Overall report: Reference
  Specific report for each operator (request for corrective action plan)
  Report for publication
23

## Slide 24
  Publication of comparative outcomes
Overall success rate (onNet and offNet) by measurement site and by operator |  |  |  | 
Measurement site | MSR | Operator 1 | Operator 2 | Operator 3
All sites | 95.32% | = | = | =
Cities | 96.78% | = | = | =
Motorways | 95.68% | = | - - | +
Major roads | 96.03% | + | = | =
Railways | 87.00% | = | = | =
The mean success rate (MSR) is equal to the average success rates (SR) recorded by each of the three operators: ASR
MSR×0.95
MSRX0.95
MSR×0.98
MSR×0.99
MSR×1.01
MSR×1.02
MSR×1.05
MSR
24

## Slide 25
Measuring the QoS (data) of the mobile Internet

## Slide 26: Basic principles of QoS monitoring
The methodology used for evaluating QoS data for 3G networks (UMTS or CDMA2000 on PCs or smartphones) is perfectly valid for future-generation mobile networks:
4G ( ),
Wifi Outdoor (offloading ),…
Kampala, Uganda, 24 June 2014

## Slide 27: QoS of 3G mobile Internet
QoS measurements - types and conditions:
  3G mobile Internet on PCs: USB dongles (prepaid or postpaid) on computers, for UMTS or CDMA-2000
  3G mobile Internet on smartphones: SIM/3G for subscribers using smartphones/tablets, for UMTS only
  Measurements in FTP or HTTP mode: carried out using files of specific sizes for the purposes of the measurements (upload/download): 1 MB, 5 MB, …
Kampala, Uganda, 24 June 2014

## Slide 28: QoS of 3G mobile Internet
QoS measurements - types and conditions:
  Evaluation of QoS ≠ Evaluation of coverage.
  Measurements are to be taken only in areas declared as being covered by all the operators concerned: exercise involving geographic sampling and coverage mapping.
  The coverage mapping exercise is to be carried out by district, not by town/city.
Kampala, Uganda, 24 June 2014

## Slide 29: QoS of 3G mobile Internet
What are the relevant indicators for each type of measurement?
  Jitter, delay, rate, data losses, …?
  Pragmatic objectives (determined by means of satisfaction surveys) of relevance to the user experience: measurement of accessibility (connection ratio and time), reliability and speed (transmission and reception rates).
  Conversion of these data items into ten indicators:
Kampala, Uganda, 24 June 2014

## Slide 30: QoS of 3G mobile Internet
List of the ten indicators measured:
  Successful connection rate: a connection is successful when it is set up in less than one minute. The successful connection rate is calculated on the basis of all of the measurements taken.
  Successful connection in under ten seconds rate: the successful connection in under ten seconds rate is calculated on the basis of all of the measurements taken.
  The rate for 1 MB files transferred in less than two minutes: a file is considered to have been sent when it has been transmitted in its entirety, and with its content in order, within a period Dmax. The rate is calculated on the basis of the total number of files sent.
  The rate for 5 MB files received in less than five minutes: a file is considered to have been received when it has been downloaded in its entirety and with its content in order. The rate is calculated on the basis of the total number of files downloaded.
Kampala, Uganda, 24 June 2014

## Slide 31: QoS of 3G mobile Internet
List of the ten indicators measured:
  Data rate achieved for 90% of 1 MB files sent: corresponds to the 90th percentile of files sent.
  Data rate achieved for 50% of 1 MB files sent: corresponds to the 50th percentile of files sent.
  Data rate achieved for 10% of 1 MB files sent: corresponds to the 10th percentile of files sent.
Kampala, Uganda, 24 June 2014

## Slide 32: QoS of 3G mobile Internet
List of the ten indicators measured:
  Data rate achieved for 90% of 5 MB files received: corresponds to the 90th percentile of files sent.
  Data rate achieved for 50% of 5 MB files received: corresponds to the 50th percentile of files sent.
  Data rate achieved for 10% of 5 MB files received: corresponds to the 10th percentile of files sent.
Kampala, Uganda, 24 June 2014

## Slide 33: QoS of 3G mobile Internet
Measured indicators:
  Important note:
  The data rate for 3G networks is shared among users. The data rate actually used is always lower than the theoretical data rate (as marketed). This is due to technological constraints.
  However, this data rate is measurable for all operators, using the same mechanism.
Kampala, Uganda, 24 June 2014

## Slide 34: QoS of 3G mobile Internet
Kampala, Uganda, 24 June 2014
Supplementary indicator: Rate of use of contractual data rate, corresponding to the ratio of the data rate actually used (observed) to the contractual rate (marketed) with a given operator. The ratio is expressed as a percentage.
Actual example for a 3G network:
Data rates observed vs. data rates marketed (%) (Rate attained for 50% of files received)
Marrakesh
Fez
National
average
Tangiers

## Slide 35: QoS of 3G mobile Internet
Measurement server platform:
  Measuring the performance of a 3G mobile Internet network means measuring the QoS of a connection, via that network, between a terminal and a data server.
  Various external factors may affect any given test path segment, and this may lead the operator concerned to challenge the measurement results.
  The option of using an international server for measurement must be ruled out.
Kampala, Uganda, 24 June 2014

## Slide 36: QoS of 3G mobile Internet
Measurement server platform:
  Problem: lack of a server (available to hosting providers) at the national level with simultaneous connections to all networks and with a capacity exceeding the highest available data rate!
  Solution: design a measurement server platform to operate within the regulator’s premises, with link capacities exceeding the data rates measured (e.g. 10 Mbps to measure 7.2 Mbps and 20 MBps to measure 14.4 Mbps).
Kampala, Uganda, 24 June 2014

## Slide 37: QoS of 3G mobile Internet
Server platform:
All test files are installed in each platform server, with a fibre-optic connection to the operator’s 3G network.
Kampala, Uganda, 24 June 2014
Test server platforms
(hosted at ANRT HQ)
Test tools
IAM PC server
MdT PC server
WANA PC server
IAM 3G network
(UMTS)
Mdt 3G network
(UMTS)
WANA 3G network
(CDMA2000)

## Slide 38: QoS of 3G mobile Internet
Measurement tools (precautions)
  Terminal equipment (PCs, smartphones and USB dongles) - selection criteria:
    Selection from among the most widely used mass-production models in the domestic market.
    Performance must in all cases accommodate the higher data rates to be measured. For PCs (OS, firewalls, antivirus, etc.) and for terminals (Twindowsize, MTU, CPU, RAM, etc.).
Kampala, Uganda, 24 June 2014

## Slide 39: QoS of 3G mobile Internet
Measurement tools (precautions)
  Subscription types taken into account:
    Postpaid or prepaid.
    Be aware of possible data rate downgrade if total download volume reaches threshold values.
    Tests on smartphones must be done in forced 3G mode rather than dual mode (avoid confusion with GPRS or EDGE).
    For each operator (one server and one link), a single measurement at a time is to be taken.
Kampala, Uganda, 24 June 2014

## Slide 40: QoS of 3G mobile Internet
Measurement tools
  Software application (agents installed in terminals, i.e. PCs and smartphones):
    At each data connection, the application provides feedback to allow automated calculation of all QoS indicators for that connection (field level, SC, failures, successes, etc.), and the GPS location.
    The application allows direct and automatic storage of all results (indicators) on a server which centralizes reporting for the dedicated portal.
Kampala, Uganda, 24 June 2014

## Slide 41: Conclusions and recommendations
Recommendation 1
  Continuous consultations on methodology with operators upstream. Adoption of a standard coordinated follow-up procedure.
Recommendation 2
  Details of measurement sites or periods are not communicated to any operator.
Kampala, Uganda, 24 June 2014

## Slide 42: Conclusions and recommendations
Recommendation 3
  Perform a large number of demonstration QoS measurements using the same tools as those used in real measurement campaigns, preferably in the presence of representatives of the operators concerned (to minimize the likelihood of subsequent challenges by operators).
Kampala, Uganda, 24 June 2014

## Slide 43: Conclusions and recommendations
  Recommendation 4
  Operator action: positive use of results by operators (use of the test server platform; possible operator funding of campaigns).
  Recommendation 5
  Publish (comparative) results, adopt a communication strategy and consider possible sanctions as a last resort in the event of anomalies.
Kampala, Uganda, 24 June 2014

## Slide 44: Conclusions and recommendations
  Recommendation 5 (continued)
  Publication of measurement results:
Initial voice campaign based on a broad sample (30 or so urban centres and populated areas such as airports, tourist centres, etc.)
First quarter.
Second campaign, similar to the first, using more or less the same sample.
Last quarter.
Communicate results to operators
Allow 5 to 6 months for correction of anomalies identified by ANRT
(Publication of results and communication)
Kampala, Uganda, 24 June 2014

## Slide 45: Conclusions and recommendations
  Recommendation 6
  Regulators must prepare themselves well to meet the upcoming challenge of managing the QoS of all-IP networks: NGN, VoLTE,…

## Slide 46
Thank you for your attention.
Questions/Answers
talib@anrt.ma // htalib@ties.itu.int
Kampala, Uganda, 24 June 2014