## Slide 1: ITU Regional Standardization Forum for Africa Livingstone, Zambia 16-18 March 2016
QoS Classes - Mobile vs. Fixed Joachim Pomy
OPTICOM GmbH Germany
consultant@joachimpomy.de

## Slide 2: Outline
Selected communication scenarios
Review of related standards
Applying the standards to the scenarios
Some conclusions

## Slide 3: Selected communication scenarios between terminal with different access
1 Mobile < ---- > Mobile
2 Mobile < ---- > Fixed (> 1.5 Mbit/s)
3 Mobile < ---- > Fixed (< 1.5 Mbit/s)
4 Fixed (> 1.5 Mbit/s) < ---- > Fixed (> 1.5 Mbit/s)
5 Fixed (> 1.5 Mbit/s) < ---- > Fixed (< 1.5 Mbit/s)
6 Fixed (< 1.5 Mbit/s) < ---- > Fixed (< 1.5 Mbit/s)

## Slide 4: Review of related standards
Recommendation ITU-T G.114 Appendix III “Delay variation on unshared access lines”
Recommendation ITU-T Y.1541 “Network performance objectives for IP-based services”
3GPP TS 23107 “Technical Specification Group Services and System Aspects; Quality of Service (QoS) concept and architecture”
IETF RFC 3611 “RTP Control Protocol Extended Reports (RTCP XR)”

## Slide 5: Recommendation ITU-T G.114 Appendix III
Provides introduction on the effect of different IP services on lines with limited bandwidth (e.g., DSL)
Explains the mechanism of serialization delay
Gives an overview over prioritization
Shows how the maximum delay variation due to concurrent traffic can be calculated
Shared lines are excluded.

## Slide 6: Serialization delay

## Slide 7: Example of serialization delays with different line speeds and packet sizes

## Slide 8: Concept of prioritization
In the playout buffer, there is no prioritization. Packets in the playout buffer will be sent to the line in the order they arrived (FIFO, first in, first out).
If the playout buffer is full, not even a packet from the real-time queue can be sent to it. The prioritized packet from the real-time queue has to wait until the packet in the playout buffer is sent to the line.

## Slide 9: Recommendation ITU-T Y.1541
QoS objectives are primarily applicable when access link speeds are at the T1 or E1 rate and higher.
This limitation recognizes that
  IP packet serialization time is included in the definition of IP packet transfer delay (IPTD)
  sub-T1 access rates can produce serialization times of over 100 ms for packets with 1500 octet payloads
Although not explicitly mentioned inY.1541 it is used for fixed networks only

## Slide 10: UNI-to-UNI reference path for network QoS objectives

## Slide 11: QoS classes
Network performance parameter | Nature of network performance objective | QoS Classes |  |  |  |  |  | provisional | 
 |  | Class 0 | Class 1 | Class 2 | Class 3 | Class 4 | Class 5 Unspecified | Class 6 | Class 7
IPTD | Upper bound on the mean IPTD | 100 ms | 400 ms | 100 ms | 400 ms | 1 s | U | 100 ms | 400 ms
IPDV | Upper bound on the 1  10–3 quantile of IPTD minus the minimum IPTD | 50 ms | 50 ms | U | U | U | U | 50 ms | 
IPLR | Upper bound on the packet loss probability | 1 × 10–3 | 1 × 10–3 | 1 × 10–3 | 1 × 10–3 | 1 × 10–3 | U | 1 × 10–5 | 
IPER | Upper bound | 1 × 10–4 (Note 5) |  |  |  |  | U | 1 × 10–6 | 
IPRR | Upper bound |  |  |  |  |  |  | 1 × 10–6 | 

## Slide 12: Applications
QoS class | Applications (examples)
0 | Real-time, jitter sensitive, high interaction (VoIP, VTC)
1 | Real-time, jitter sensitive, interactive (VoIP, VTC).
2 | Transaction data, highly interactive (Signalling)
3 | Transaction data, interactive
4 | Low loss only (short transactions, bulk data, video streaming)
5 | Traditional applications of default IP networks

## Slide 13: Y.1541 is evolving
Classes 0 to 5 are no longer sufficient
  For new applications, e.g. IPTV
  Therefore, classe 6 and 7 have provisionally been defined
  Introducing a new parameter
  IPRR = IP Packet Reordering Ratio

## Slide 14: 3GPP TS 23107
UMTS QoS classes are also referred to as traffic classes
Restrictions and limitations of the air interface have to be taken into account
QoS mechanisms provided in the cellular network have to be robust and capable of providing reasonable QoS resolution. There are four different QoS classes:
  conversational class
  streaming class
  interactive class
  background class
Main distinguishing factor delay sensitivity of traffic

## Slide 15: Conversational class
Typical applications
  telephony speech (e.g. GSM)
  voice over IP
  and video conferencing
Real time conversation is always performed between peers (or groups) of live (human) end-users
Transfer delay requirement of the conversational class
  significantly lower and more stringent compared to interactive traffic case.
Real time conversation - fundamental characteristics for QoS: Preserve
  time relation (variation) between information entities of the stream
  conversational pattern (stringent and low delay)

## Slide 16: Streaming class
Typical applications
  real time audio and video streaming
Real time data flow is always aiming at a live (human) destination
Delay variation of the end-to-end flow shall be limited
Stream normally is time aligned at the receiving end
  highest acceptable delay variation given by the capability of the time alignment function of the application
Acceptable delay variation much greater than in conversational class

## Slide 17: Interactive class
Typical applications
  End-user, that is either a machine or a human, is online requesting data from remote equipment (e.g. a server)
    web browsing
    data base retrieval
    server access
    polling for measurement records
    and automatic data base enquiries
Round trip delay is one of the key attributes.
Another characteristic is that the content of the packets shall be transparently transferred (with low bit error rate)
Interactive traffic - fundamental characteristics for QoS:
  request response pattern
  preserve payload content

## Slide 18: Background class
Typical applications
  End-user, that typically is a computer, sends and receives data-files in the background
    delivery of E-mails or SMS
    download of databases
    reception of measurement records
Background traffic is one of the classical data communication types
  destination is not expecting the data within a certain time
  more or less delivery time insensitive
  content of the packets shall be transparently transferred (with low bit error rate).

## Slide 19: Allocation of classes
In order to have a specific service transported in the appropriate QoS class
  it has to be recognized by the protocol instances to which class it belongs.
Of special importance in cases where new services demand for close to real-time transmission and make use of existing services.
The best example in this context is a financial service which makes use of the SMS service
  Without any additional measures taken, the network does not recognize the financial service but only the SMS service and will transmit it in the background class
  In consequence the financial service is not being provided with the necessary real-time transmission

## Slide 20: IETF RFC 3611
Defines the Extended Report (XR) packet type for the RTP Control Protocol (RTCP)
Defines how the use of XR packets can be signaled by an application if it employs the Session Description Protocol (SDP)
XR packets are composed of report blocks
Purpose of the extended reporting format is to convey information that supplements statistics that are contained RTCP
Some applications, such as voice over IP (VoIP) monitoring, require other and more detailed statistics
Additional block types may be defined in the future

## Slide 21: VoIP Metrics Report Block
The block is encoded as seven 32-bit words:
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| BT=7 | reserved | block length = 8 |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| SSRC of source |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| loss rate | discard rate | burst density | gap density |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| burst duration | gap duration |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| round trip delay | end system delay |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| signal level | noise level | RERL | Gmin |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| R factor | ext. R factor | MOS-LQ | MOS-CQ |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| RX config | reserved | JB nominal |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| JB maximum | JB abs max |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 22: Applying the standards to each scenario
QoS classes are different for mobile and fixed
  No agreed-upon mapping
Bottleneck in in fixed networks
  slow access lines, e.g. DSL

## Slide 23: Mobile < ---- > Mobile
Fully governed by 3GPP TS 23107
Service must be recognized by the system
IETF RFC 3611 not used

## Slide 24: Mobile < ---- > Fixed (> 1.5 Mbit/s)
3GPP TS 23107 applies to mobile part of connection
Rec. ITU-T Y.1541 literally does not apply
  Only one end terminated by a UNI
Mapping of mobile class to fixed class not specified
IETF RFC 3611 not used

## Slide 25: Mobile < ---- > Fixed (< 1.5 Mbit/s)
3GPP TS 23107 applies to mobile part of connection
Rec. ITU-T Y.1541 literally does not apply
  Only one end terminated by a UNI
  Access speed below T1
Mapping of mobile class to fixed class not specified
IETF RFC 3611 not used
QoS degredation due to low access speed as discussed in Rec. ITU-T G.114 Appendix III

## Slide 26: Fixed (> 1.5 Mbit/s) < ---- > Fixed (> 1.5 Mbit/s)
Fully governed by Rec. ITU-T Y.1541
IETF RFC 3611 could be used
  No information available whether it is used

## Slide 27: Fixed (> 1.5 Mbit/s) < ---- > Fixed (< 1.5 Mbit/s)
Rec. ITU-T Y.1541 literally does not apply
  Access speed below T1 at one end
IETF RFC 3611 could be used
  No information available whether it is used
QoS degredation due to low access speed as discussed in Rec. ITU-T G.114 Appendix III

## Slide 28: Fixed (< 1.5 Mbit/s) < ---- > Fixed (< 1.5 Mbit/s)
Rec. ITU-T Y.1541 literally does not apply
  Access speed below T1
IETF RFC 3611 could be used
  No information available whether it is used
QoS degredation due to low access speed as discussed in Rec. ITU-T G.114 Appendix III

## Slide 29: Some conclusions
No single concept for end-to-end QoS for all networks
Mechanism are standardized but
  Implementation depends on network resources
  Allocation of services to classes unspecified in certain cases

## Slide 30: Any questions ?
Contact: Consultant@joachimpomy.de