## Slide 1: STIR
Secure Telephone Identity

## Slide 2: Introduction
Context and drivers
STIR Working Group Charter
Problem Statement
Threats
Status of work
Related work and links

## Slide 3: Context – Past and Present
Calling number used to be considered as trustworthy
  it is marked as such (« network provided » / asserted identity) in the signaling
  it is provided by a third party which is expected to be trustworthy.
Problem: in practice it is less and less reliable
  calling party numbers may be flagged by networks as asserted and trustworthy when the upstream source is not.
  there is nothing in the number or the signaling to demonstrate it is being used by an entity (provider/customer) that has ‘authority’ over that number

## Slide 4: Drivers
Various applications assume a valid calling party number
  calling line number presentation
  Network functions
    Fixed & mobile implicit/partial: voicemail authentication, customer support helpline
    added value service routing, emergency service directory reverse-lookup
    Implicit identification
  User/application-level features
    implicit identification for location based services (landlines).
    implicit authentication: transaction confirmation TEXTs…,
Issues raised with number misappropriation/highjack
  voice mail hacking,
  robotcalling, aggressive telemarketing…
  “vishing”: voice or VoIP phishing
  uncivil practices known as “swatting” (false report of an incident to emergency services)
=> STIR WG

## Slide 5: STIR Charter
From: http://datatracker.ietf.org/wg/stir/charter/
The STIR working group will specify Internet-based mechanisms that allow verification of the calling party's authorization to use a particular telephone number for an incoming call.
Work will produce
  A problem statement detailing the deployment environment and situations that motivate work on secure telephone identity
  A threat model for the secure telephone identity mechanisms
  A privacy analysis of the secure telephone identity mechanisms
  A document describing the SIP in-band mechanism for telephone number-based identities during call setup
  A document describing the credentials required to support telephone number identity authentication

## Slide 6: STIR Problem Statement
From: http://datatracker.ietf.org/doc/draft-ietf-stir-problem-statement/
In the classical public-switched telephone network, a limited number of carriers trusted each other, without any cryptographic validation, to provide accurate caller origination information
VoIP, text messaging, Caller ID spoofing have changed the game

## Slide 7: STIR Problem Statement
Use Cases Considered
  VoIP-to-VoIP Call
  IP-PSTN-IP Call
  PSTN-to-VoIP Call
  VoIP-to-PSTN Call
  PSTN-VoIP-PSTN Call
  PSTN-to-PSTN Call
Limitations of current solutions
  Identity
  Verification Involving PSTN Reachability
  Credential handling

## Slide 8: Threats
From: http://datatracker.ietf.org/doc/draft-ietf-stir-threats/
Impersonation of a calling party number enables
  Robocalling
  Vishing
  Swatting
  Even more…
Attacks
  Voicemail Hacking
  Unsolicited Commercial Calling
  Denial of Service Attacks
The work considers various use cases of how impersonation takes place and the attack vectors

## Slide 9: Status of work
The Problem Statement document has been submitted for Publication as an Information RFC
The Threats document has another round of updates to go before being progressing to the next step toward RFC
General consensus that the signing mechanism will mimic what already exists for email-like SIP URIs john@example.com and adapt it for phone numbers:
  Associate credentials with phone numbers
  Define extensions in SIP to convey a “proof” that the calling ‘party’ (user/network…) has some authority over the number
  Make it possible for the called party (user/network…) to verify this

## Slide 10: Become involved!
IETF
  www.ietf.org
STIR work
  http://datatracker.ietf.org/wg/stir/charter/
  Mailing List
    https://www.ietf.org/mailman/listinfo/stir
Meeting archive from last IETF meeting
  http://www.ietf.org/proceedings/89/stir.html

## Slide 11: Related work and links
STIR Working Group
  http://datatracker.ietf.org/wg/stir/
  Charter and latest documents can be found there
M3AAWG
  http://www.m3aawg.org/
  Voice and Telephony Anti-Abuse Workshop
    http://www.m3aawg.org/vta-sig
  Presentation given at IETF 89 in March 2014
    http://www.ietf.org/proceedings/89/slides/slides-89-stir-2.pdf