## Slide 1: ITU Workshop on “Voice and Video over LTE” Geneva, Switzerland, 1 December 2015
China Mobile VoTLE Status and Further Consideration
Yachen Wang
Senior Manager of Network Technology Dept
China Mobile
wangyachen@chinamobile.com

## Slide 2: Agenda
Why VoLTE?
China Mobile VoLTE status
China Mobile VoLTE further consideration

## Slide 3: Alternative LTE Voice Solutions
TD-LTE Multi-mode
Dual Standby
TD-LTE Multi-mode
Single Standby
LTE support voice& data
LTE support data only
VoLTE/SRVCC
In LTE coverage, provide IMS voice, support SRVCC to provide voice continuity.
CSFB
Terminal prefer LTE residence ，Fallback to 2/3G when using voice service.
TARGET
SOLUTION
LTE
CSFB phone
Multi-mode dual standby
Terminal resident in LTE and CS ，voice service provided by CS and data service provided by LTE.
TRANSITION
SOLUTION
LTE
CS
Voice
TRANSITION
SOLUTION
Data
There are two kinds of LTE terminals: LTE multi-mode dual standby and LTE multi-mode single standby.
Voice service of LTE multi-mode dual standby terminals is provided by CS network.
Voice service of LTE multi-mode single standby terminals is provided by LTE(VoLTE) or CS(CSFB)network.
DS phone
CS
Fallback
①
②
③
④
SGs
LTE
CS
SRVCC
HO
VoLTE phone
VoIP
VoCS
Data
Sv

## Slide 4: VoLTE Overview and Basic Features
FEATURE1：
VoLTE call control & service trigger based on IMS
FEATURE2：
EPC provide Guaranteed QoS for VoLTE
FEATURE3：
Before full coverage, eSRVCC can provide voice call continuity
X2
XN
X2.5
All IP
Low cost
HD voice
& video
Capacity
improved
Service
expansion
↓70%
Call
Setup time
↓50%
VoLTE supports HD voice and Video in the mean time, interworks with CS voice.

## Slide 5: Agenda
Why VoLTE?
China Mobile VoLTE status
China Mobile VoLTE further consideration

## Slide 6: China Mobile at a glance
VoLTE deployment will migrate 820 million CMCC voice service users from CS to IMS.
TD-LTE stations
1 Million+
2G/3GSubscribers
820 million
268 million
4G Subscribers
Roaming Partners
500+
IMS Domains
31

## Slide 7: VoLTE Commercial Launch
China Mobile starts commercial launch from July 2015.
By Sept, Hangzhou and Beijing became the first two commercial cities with 4081 subscribers.
China Mobile is planning to roll out VoLTE in 145 cities by the end of 2015.
Hang
Zhou
Bei Jing
18 more cities
21 more cities
104 more cities
2015.08
2015.09
2015.10
2015.11
2015.12
VoLTE commercial launch plan

## Slide 8: High level functional architecture
VoLTE major functionalities have been developed:
  Network attach, IMS registration, HD voice & video call
  Mobility management, including eSRVCC
  IPv6 supported
  Policy Charging Control…
BOSS
NMS
OMC
BOSS
Application Layer
Core Network
IMS
EPC
PCC
2G/3G
MSC
BTS/BSC
Access
2G
Terminal
VoLTE UE
DRA
HSS
IP bearer
VoLTE AS
eNodeB
LTE
SCP AS
Value added AS

## Slide 9
International Roaming
HD Voice
Intelligent network service
IMS
Emergency call
eSRVCC
Supplementary service
HD Video
Value added service
VoLTE Service
Supported
TBD

## Slide 10: TD-LTE VoLTE Terminals
4 types of TD-LTE commercial terminals are provided for VoLTE by Sep. 2015.
Around 20 types of TD-LTE terminals are proposed for VoLTE launch by the end of 2015.

## Slide 11: Suggestions in VoLTE Deployment
Services Migration
User Experience
Charging Policy
Various Services Exist:
  Supplementary Services
  Value-added Services
  IN Services
No unified Solution for Service Migration
Operators need to carefully develop Service Migration Solution, according to their own service situations
#1 Introduce New Features:
  eSRVCC
  aSRVCC
  bSRVCC
  Mid-call SRVCC
#2 Extend LTE Coverage
Operators need to balance between #1 and #2
Minutes Based Charging vs. Volume Based Charging
More things to think about on VBC
  CDR correlation
  Content charging
  Roaming charging
Operators need to pay more attention to charging policy

## Slide 12: Agenda
Why VoLTE?
China Mobile VoLTE status
China Mobile VoLTE further consideration
  International Roaming
  VoLTE Interoperability
  “VoLTE+” Project

## Slide 13: International Roaming
GSMA’s endorsement of two roaming architectures that can’t interworking with each other is leading to market fragmentation between operators.
The main contradiction is whether access IMS in Visited network or in Home network.
RAVEL: Roaming Architecture for Voice over IMS with Local Breakout
S8HR: S8 Home Routed

## Slide 14: International Roaming Trials
China Mobile drives VoLTE International Roaming Trial in GSMA, and release “VoLTE International Roaming Trial Guidance”.

## Slide 15: VoLTE Interoperability
VoLTE Interoperability issue (UNI & NNI) delayed VoLTE deployment
  Significantly increased support burden and cost for OEMs
  Operators must complete complex integration and IOT test
GSMA launches “VoLTE Interoperability Initiatives”
  VIRTUE: improvement to GSMA Specs
  China Task Force Light House project:
    Lead by China Mobile, along with other China operators and Huawei, ZTE, Qualcomm, MTK etc.
    Define detailed VoLTE UNI profile to eliminate IOT issue
    Conformance test
    Support VoLTE Open Market Device

## Slide 16: China Mobile“VoLTE+” Project
+
: Improvement of user experience
+ new services/features
(multi-party Video call…)
+ new access types
(VoWiFi… )
+ new type of terminals
(WebRTC terminal…)
VoLTE

## Slide 17: 1、VoWiFi (VoLTE Wifi offload)
Core Network and Services
Internet and
Internet Services
User Equipment
WiFi Access Point
2G/3G/LTE
Voice continuity between LTE and Wifi
Better indoor coverage when higher LTE frequency bands are used.
Widely available and supported by UEs/handsets, tablets, laptops.
Lower charging strategy especially when roaming.

## Slide 18: 2、Multi-party video call
EPC
Expansion of VoLTE services
HD multiparty video call compared with OTT
Without installing APP
IMS
AS+
HD Video
Multiparty Video Call

## Slide 19: 3、WebRTC & VoLTE capability exposure
VoLTE
WLAN/3G/LTE
WebRTC terminal
VoLTE terminal
Expansion of telecom capability
New type of terminals access to IMS
New experience for browser users
New mode for service capability exposure
New features introduced from OTT service

## Slide 20: Summary
Collaborations are important on VoLTE international roaming through standardization and tests for its commercial use.
VoLTE UNI profile could advance the fast development of VoLTE gloably.
ITU Standardization on “VoLTE +” would be beneficial for operators to find a way for the next step of network and service evolution.

## Slide 21: Thanks!