## Slide 1: IEEE 1588 revision
Silvana Rodrigues,
Director of System Engineering, IDT
silvana.rodrigues@idt.com
Joint IEEE-SA and ITU Workshop on Ethernet

## Slide 2: Agenda
IEEE 1588 Revision
Project Authorization Request (PAR)
PAR Items
Other Proposals not explicitly stated in the PAR
Architecture

## Slide 3: IEEE 1588 Revision
Study Group to revise IEEE 1588 was formed to come up with a PAR, primarily the Scope
Project Authorization Request (PAR) was sent to IEEE NesCom
Officers
  Kang Lee (NIST), Sponsor, Project Manager
  John Eidson, (UC Berkeley): Co-Chair
  Doug Arnold: Co-Chair
  Hans Weibel (ZHAW), Vice-Chair
  Silvana Rodrigues (IDT): Secretary
  John Mackay (Progeny Systems): Editor

## Slide 4: Scope of the PAR
Several items have been included in the Scope of the PAR
  Correct known technical and editorial errors
  Address Transparent Clock layer violation
  Precision and accuracy improvements
  SNMP-compliant MIB
  Security
  Backwards compatibility with version 2 is a must
Some proposals are not explicitly stated in the Scope of the PAR, as they were covered by other proposals

## Slide 5: Correct known technical and editorial errors
Items dealt at the IEEE 1588 Interpretations Committee will be addressed
  Transparent Clock Source Address will be clarified
  Clarification is needed throughout the standard
    Ex. ClockIdentity, Announce Receipt Timeout, Unicast
  Correction of known errors
Clarification of layering, interfaces and protocol
  It will include clarification of systems that deploy different protocol options

## Slide 6: Precision and Accuracy Improvements
Proposal includes the option to use Synchronous Ethernet for frequency synchronization at the physical layer
Add a clause to clearly describe the steps when a PTP link is being established for high accuracy
  Definitions of dataset fields and TLVs
  High Accuracy state machine
Add a profile for High Accuracy

## Slide 7: SNMP-compliant MIB
The proposal is to create a single IEEE 1588 MIB
IEEE C37.238 (Power profile) and IEEE 802.1AS have defined their own MIB

## Slide 8: Security
MACSec – link (MAC) based has been proposed
Can use same mechanisms as other time transfer protocols (e.g. NTP security mechanism)
Suppress Annex K

## Slide 9: Backwards compatibility
Backwards compatibility with version 2 is a must

## Slide 10: Other Proposals not explicitly stated in the PAR
Several working items have been proposed such as:
  Support of multiple profiles on the same network
  Mapping of IEEE 1588 to 802.11 using 802.11v
  Multiple time sources and multiple time distribution methods
  Mixed mode multicast (sync/Announce) and unicast (delay_req/delay_resp)
  Review IPv6 mapping
  Multilane Ethernet (e.g. 40 and 100 Gigabit)

## Slide 11: Architecture
Michael Teener gave a presentation on PTP Architecture
It highlighted some aspects where different profiles intersect
Good discussion on how to solve this problem
  Needs clarification in IEEE 1588
  Guidelines on the interaction of different profiles

## Slide 12: Architecture cont’d
Agreed to revise the description of the IEEE 1588 architecture and layering of the protocol
  Future modifications become easier
  Reduce duplication between SDOs (ex. IEEE 802.1AS and IEEE 1588)

## Slide 13: Next Steps
PAR was submitted on May 2, approved on June 13
IEEE 1588 Working Group has been formed
First Working Group teleconference call was July 3, 2013
Working Group teleconference calls are scheduled for one hour on Wednesdays, twice a month (1st and 3rd week of each month)
First face-to-face meeting will be in September 27-28 co-located with ISPCS