## Slide 1
SUYAMA Masuo, FUJITSU LTD
Estimates of Required Funding for Green Cable Development Phase

## Slide 2: Objective
International standardization is necessary to provide “the same utility regardless of supplier”.
(Proposal Eng Functional Specs_Phibbs -draft_31 July 2013 to be shared with JTF_vcm1.docx)
To provide “the same utility regardless of supplier”, we would like to propose a verification test for the comparison of observation characteristics among the suppliers.

## Slide 3: Development Phase of Green Cable
Finalization of
Green Repeater Spec.
Modification of Repeater
Verification Tests
Sensor requirements - Water temperature, - 3-axis acceleration, - Pressure
Functional and performance requirements, etc.
Green Cable
Development Phase
Verification Tests - Participation of potential vendors to minimize cost and share external fund. - Continuous observation in a stable atmosphere
such as on the ocean floor. - Comparison of obtained continuous data to
check the utility among the suppliers. - Mechanical deployment check using cable ship (Sea Trial).

## Slide 4: Verification Test
Dummy units
Observation Instruments
Through fibers
Thermometer
Pressure Gauge
3 - Axis accelerometer
Fibers for the instruments
Power feeding conductor
Configuration
- Three sensors are equipped
- Dummy units are to be included instead of repeater units to reduce
cost and fiber pairs.
B
C
D
A
Supplier
A
Supplier
B
Supplier
C
Supplier
D
End Box
Terminals
PWR
PWR
PWR
PWR
PWR

## Slide 5: Testing Configuration Options
Configuration | Test Period | Advantage / Disadvantage
1. Short-haul Observation Cable (e.g., using a retired cable) |  | 
 | Long e.g., 1 year | The most appropriate condition Long stability check available Higher cost
2. Sea Trial (using cable ship) |  | 
 | Short e.g., 1 week | Appropriate condition Mechanical deployment check
3. Using the Cable Tank in Cable Factory or Cable Depot |  | 
 | Long e.g., 1 year | Economical solution It may be hard to keep the stable atmosphere.
4. Using the place with Constant Temperature, such as abandoned mine |  | 
 | Long e.g., 1 year | Economical solution (without cables)
Terminal
Cable Tank
Cable ship

## Slide 6: Rough Order of Magnitude
Items | Condition | Sub-Total
Repeater Modification | 1M x 5? suppliers | USD 5 M
Cables, System Assembly and Test | Total 100 km | USD 3 M
Load & Laying | Depends on the location | USD 3-5 M
Testing including Test Equipment | 5? suppliers | USD 5 M
Contingencies |  | USD 2 M
 | Total | About 20 M$
  ROM for Development Cost with Sea Trial
  External funding is expected.

## Slide 7: Conclusion
  The following conditions shall be specified for more accurate cost estimate.
  Green Repeater Spec. - Sensors - Function and performance
  Development Process - Requirements for the modification - Verification tests; Items, How to perform, etc.
  We have proposed verification test and shown ROM for Green Cable development phase.

## Slide 8
Thank you