## Slide 1
Antoine Lecroart
Alcatel-Lucent Submarine Networks
Green Cable: any idea of how much it would cost?

## Slide 2: Session 8: Business Plan (costs)
Need for estimates on how much a green cable will cost
Two distinct families of costs:
  NRE costs including pilots, qualification…
  Project costs:
    Construction costs
    Maintenance costs

## Slide 3: Session 8: Business Plan (costs)
NRE costs will only be known when:
  functional requirements are known
  extent of qualification is known (including pilot project)
Suppliers may ask for:
  Direct funding:
    NRE is paid (wholly or partly)
  Commitment on Sales:
    Supplier is guaranteed to sell a given amount
    NRE costs are amortized over the guaranteed quantities

## Slide 4: Session 8: Business Plan (costs)
Project costs main assumptions:
  Marine installation and Marine Maintenance costs are not affected by sensors:
    Sensors do not affect sensibly repeater reliability
    Repeaters with faulty sensors are not replaced
Project maintenance costs are similar to non Green Cables over the 25 year design life

## Slide 5: Session 8: Business Plan (costs)
Construction costs will slightly increase:
  Depending on requirements and associated solution complexity the additional costs could reach between 5% and 10 % of a transoceanic system (see slides below)
  With sensors in every repeater
  Without NRE amortization
  Based on industry rules of thumb

## Slide 6: Session 8: Business Plan (costs)
Main assumptions:
  Standard scope
    Existing cable landing stations (CLS)
    Existing terrestrial links (ducts) between CLS and BMH
    Direct point to point link about 5000 km
    2 telecom fiber pairs (no extra fiber required for sensors)
    State of the art capacity capabilities
    Standard initial equipage

## Slide 7: Session 8: Business Plan (costs)
5000 km, 2 fp Cable | Wet Plant (1/3) |  | Marine Installation (1/3) | Terminal Equipment, Other services (1/3) | Total
Standard Scope |  |  |  |  | 
Non Green | Cable (6/10) | Repeaters (4/10) |  |  | 
 | 20 | 13,3 | 33,4 | 33,3 | 100
Green High End | Same | +40% | Same | +10% | 
 | 20 | 18,62 | 33,4 | 36,63 | 108,65
Green Low End | Same | +20% | Same | +5% | 
 | 20 | 15,96 | 33,4 | 34,97 | 104,33

## Slide 8: Session 8: Business Plan (costs)
Discussion:
  Are cable owners ready to cope with this price increase?
  Will the Scientists contribute?
  Will the cable owners get benefits out of it?
    Tax exemptions, tax reductions…
    What could be the incentives beyond the “environmental friendly” image?

## Slide 9
Thank you