## Slide 1: ITU Workshop on “Quality of Service and Quality of Experience of Multimedia Services in Emerging Networks” (Istanbul, Turkey, 9-11 February 2015)
Mobile QoS Framework: Counters, KPI, KQI
Joachim Pomy,
Senior Engineer, Opticom GmbH Germany
Consultant@joachimpomy.de
Notes: 1

## Slide 2
Mobile QoS Framework: Counters, KPI, KQI
  Recent ITU-T work on Mobile QoS
  Layered Approach – Selection of Mobile QoS Parameters perceived by the User
  Test Scenarios and Trigger Points
  Voice Quality Assessment – Drive Testing
  Statistics – Presentation of Results
  Counters, KPI, KQI
ITRs: Setting the stage for a connected world
[Agenda]
Notes: 2

## Slide 3: ITU-T work on Mobile QoS
Mobile KPIs
  centric to equipment / infrastructure
  aggregation of proprietary network counters
  not standardized
Recent work in ITU-T on Mobile QoS
  Draft new Recommendation E.MQoS
    QoS Aspects for Popular Services in Mobile Networks
  Draft new Supplement to E.800 series of Recommendations
    Guidelines on Regulatory Aspects of QoS
Other ITU-T Recommendations on QoS cover
  Aspects of Terminal requirements
  Aspects of end-to-end quality
  Aspects of user perceptions

## Slide 4
Mobile QoS Framework: Counters, KPI, KQI
  New ITU-T work on Mobile QoS
  Layered Approach – Selection of Mobile QoS Parameters perceived by the User
  Test Scenarios and Trigger Points
  Voice Quality Assessment – Drive Testing
  Statistics – Presentation of Results
  Counters, KPI, KQI
ITRs: Setting the stage for a connected world
[Agenda]
Notes: 4

## Slide 5: QoS Layers in Mobile
QoS model for mobile has four layers.
First layer is the Network Availability
  defines QoS rather from the viewpoint of the service provider than the service user
Second layer is the Network Access
  from user's point of view basic requirement for all the other QoS aspects and parameters
Third layer contains other QoS aspects
  Service Access, Service Integrity & Service Retainability
Different services are located in the fourth layer
  Their outcome are the QoS parameters as perceived by the user

## Slide 6: QoS aspects of Mobile

## Slide 7: Layered Mobile QoS (1)
If we follow the layered approach
  focussing on events that can be perceived by the user
  focussing on most relevant services in the market
    Telephony
    SMS
    MMS
    Video Telephony
    Video Streaming
    Web Browsing

## Slide 8: Layered Mobile QoS (2)
Layer 1
Radio Network Unavailability [%]
Layer 2
Network Selection and Registration Failure Ratio [%]

## Slide 9: Layered Mobile QoS (3)
Telephony Layer 3
  Telephony Service Non‑Accessibility [%]
Telephony Layer 4
  Telephony Setup Time [s]
  Telephony Cut‑off Call Ratio [%]

## Slide 10: Layered Mobile QoS (4)
SMS Layer 3
  SMS Service Non‑Accessibility [%]
SMS Layer 4
  SMS End‑to‑End Delivery Time [s]
  SMS Completion Failure Ratio [%]

## Slide 11: Layered Mobile QoS (5)
MMS Layer 3
  MMS Send Failure Ratio [%]
MMS Layer 4
  End‑to‑End Delivery Time [s]
  MMS End‑to‑End Failure Ratio [%]

## Slide 12: Layered Mobile QoS (6)
Video Telephony Layer 3
  VT Service Non‑Accessibility [%]
Video Telephony Layer 4
  VT Audio/Video Setup Time [s]
  VT Cut‑off Call Ratio [%]

## Slide 13: Layered Mobile QoS (7)
Streaming Video Layer 3
  Streaming Service Non‑Accessibility [%]
Layer 4:
  Streaming Service Access Time [s]
  Streaming Reproduction Cut-off Ratio [%]

## Slide 14: Layered Mobile QoS (8)
Web Browsing (HTTP) Layer 3
  HTTP Service Non‑Accessibility [%]
Web Browsing (HTTP) Layer 4
  HTTP Setup Time [s]
  HTTP Session Failure Ratio [%]
  HTTP Data Transfer Cut‑off Ratio [%]

## Slide 15: Layered Mobile QoS (9)
This approach would make us end up with > 20 QoS parameter
  All relate to user perceptional events
  But this is just end-to-end parameters
  Many more parameters defined for events related to network segments, hand-over etc.

## Slide 16
Mobile QoS Framework: Counters, KPI, KQI
  New ITU-T work on Mobile QoS
  Layered Approach – Selection of Mobile QoS Parameters perceived by the User
  Test Scenarios and Trigger Points
  Voice Quality Assessment – Drive Testing
  Statistics – Presentation of Results
  Counters, KPI, KQI
ITRs: Setting the stage for a connected world
[Agenda]
Notes: 16

## Slide 17: Test Scenarios
Test scenarios need to distinguish the following principal user cases
  User-to-user services (typically telephony)
  Store-and-forward services (e.g. SMS)
  Information services (e.g. accessing the internet or FTP download)
  Push services (sender initiated transfer)

## Slide 18: Considerations on trigger points
It can be assumed that
  any feasible test equipment will contain some kind of communication terminal (UE) which may be a special type (e.g. a Trace Phone)
  or a standard UE
Also, it can be assumed that each such device will provide information from different communication layers
  from Application Layer (close to the user interface)
  down to lower layers, e.g. operating-system events, TCP/IP layer, or Layer 3 signalling information, which is used as trigger points for QOS PARAMETERS processing
  Typically AT commands can be used in majority of cases
Action is typically triggered
  by some emulated user action
  causing some action on the air interface

## Slide 19: Considerations on trigger points
Process of event propagation is deterministic
  allowing for kind of mapping between layers
  associated with communication and processing delay in each stage.
Choice of the layer for trigger point information retrieval
  determines the view expressed in a QOS PARAMETER
  choosing lower-level events ( Layer 3) gives more network-centric view
  events on higher levels to produce views more user-related
  for same QoS PARAMETER source layer for events used as trigger points should be the same
In benchmarking, for all all networks under test
  use same type of UE, and QOS PARAMETERS
  use trigger points from the same layer.
Changing the source layer for a given trigger point
  changes in QOS PARAMETERS should be expected
  calibration measurements required
    to assess influence on QOS PARAMETERS both quantitatively and qualitatively.

## Slide 20
Mobile QoS Framework: Counters, KPI, KQI
  New ITU-T work on Mobile QoS
  Layered Approach – Selection of Mobile QoS Parameters perceived by the User
  Test Scenarios and Trigger Points
  Voice Quality Assessment – Drive Testing
  Statistics – Presentation of Results
  Counters, KPI, KQI
ITRs: Setting the stage for a connected world
[Agenda]
Notes: 20

## Slide 21: Telephony Measurements in the Network (1)
Transaction definition and transaction types
  The basic transaction for telephony testing is equivalent to a single call to a counterpart extension. It is assumed that the call partner is typically a fixed-network type extension to avoid uncertainties related to a second mobile connection.
  Type is either Mobile Originated (MO) or Mobile Terminated (MT).
  It is assumed that once a connection has been established, for further measurements it does not matter which side has triggered it. Therefore, the audio data flow parameter will not be logically linked to the call type.

## Slide 22: Telephony Measurements in the Network (2)
Content quality
  Content quality assessment data generated at receiving end
  For downlink content data storage is straightforward
  For uplink content, at some point in time results have to be integrated
  For assessing content quality of complete transmitted speech samples, at least the following methods are possible:

## Slide 23: Telephony Measurements in the Network (3)
Content quality (ctd.)
  Real-time assessment
    streaming mode
    speech quality assessment algorithm determines MOS-LQO real time
  Offline assessment
    content first recorded
    being processed later
  Data processing must ensure that only valid content quality data is processed
    inside the "connection active" time window

## Slide 24: Telephony Measurements in the Network (4)
Verification of usable two-way connection
Only calls with a valid two-way end-to-end information connection shall be considered for content quality assessment (valid calls).
Non-valid calls treated like dropped calls
  with indicator for this particular cause

## Slide 25: Hot Topic: POLQA™ - Rec. P.863 (1)

## Slide 26: POLQA™ - Rec. P.863 (2)
New POLQA standard winner of rigorous technical competition
  Carried out by ITU-T to define technology update for PESQ/P.862
  PESQ was state-of-the-art in almost any telecom service globally
  POLQA - “Perceptual Objective Listening Quality Assessment” - offers new level of benchmarking capability
    to determine the voice quality of mobile network services

## Slide 27: POLQA™ - Rec. P.863 (5)
The limitations of existing standards that are now addressed by POLQA
  CDMA
  Chinese 3G TD-SCDMA
POLQA will also offer immediate, strong support for testing of new wideband 4G/LTE networks delivering HD-quality voice services
Tests carried out during the POLQA evaluation included future technologies such as
  Unified Communications
  Next Gen Networks
  4G/LTE
  HD Voice, i.e. "wide-band" and "super-wide-band"
See POLQA: The Next Generation in Voice Quality Testing http://www.polqa.info

## Slide 28
Notes: 28

## Slide 29
POLQA Introduction - (c) OPTICOM GmbH 2010
29
Performance Validation
The ITU has validated POLQA on:
Languages included in the POLQA validation:
  German
  Swiss German
  Italian,
  Japanese,
  Swedish
  American English and British English
  Chinese (Mandarin),
  Czech,
  Dutch,
  French,
  47000 file pairs across
  64 subjective experiments
Notes: TNO Meeting, Delft, 01.09.2005
(c) OPTICOM 2005 - C O N F I D E N T I A L
29

## Slide 30
Mobile QoS Framework: Counters, KPI, KQI
  New ITU-T work on Mobile QoS
  Layered Approach – Selection of Mobile QoS Parameters perceived by the User
  Test Scenarios and Trigger Points
  Voice Quality Assessment – Drive Testing
  Statistics – Presentation of Results
  Counters, KPI, KQI
ITRs: Setting the stage for a connected world
[Agenda]
Notes: 30

## Slide 31: Confidence Intervalls for Different Sample Sizes (1)
Effect of different sample sizes in a measurement campaign
  based on the Pearson-Clopper formulas for calculation of confidence intervals
  valid in a generic way and even for small sample sizes
  for higher sample numbers, the calculation of confidence intervals based on the approximation of a normal distribution can be applied
  Three different graphs are depicted: Sample sizes in the range:
    between 100 and 1 100 samples;
    between 1 100 and 2 100 samples; and
    between 1 000 and 11 000 samples.

## Slide 32: Confidence Intervalls for Different Sample Sizes (2)

## Slide 33: Confidence Intervalls for Different Sample Sizes (3)

## Slide 34: Confidence Intervalls for Different Sample Sizes (4)

## Slide 35: Reporting of results (1)
Which pieces of information should be given to the reader when generating a test report ?
  When quantile values are used, it should be kept in mind that the computation of quantiles separates a low percentage of outlier data from the remaining data. This means:
    If lower values represent a better outcome from the customer's perspective, a small percentage containing the highest values could be separated by calculating a 95 %-quantile or a 90 %-quantile. This is the case for example for duration values.

## Slide 36: Reporting of results (2)
    If higher values represent a better outcome from the customer's perspective, a small percentage containing the lowest values could be separated by calculating a 5 %-quantile or a 10 %-quantile. This is the case for example for throughput values.
    Related to content quality, the appropriate quantile computation orientates itself on the scale of the determined test results. In practice, some algorithms define a value of 0 on a scale from 0 to 5 as the best quality whereas others define the value of 5 as the highest possible quality

## Slide 37
Mobile QoS Framework: Counters, KPI, KQI
  New ITU-T work on Mobile QoS
  Layered Approach – Selection of Mobile QoS Parameters perceived by the User
  Test Scenarios and Trigger Points
  Voice Quality Assessment – Drive Testing
  Statistics – Presentation of Results
  Counters, KPI, KQI
ITRs: Setting the stage for a connected world
[Agenda]
Notes: 37

## Slide 38: KPIs based on Network Counters
Vendor specific = network internal KPIs
  different strategies
    how to count network events
    which events are included in which counter(s)
Requires knowledge of specific system
  specialists with detailed system knowledge
  testing the counters
    documentation may be faulty
    approach to counter change with system update
Mobile operators struggling with this
  most operator live in a multi vendor environment
  counters from different vendors cannot be directly compared
  requires continous attention and a strategy

## Slide 39: KPIs from Users' Perspective = KQIs
Key Quality Indicators (KQIs) = external indicators
  can be assessed in the Field
For Monitoring, Regulation etc.
  a subset can be selected
    applicable across all vendors & operators
    not limited to mobile, but also good for broadband

## Slide 40: KPIs versus KQIs
Sometimes confused
  KPIs = internal indicators
    part of network performance
    based on network counters
    essential for operation, maintenance, business model
    could be reported, audited etc.
    however, meaningless when out of context
  KQIs = external indicators
    basis for QoS assessment as perceived by the user
    vendor independant
    operator independant
    ideal to compare different operators on a statistical basis
    cannot be reported from the system itself
    requires some kind of field testing, drive, walk etc.

## Slide 41: Any questions ?
Contact: Consultant@joachimpomy.de