## Slide 1: Regulatory framework for QoS and QoE: the case of ARGENTINA
Guillermo Montenegro Engineering Manager Comisión Nacional de Comunicaciones gmontenegro@cnc.gov.ar
ITU Workshop on “Monitoring and Benchmarking of QoS and QoE of Multimedia Services in Mobile Networks”
(Buenos Aires, Argentina, 24-25 July 2014)

## Slide 2: ITU-T RECOMMENDATION E.800
QoS comprises both network performance and non-network related performance.
QUALITY OF SERVICE
NETWORK PERFORMANCE
NON-NETWORK PERFORMANCE

## Slide 3: ITU-T RECOMMENDATION G.1000
CUSTOMER
CUSTOMER’S QoS
REQUIREMENTS
PROVIDER
QoS OFFERED BY
PROVIDER
QoS ACHIEVED BY
PROVIDER
QoS
PERCEIVED BY
CUSTOMER

## Slide 4: REGULATORY FRAMEWORK FOR THE PROVISION OF TELECOMMUNICATION SERVICES
ENABLING LICENCE FOR THE PROVISION OF ALL TYPES OF TELECOMMUNICATION SERVICE
PROVISION OF SERVICES WITH OR WITHOUT OWN INFRASTRUCTURE
FREE NETWORK ARCHITECTURE AND TECHNOLOGY
REGULATIONS FOR LICENSING OF TELECOMMUNICATION SERVICES
(Annex I to Decree 764/2000)

## Slide 5: FRAMEWORK THAT EXISTED BEFORE THE NEW QoS REGULATIONS
QUALITY REGULATIONS DIFFERENTIATED BY SERVICE
INDICATORS RELATING TO NETWORK PERFORMANCE
INDICATORS OBTAINED FROM FORCED PROVING
SCOPE OF APPLICATION COINCIDES WITH OPERATONAL AREA

## Slide 6: FRAMEWORK THAT EXISTED BEFORE THE NEW QoS REGULATIONS
QUALITY INDICATORS FOR MOBILE SERVICES
SERVICE ACCESSIBILITY (voice)
SERVICE RETAINABILITY (voice) – CUT-OFF RATE
POST-DIALLING DELAY (voice)

## Slide 7: ITU-T RECOMMENDATION G.1000
QoS
CUSTOMER
PROVIDER
CUSTOMER’S QoS
REQUIREMENTS
QoS OFFERED BY
PROVIDER
QoS ACHIEVED BY
PROVIDER
QoS
PERCEIVED BY
CUSTOMER

## Slide 8: CONSIDERATIONS TO BE INCORPORATED IN THE QoS REGULATONS
INCLUSION OF ALL TELECOMMUNICATION SERVICES INTENDED FOR USE BY THE GENERAL PUBLIC
ADJUSTMENT OF AREAS OF INDICATOR COMPLIANCE (ACCURACY)
ADJUSTMENT OF PERIODICITY OF MEASUREMENTS (ACCURACY)
MEASUREMENTS OBTAINED ON NETWORK ELEMENTS (HIGHER LEVEL OF DATA-GATHERING)
MEASUREMENTS BY PROVIDERS
PUBLICATION OF RESULTS OBTAINED
ADDITIONAL MEASUREMENTS (BY THE MONITORING AUTHORITY)

## Slide 9: CONSIDERATIONS INCORPORATED IN THE QoS REGULATIONS
PREVIOUS REGULATORY
FRAMEWORK
FIXED AND MOBILE
NETWORKS
CIRCUIT AND PACKET
SWITCHING
INTERNET
VIDEO
CONFERENCING
TxDat, etc.
TELEPHONY
PROPOSED
NEW FRAMEWORK

## Slide 10: OVERALL STRUCTURE
DEFINITIONS
INDICATORS
SANCTIONS
AUDIT AND
MONITORING
REGULATIONS

## Slide 11
INDICATORS AND PRESENTATION
INDICATORS
RELATING TO CUSTOMER
SATISFACTION
RELATING TO NETWORK
OPERABILITY
PRESENTATION
MEASUREMENTS UNDERTAKEN BY
THE PROVIDER
PERIODIC PRESENTATION VIA
THE WEB PORTAL

## Slide 12: CUSTOMER SATISFACTION INDICATORS
INDICATORS
  Customer complaints to provider
  Repeated complaints to provider
  Complaints to the enforcement authority
  Operator’s response to customer
  Complaints concerning prepaid account balances
  Complaints concerning invoicing
  Delay in requested service becoming operational

## Slide 13: NETWORK OPERABILITY INDICATORS
INDICATORS
  Nominal reuse factor
  Service accessibility/resource allocation rate
  Service retainability/cut-off rate
  Transmission time compliance rate
  Packet-loss rate
  Maximum fluctuation compliance rate
  Synchronism compliance rate
  Effective mean transfer velocity compliance rate

## Slide 14: QoS OFFERED BY THE PROVIDER
REQUIREMENT TO PRESENT, ON A MONTHLY BASIS, PLANS, PRICES, COMMERCIAL CONDITIONS AND SERVICE PROMOTIONS.
REQUIREMENT TO PRESENT THE SERVICE COVERAGE AREA TO CUSTOMERS AND THE REGULATORY BODY.
REQUIREMENT TO HAVE CUSTOMER CENTRES IN ALL AREAS WHERE THE SERVICE IS OFFERED.
REQUIREMENT TO HAVE LINES FOR COMPLAINTS AND ENQUIRIES WHICH MUST OPERATE 365 DAYS A YEAR.
ADHERENCE TO MAXIMUM TIME-LIMIT FOR RESPONDING TO CALLS.

## Slide 15: ITU-T RECOMMENDATION G.1000
QoE
CUSTOMER
PROVIDER
CUSTOMER’S QoS
REQUIREMENTS
QoS OFFERED BY
THE PROVIDER
QoS ACHIEVED BY
THE PROVIDER
QoS
PERCEIVED BY
THE CUSTOMER

## Slide 16: QUALITY OF EXPERIENCE (QoE)
SURVEYS
BASIC TELEPHONY SERVICE
(FIXED TELEPHONY)
MOBILE TELEPHONY
INTERNET

## Slide 17: QUALITY OF EXPERIENCE (QoE) SURVEYS
METODOLOGÍA
QUANTITATIVE, BASED ON SATISFACTION AND EXPECTATION SURVEYS, WITH GENERATION OF SATISFACTION INDICATORS FOR EACH SERVICE REVIEWED.
CONDUCTED ON THE BASIS OF SEMI-STRUCTURED QUESTIONNAIRES CONDUCTED IN THE HOME OR BY TELEPHONE.
THE SAMPLE DESIGN INCLUDES SPECIFIC FEATURES IN EACH SURVEY, BUT PROBABILISTIC SAMPLES ARE DESIGNED IN ALL CASES.

## Slide 18: QUALITY OF EXPERIENCE (QoE) PERCEIVED QUALITY OF VOICE, SMS AND DATA SERVICES
METODOLOGÍA
VOICE Coverage Frequency of successful call setup Clarity of communication during call Call continuity
SMS Messages delivered in a timely manner Messages delivered to recipient
DATA Availability of connection Connection continuity Availability of speed specified in contract

## Slide 19: QUALITY OF EXPERIENCE (QoE) PERCEIVED QUALITY OF VOICE, SMS AND DATA SERVICES
METODOLOGÍA
CUSTOMER CARE Clarity of information provided Time waiting to be served Friendliness and politeness of the agent Technical and professional capacity of the staff
PLANS AND PROMOTIONS ON OFFER Number of plans and promotions available Clarity of information regarding plans and promotions Proper fulfilment of plans and promotions on offer Options for cancelling a plan or promotion
BILLING AND FACILITIES FOR TOPPING UP CREDIT Variety of available facilities for topping up credit (prepaid and mixed segment) Clarity and reliability of the information contained in the invoice (postpaid segment)
RELATIONSHIP BETWEEN PRICING AND QoS RECEIVED

## Slide 20: QUALITY OF SERVICE REGULATORY FRAMEWORK
THANK YOU!
GUILLERMO MONTENEGRO (gmontenegro@cnc.gob.ar)
ENGINEERING MANAGER
COMISIÓN NACIONAL DE COMUNICACIONES
Perú 103 5º piso - Ciudad Autónoma de Buenos Aires – República Argentina

## Slide 21: INDICATORS RELATING TO CUSTOMER SATISFACTION
INDICADORES
Customer complaints indicator (CCI)
This is the ratio between the total number of complaints addressed by customers to the provider within a given period (GP) – irrespective of the means used to do so, resulting solution and/or reasonableness thereof – and the total number of access events recorded up to the final day of the given period.

## Slide 22: INDICATORS RELATING TO CUSTOMER SATISFACTION
INDICADORES
Repeated complaints indicator (RCI)
This is the ratio between the number of users having addressed more than one complaint to the provider within the given period – irrespective of the means used to do so or resulting solution (favourable or otherwise) – and the total number of users having addressed complaints to the provider during that same period.
where:
CustomersRCP: Customers having addressed more than one complaint to the providers
CustomersCP: Customers having addressed complaints to the provider
GP: Given period

## Slide 23: INDICATORS RELATING TO CUSTOMER SATISFACTION
INDICADORES
Indicator for complaints to the enforcing authority (ICEA)
This is the ratio between the number of customers having addressed complaints to the enforcing authority in respect of a specific provider, within the given period – irrespective of the means used to do so or resulting solution (favourable or otherwise) – and the total number of users having addressed complaints to the provider in question during the period immediately preceding the given period.
where:
CustomersCompEA: Customers having addressed complaints to the enforcing authority
CustomersCompP: Customers having addressed complaints to the provider
GP: Given period
PGP: Period immediately preceding the given period

## Slide 24: INDICATORS RELATING TO CUSTOMER SATISFACTION
Indicator for operator customer care response (IOCCR)
This is the ratio between the number of calls responded to by a human operator within THIRTY (30) seconds of being initiated by the caller, and the total number of calls made to the customer care number.
where:
N: Number of days in the month
CSA: Number of requests for assistance answered within 30 seconds each day
CS: Total number of requests for assistance per day

## Slide 25: INDICATORS RELATING TO CUSTOMER SATISFACTION
INDICADORES
Indicator for complaints relating to prepaid account balances (ICPAB)
This is the ratio between the total number of complaints relating to prepaid account balances – irrespective of the means used to communicate those complaints or resulting solution (favourable or otherwise) – and the total number of accesses effected in prepaid mode.
where:
ComPAB : Complaints relating to prepaid account balances
AccCustPM: Accesses by customers with prepaid mode
GP: Given period

## Slide 26: INDICATORS RELATING TO CUSTOMER SATISFACTION
INDICADORES
Indicator for complaints relating to billing (ICB)
This is the ratio between the total number of complaints relating to billing – irrespective of the means used to communicate those complaints, the date on which bills were issued or the resulting solution (favourable or otherwise) – and the total number of bills issued during the period in question.
where:
N: Number of days in the month
ComB : Complaints relating to bills
BillsIss: Bills issued
GP: Given period

## Slide 27: INDICATORS RELATING TO CUSTOMER SATISFACTION
INDICADORES
Indicator relating to delay in the requested service becoming operational (IDRSO)
Defined as the delay between the time at which a service is requested by a customer and the time at which that service actually becomes accessible.
To obtain the indicator, we must register the number of requests met within the maximum installation time (MIT) and number of requests received within the given period.
where:
MIT: Maximum installation time
GP: Given period: time-frame within which measurements are conducted
IDRSO: Percentage of requests met within the MIT

## Slide 28: NETWORK OPERABILITY INDICATORS
Buenos Aires, Argentina, 24-25 July 2014
28
INDICADORES
Service accessibility indicator
This indicator is obtained from the resource allocation rate (RAR), which is defined as the percentage ratio of successful allocations of resources required for a given call to the total number of attempted allocations. Measurements need to be taken on a daily basis and at the time of peak traffic.
The indicator is obtained from the monthly sum of daily values using the following formula:
MOBILE ACCESS NETWORKS
FIXED ACCESS NETWORKS
  where:
  N: Number of days in the month
  CAED: Number of daily successful resource allocations
  CAD: Number of daily resource allocation attempts
  RAR: Resource allocation rate
Notes: 28

## Slide 29: NETWORK OPERABILITY INDICATORS
INDICADORES
Service retainability (SR) indicator
This indicator is obtained from the cut-off rate (CR), defined as the number of established calls that are released for a reason other than intentional by any of the parties involved in the call as a percentage of the total quantity of resources allocated for traffic management purposes. This is measured daily at the time of peak traffic.
The indicator is obtained from the monthly sum of daily values using the following formula:
MOBILE ACCESS NETWORKS
FIXED ACCESS NETWORKS
  where:
  N: Number of days in the month
  CDRLI: Daily number of resources released involuntarily
  CDRA: Daily number of assigned resources
  CR: Cut-off rate

## Slide 30: NETWORK OPERABILITY INDICATORS (PARAMETERS RELATING TO TYPE OF INFORMATION)
INDICADORES
Transmission time compliance rate (TTCR)
Defined as the percentage ratio between the number of packets received within period of time T1 and the total number of packets received. Measurements need to be taken on a daily basis and at the time of peak traffic.
The indicator is obtained from the monthly sum of daily values using the following formula:
Type of information | Time (T1) [mS] | X [%]
Bidirectional audio (voice) | 400 | 98
Audio (music) | 10 000 | 99.5
Bidirectional video | 400 | 99.5
Unidirectional video | 10 000 | 99.5
Data | 10 000 | 95
  where:
  D: Number of days in the month
  NPREC: Number of packets received in time (t ≤ T1)
  NTPR: Total number of packets received
  TTCR: Transmission time compliance rate

## Slide 31: NETWORK OPERABILITY INDICATORS (PARAMETERS RELATING TO TYPE OF INFORMATION)
INDICADORES
Packet-loss rate (PLR)
Defined as the percentage ratio between the number of packets lost and total number of packets received. Measurements need to be taken on a daily basis and at the time of peak traffic.
The indicator is obtained from the monthly sum of daily values using the following formula:
Type of information | X [%]
Bidirectional audio (voice) | 3
Audio (music) | 1
Bidirectional video | 1
Unidirectional video | 1
Data | 1
  where:
  D: Number of days in the month
  NPL: Number of packets lost
  NTPT: Total number of packets transmitted
  PLR: Packet-loss rate

## Slide 32: NETWORK OPERABILITY INDICATORS (PARAMETERS RELATING TO TYPE OF INFORMATION)
INDICADORES
Maximum fluctuation compliance rate (MFCR)
Defined as the percentage ratio between the number of packets received with maximum fluctuation ΔT1 and total number of packets received. Measurements need to be taken on a daily basis and at the time of peak traffic.
The indicator is obtained from the monthly sum of daily values using the following formula:
Type of information | Time (ΔT1) [mS] | X [%]
Bidirectional audio (voice) | 1 | 98
Audio (music) | 1 | 99.7
  where:
  D: Number of days in the month
  NPRFM: Number of packets received with fluctuation ≤ Δ T1
  NTPR: Total number of packets received
  MFCR: Maximum fluctuation compliance rate

## Slide 33: NETWORK OPERABILITY INDICATORS (PARAMETERS RELATING TO TYPE OF INFORMATION)
INDICADORES
Synchronism compliance rate (SCR)
Defined as the percentage ratio between the number of packets received with maximum lip/voice synchronism ΔT1 and total number of packets received. Measurements need to be taken on a daily basis and at the time of peak traffic.
The indicator is obtained from the monthly sum of daily values using the following formula:
Type of information | Time (ΔT1) [mS] | X [%]
Bidirectional video | 80 | 95
Unidirectional video | 80 | 95
  where:
  D: Number of days in the month
  NPRS: Number of packets received with synchronization ≤ Δ T1
  NTPR: Total number of packets received
  SCR: Synchronism compliance rate

## Slide 34: NETWORK OPERABILITY INDICATORS
INDICADORES
Effective mean transfer speed compliance rate (EMTSCR)
Defined as the percentage ratio between the effective mean transfer speed and the nominal transfer speed. This will be measured between customers and the provider’s upper-hierarchy interconnection link. Measurements need to be taken on a daily basis and at the time of peak traffic.
The indicator is obtained from the monthly sum of daily values using the following formula:
  where:
  D: Number of days in the month
  SEMT: Effective mean transfer speed
  SNT: Nominal transfer speed
  EMTSCR: Effective mean transfer speed compliance rate