## Slide 1
The 5G Wireline Challenge
March 2016
Peter Ashwood-Smith
Chair – FG IMT-2020 Wireline

## Slide 2: Agenda
Some wireless 4G basics
5G goals
What is 5G slicing
Potential 5G architecture incorporating multiple cloud concepts
Challenges and futures/ITU-T FG

## Slide 3: Some current wireless basics – Antenna Site
Different bands =>
Different Antennas
Different Service providers =>
Different Antennas
Analog (or digitally encoded
Analog) signals runs up the mast.
Cooled/Heated enclosure at base of mast for equipment
driving antennas.
))))
))))
))))
Front Haul
CPRI
Back Haul IP - Packet
IP network delivers packets to / from antenna site.
Devices at base of the mast process packets and generate analog signals to antennas.
(I)FFT
AT&T
VZ

## Slide 4: Some current wireless basics – Packet Processing(Core)
IP
))))
eNODEb
Core network is responsible for packet processing and consists of multiple different functions that inter-communicate over IP tunnels over the IP backhaul.
Functions are often run in different dedicated hardware!
Functions are often aware of the radio access interfaces, tightly coupled.
NFV was basically created to consolidate these core functions and lower costs.
Fronthaul
MOBILITY MGMT ENTITY
MME
HOME SUBSCRIBER SERVER HSS
SERVING GW
PDN GW
DATA
CTRL
IP Multimedia Core Sys
Internet

## Slide 5: A few areas for improvement
))))
))))
Fronthaul
01
02
01
03
More flexible antennas
Lower bandwidth, longer reach fronthaul reduced energy/cooling costs
Centralized ‘numerology’ / programmable
02
03
04
No more custom hardware
Flexible allocations of functions, OPEX reductions
Lower ‘stress’ mobility
05
06
07
IP
eNODEb
MOBILITY MGMT ENTITY
MME
HOME SUBSCRIBER SERVER HSS
SERVING GW
PDN GW
DATA
CTRL
SECURITY
04
05
06
07
Internet
IP Multimedia Core Sys

## Slide 6: Cloud can help with many of these issues
NFV was primarily created to address 4G cost/flexibility issues.
NFV essentially brings cloud computing to ‘one’ aspect of wireless networking. The core (i.e. the packet processing).
5G will look at end to end virtualization and what values that can bring.
This includes all the ‘Radio Access Technologies” or RAT.
This imposes new challenges if cloud is to be used to process the RAT.
And then there is the concept of slicing …
Cloud and its related technologies are central to 5G but also impose challenging new requirements.
Notes: If we look at some of the goals of 5G vs where we are today we an see the gap that has to be bridged over the next few years. The goal of 1ms latency is nearly 50x better than current LTE systems, to get from 100Mbps per user to 10G we need 100x the throughput per connection. The current 10,000 connections per square kilometer needs to increase to 1Million connetions so a 100x increase in density. Reliabile communications today with LTE top out about 350km/h and we expect to bring that up by 1.5x to 500km/h . Finally the current core networks and backhaul/front haul are inflexible with wasted pools of bandwidth. The introduction of SDN/NFV will allow much better ability to chop up and virtualize the network resources for lower operational costs and capital costs and much greater flexibility.

## Slide 7: Agenda
Some wireless 4G basics
5G goals
What is 5G slicing
Potential 5G architecture incorporating multiple cloud concepts
Challenges and futures and ITU-T FG.

## Slide 8: Diversified Challenges and Gaps to Reach 5G
Network Architecture
Slicing
Ability
Required
Connections
1,000K
Connections
Per km2
Mobility
500km/h
High-speed
Railway
Throughput
10Gbps
Per
Connection
Latency
1 ms
E2E
Latency
5G
100Mbps
10K
350Km/h
30~50ms
Inflexible
LTE
GAP
30~50x
100x
100x
1.5x
NFV/SDN
Challenges because many of these requirements are conflicting
Notes: If we look at some of the goals of 5G vs where we are today we an see the gap that has to be bridged over the next few years. The goal of 1ms latency is nearly 50x better than current LTE systems, to get from 100Mbps per user to 10G we need 100x the throughput per connection. The current 10,000 connections per square kilometer needs to increase to 1Million connetions so a 100x increase in density. Reliabile communications today with LTE top out about 350km/h and we expect to bring that up by 1.5x to 500km/h . Finally the current core networks and backhaul/front haul are inflexible with wasted pools of bandwidth. The introduction of SDN/NFV will allow much better ability to chop up and virtualize the network resources for lower operational costs and capital costs and much greater flexibility.

## Slide 9: Agenda
Some wireless 4G basics
5G goals
What is 5G slicing
Potential 5G architecture incorporating multiple cloud concepts
Challenges and futures and ITU-T FG

## Slide 10: What is slicing and why is it useful
Not all devices need the same QOS/QOE from the network
  IOT “things” (low B/W) not the same as smart phones (high B/W)
  Delay requirements for cars.
Value in ability to create network for short term use.
  Emergency/Events
Future proof technique , migration to new technologies
Group similar { speed, capacity, coverage, delay, admin etc } devices into a ‘slice’
FROM DEVICE PERSPECTIVE
Notes: If we look at some of the goals of 5G vs where we are today we an see the gap that has to be bridged over the next few years. The goal of 1ms latency is nearly 50x better than current LTE systems, to get from 100Mbps per user to 10G we need 100x the throughput per connection. The current 10,000 connections per square kilometer needs to increase to 1Million connetions so a 100x increase in density. Reliabile communications today with LTE top out about 350km/h and we expect to bring that up by 1.5x to 500km/h . Finally the current core networks and backhaul/front haul are inflexible with wasted pools of bandwidth. The introduction of SDN/NFV will allow much better ability to chop up and virtualize the network resources for lower operational costs and capital costs and much greater flexibility.

## Slide 11: Agenda
Some wireless 4G basics
5G goals
What is 5G slicing
Potential 5G architecture incorporating multiple cloud concepts
Challenges and futures and ITU-T FG

## Slide 12: 5G will support many varied Radio Access Technologies (RATs) – “numerology”
Error Correction
Number of Antennas
Frequencies /bands
Power
Direction
SCMA Attributes..
F-OFDM Attributes..
Long Range, High Power Lower Bandwidth
No signaling, No reservation
Attr - X
Attr - Y
Attr - Z
Short Range, High Bandwidth, Signaling/ Reservations
Notes: We expect to see SDN and Transport SDN play important roles in the integration of the various networks under one orchestration umbrella. T-SDN can be used to control the microwave links between antenna sites, likewise T-SDN can be used to control the metro network where the front-haul and back-haul wire-line is executed. SDN again plays a role managing the network and servers that resides in the data center where the NFV functions and/or C-RAN functions execute.
Various applications/services can reside on top of the 5G orchestration system which provide them with an unprecedented flexibility to operate on the entire 5G network end to end and if suitable hooks are provided into the C-RAN functions and the EPC functions the 5G applications can co-ordinate all the behavior of their slice of a 5G network end to end.

## Slide 13: Cloud Radio Access Network (CRAN)
))))
))))
))))
))))
Place expensive equipment in small DC/CLOUD < 20km
Place extremely cheap equipment at antenna site.
Statistical gain from sharing expensive equipment.
Power/cooling at antenna sites decreases (40%).
Operations costs of antenna sites decreases.
Upgrades / differences mostly at CRAN site.
Can more easily coordinate multiple antennas (50% gain).
Notes: We expect to see SDN and Transport SDN play important roles in the integration of the various networks under one orchestration umbrella. T-SDN can be used to control the microwave links between antenna sites, likewise T-SDN can be used to control the metro network where the front-haul and back-haul wire-line is executed. SDN again plays a role managing the network and servers that resides in the data center where the NFV functions and/or C-RAN functions execute.
Various applications/services can reside on top of the 5G orchestration system which provide them with an unprecedented flexibility to operate on the entire 5G network end to end and if suitable hooks are provided into the C-RAN functions and the EPC functions the 5G applications can co-ordinate all the behavior of their slice of a 5G network end to end.

## Slide 14: 5G - how much kit at antenna vs CRAN? “the split”
))))
Analog over fiber
X,Y,Z
))))
011011,1001010,101010,1010110,1011
Digitized Analog(CPRI)
X,Y,Z
))))
Packetized Analog (ROE)
10110
10110
10110
10110
X,Y,Z
))))
Packetized
X,Y,Z
X
Y
Z
#
#
#
Moderate F/H Bandwidth usage
Extremely flexible, all RAT in CRAN
Low OPEX , most equipment in CRAN
Migration 3G,4G,5G from same CRAN
High F/H Bandwdith usage
Extremely flexible, all RAT in CRAN
Low OPEX, most equipment in CRAN
Migration T.B.D
Very High F/H Bandwidth usage
Extremely flexible, all RAT in CRAN
OPEX higher, need time of day clocking
Easily switched
Lowest F/H bandwidth usage
Inflexible RAT processing at antenna
OPEX higher, truck rolls
Easily switched
Notes: We expect to see SDN and Transport SDN play important roles in the integration of the various networks under one orchestration umbrella. T-SDN can be used to control the microwave links between antenna sites, likewise T-SDN can be used to control the metro network where the front-haul and back-haul wire-line is executed. SDN again plays a role managing the network and servers that resides in the data center where the NFV functions and/or C-RAN functions execute.
Various applications/services can reside on top of the 5G orchestration system which provide them with an unprecedented flexibility to operate on the entire 5G network end to end and if suitable hooks are provided into the C-RAN functions and the EPC functions the 5G applications can co-ordinate all the behavior of their slice of a 5G network end to end.

## Slide 15: 5G concept of an end to end “Slice”
+
+
U =
+
+
Antennas
Fronthaul
CRAN fabric
CRAN CPU/S/W
RAT Numerology
+
+
Back Haul
Core CPU/S/W
+
+
Si =
+
+
Antennas
Fronthaul
CRAN fabric
CRAN CPU/MEM
RAT Numerology
+
+
Back Haul
Core CPU/MEM
1010101
If U is the set of all resource sets { Antennas, Fronthaul , ..} then
Slice Si is a set of resource subsets taken from resource sets { Antenna, Fronthaul }
There are a nearly infinite number of possible slices | S* |
U
U
S
S
Notes: We expect to see SDN and Transport SDN play important roles in the integration of the various networks under one orchestration umbrella. T-SDN can be used to control the microwave links between antenna sites, likewise T-SDN can be used to control the metro network where the front-haul and back-haul wire-line is executed. SDN again plays a role managing the network and servers that resides in the data center where the NFV functions and/or C-RAN functions execute.
Various applications/services can reside on top of the 5G orchestration system which provide them with an unprecedented flexibility to operate on the entire 5G network end to end and if suitable hooks are provided into the C-RAN functions and the EPC functions the 5G applications can co-ordinate all the behavior of their slice of a 5G network end to end.

## Slide 16: Resource Movement Slice to Slice
+
+
Sj =
+
+
+
+
1010101
Resources can be moved from a resource set in one slice Si to the corresponding resource set in slice Sj. This should be hit-less.
+
+
Si =
+
+
Antennas
Fronthaul
CRAN fabric
CRAN CPU/MEM
RAT Numerology
+
+
Back Haul
Core CPU/MEM
1010101
S
S
Notes: We expect to see SDN and Transport SDN play important roles in the integration of the various networks under one orchestration umbrella. T-SDN can be used to control the microwave links between antenna sites, likewise T-SDN can be used to control the metro network where the front-haul and back-haul wire-line is executed. SDN again plays a role managing the network and servers that resides in the data center where the NFV functions and/or C-RAN functions execute.
Various applications/services can reside on top of the 5G orchestration system which provide them with an unprecedented flexibility to operate on the entire 5G network end to end and if suitable hooks are provided into the C-RAN functions and the EPC functions the 5G applications can co-ordinate all the behavior of their slice of a 5G network end to end.

## Slide 17: 5G will support software defined Front / Back haul.
))))
))))
))))
))))
))))
))))
))))
))))
))))
))))
))))
))))
))))
))))
))))
TSDN CONTROLLED Packet/Optical
PATH, B/W, QOS, Wavelengths,
Time Slots, Labels,
Protection, etc.
Mm-wave/uWave
CRAN
CRAN
CRAN
CRAN
Notes: We expect to see SDN and Transport SDN play important roles in the integration of the various networks under one orchestration umbrella. T-SDN can be used to control the microwave links between antenna sites, likewise T-SDN can be used to control the metro network where the front-haul and back-haul wire-line is executed. SDN again plays a role managing the network and servers that resides in the data center where the NFV functions and/or C-RAN functions execute.
Various applications/services can reside on top of the 5G orchestration system which provide them with an unprecedented flexibility to operate on the entire 5G network end to end and if suitable hooks are provided into the C-RAN functions and the EPC functions the 5G applications can co-ordinate all the behavior of their slice of a 5G network end to end.

## Slide 18: 5G will likely use SDN controlled fabrics within the C-RAN/DC
Switch
Switch
Switch
TSDN CONTROLLED XHAUL
SDN CONTROLLED FABRIC – CONNECTIVITY QOS, PATHS, REDUNDENCY CHAINING, ENCAPSULATIONS
Notes: We expect to see SDN and Transport SDN play important roles in the integration of the various networks under one orchestration umbrella. T-SDN can be used to control the microwave links between antenna sites, likewise T-SDN can be used to control the metro network where the front-haul and back-haul wire-line is executed. SDN again plays a role managing the network and servers that resides in the data center where the NFV functions and/or C-RAN functions execute.
Various applications/services can reside on top of the 5G orchestration system which provide them with an unprecedented flexibility to operate on the entire 5G network end to end and if suitable hooks are provided into the C-RAN functions and the EPC functions the 5G applications can co-ordinate all the behavior of their slice of a 5G network end to end.

## Slide 19: 5G will likely use Orchestrated NFV for processing within C-RAN/DC etc.
Switch
Switch
Switch
TSDN CONTROLLED XHAUL
ORCHESTRATION SOFTWARE TO ALLOCATE VMs, CPUs, Memory, FPGAs Containers/Processes, Grouping, Affinity, Scheduling, Recovery..
VM
CONTAINER
VM
VM
CONTAINER
CORE/METAL
CONTAINER
CORE/METAL
FPGA/Custom
Lockable Caches
Notes: We expect to see SDN and Transport SDN play important roles in the integration of the various networks under one orchestration umbrella. T-SDN can be used to control the microwave links between antenna sites, likewise T-SDN can be used to control the metro network where the front-haul and back-haul wire-line is executed. SDN again plays a role managing the network and servers that resides in the data center where the NFV functions and/or C-RAN functions execute.
Various applications/services can reside on top of the 5G orchestration system which provide them with an unprecedented flexibility to operate on the entire 5G network end to end and if suitable hooks are provided into the C-RAN functions and the EPC functions the 5G applications can co-ordinate all the behavior of their slice of a 5G network end to end.

## Slide 20: All the packet processing functions vCore are software controllable.
Switch
Switch
Switch
Packet Processing functions can be split between DC/C-RANs and re-arranged as needed. Different slices can have different configurations and totally different processing:
F1->F4->F5
F2->F6
F3->F7->F8->F9
F5
F6
F2
DC POD
C-RAN PODS
F9
F1
F4
F3
F7
F8
Notes: We expect to see SDN and Transport SDN play important roles in the integration of the various networks under one orchestration umbrella. T-SDN can be used to control the microwave links between antenna sites, likewise T-SDN can be used to control the metro network where the front-haul and back-haul wire-line is executed. SDN again plays a role managing the network and servers that resides in the data center where the NFV functions and/or C-RAN functions execute.
Various applications/services can reside on top of the 5G orchestration system which provide them with an unprecedented flexibility to operate on the entire 5G network end to end and if suitable hooks are provided into the C-RAN functions and the EPC functions the 5G applications can co-ordinate all the behavior of their slice of a 5G network end to end.

## Slide 21: Slicing – Software control of all attributes including UE
DWDM
DWDM
Digital Radio
))))
))))
))))
TSDN Hybrid Slice Front Haul IDC Backhaul o DWDM
CRANs – runs RAT, CORE and, MEC
Any server/core, any function!
Red Slice – Ultra
Reliable, Low B/W, long range, 400km/hr
Yellow Slice – Highest B/W, short range
INTER C-RAN/DC (to CORE/vEPC)
Blue Slice – Lowest Delay, Low signaling
RAT / CN
RAT/ CN
RAT
RAT/ CN
RAT/MEC
CN / MEC
CN/MEC
Idle/off
Idle resources can be moved from Slice to Slice.
Any resource can be part of any slice.
Dynamic adjustment. Resources include servers, intra/inter C-RAN B/W, C-RAN to Antenna B/W
And UE device antennas/radio components.
Any antenna, any server (within delay).
Slice UE
Resources OS/Antennas etc.
Analog or Digital or
Packet Radio
400 GE
CONTROLLERS
Notes: We expect to see SDN and Transport SDN play important roles in the integration of the various networks under one orchestration umbrella. T-SDN can be used to control the microwave links between antenna sites, likewise T-SDN can be used to control the metro network where the front-haul and back-haul wire-line is executed. SDN again plays a role managing the network and servers that resides in the data center where the NFV functions and/or C-RAN functions execute.
Various applications/services can reside on top of the 5G orchestration system which provide them with an unprecedented flexibility to operate on the entire 5G network end to end and if suitable hooks are provided into the C-RAN functions and the EPC functions the 5G applications can co-ordinate all the behavior of their slice of a 5G network end to end.

## Slide 22: Slicing – Controller Hierarchy
C-RAN INSTANCE SLICE CONTROLLER
DWDM
DWDM
))))
))))
))))
RAT / CN
RAT/ CN
RAT
RAT/ CN
RAT/MEC
CN / MEC
CN/MEC
Idle/off
400 GE
UE SLICE CTRL
IDC SLICE CTRL
FH SLICE CTRL
DC FABRIC CTRL
DC SERVER CTRL
MASTER SLICE CONTROLLER
C-RAN INSTANCE SLICE CONTROLLER
C-RAN INSTANCE SLICE CONTROLLER
DWDM
DWDM
))))
))))
))))
RAT / CN
RAT/ CN
RAT
RAT/ CN
RAT/MEC
CN / MEC
CN/MEC
Idle/off
400 GE
UE SLICE CTRL
IDC SLICE CTRL
FH SLICE CTRL
DC FABRIC CTRL
DC SERVER
CTRL
METRO N/W CONTROLLER
Segment Routing (SR) or Custom via POF/PIF
VX-LAN o IP o
Analog
Analog
DC CONTROLLER
CN
CN
CN
CN
CN
CN
Idle/off
DC POD
CN
CN
CN
CN
CN
CN
Idle/off
DC POD
Notes: We expect to see SDN and Transport SDN play important roles in the integration of the various networks under one orchestration umbrella. T-SDN can be used to control the microwave links between antenna sites, likewise T-SDN can be used to control the metro network where the front-haul and back-haul wire-line is executed. SDN again plays a role managing the network and servers that resides in the data center where the NFV functions and/or C-RAN functions execute.
Various applications/services can reside on top of the 5G orchestration system which provide them with an unprecedented flexibility to operate on the entire 5G network end to end and if suitable hooks are provided into the C-RAN functions and the EPC functions the 5G applications can co-ordinate all the behavior of their slice of a 5G network end to end.

## Slide 23: Mobile Edge Computing
DWDM
DWDM
))))
))))
))))
RAT / CN
RAT/ CN
RAT
RAT/ CN
RAT/MEC
CN / MEC
CN/MEC
Idle/off
400 GE
UE SLICE CTRL
IDC SLICE CTRL
FH SLICE CTRL
DC FABRIC CTRL
DC SERVER CTRL
DWDM
DWDM
))))
))))
))))
RAT / CN
RAT/ CN
RAT
RAT/ CN
RAT/MEC
CN / MEC
CN/MEC
Idle/off
400 GE
UE SLICE CTRL
IDC SLICE CTRL
FH SLICE CTRL
DC FABRIC CTRL
DC SERVER
CTRL
DC CONTROLLER
CN
CN
CN
CN
CN
CN
Idle/off
DC POD
CN
CN
CN
CN
CN
CN
Idle/off
DC POD
Resources in DC’s extended into CRAN for general purpose use.
Brings compute/data close to user.
I.e. within about 20km.
How to decide trade-offs between RAT/CORE in CRAN v.s. MEC in CRAN?
+
Notes: We expect to see SDN and Transport SDN play important roles in the integration of the various networks under one orchestration umbrella. T-SDN can be used to control the microwave links between antenna sites, likewise T-SDN can be used to control the metro network where the front-haul and back-haul wire-line is executed. SDN again plays a role managing the network and servers that resides in the data center where the NFV functions and/or C-RAN functions execute.
Various applications/services can reside on top of the 5G orchestration system which provide them with an unprecedented flexibility to operate on the entire 5G network end to end and if suitable hooks are provided into the C-RAN functions and the EPC functions the 5G applications can co-ordinate all the behavior of their slice of a 5G network end to end.

## Slide 24: Agenda
Background - some 4G basics.
Some wireless basics and their problems
5G goals
What is 5G slicing
Potential 5G architecture incorporating multiple cloud concepts
Challenges / futures / ITU-T FG

## Slide 25: Challenges Ahead – Many Cloud related.
SDN API’s for each component of the slice
Hierarchical controllers for each cloud
Hierarchical OA&M above the slices
OA&M within a slice
Resource optimization from slice to slice (hitless)
Fronthaul slicing/switching
Ultra High performance NFV for CRAN (FPGA virt.)
Low delay NFV for core
New Cores (possibly non IP for IOT).
MEC control/trade-offs intra/inter slice
Performance/Reliability etc.
Security (everywhere)
Notes: If we look at some of the goals of 5G vs where we are today we an see the gap that has to be bridged over the next few years. The goal of 1ms latency is nearly 50x better than current LTE systems, to get from 100Mbps per user to 10G we need 100x the throughput per connection. The current 10,000 connections per square kilometer needs to increase to 1Million connetions so a 100x increase in density. Reliabile communications today with LTE top out about 350km/h and we expect to bring that up by 1.5x to 500km/h . Finally the current core networks and backhaul/front haul are inflexible with wasted pools of bandwidth. The introduction of SDN/NFV will allow much better ability to chop up and virtualize the network resources for lower operational costs and capital costs and much greater flexibility.

## Slide 26: ITU-T 5G wireline FG-IMT-2020 Phase I (2H15) Summary
ITU Focus Group to study the requirements and standardization needs of the wireline in support of 5G (non Radio)
Huawei chair (Peter Ashwood-Smith) in May 2015
Vice chairs CMCC(Y.Wantg), ETRI(N.Ko), NTT (Y.Goto), Telecom Italia (L.Pesando)
Parent Group SG-13
Completely Free format to explore ‘gaps’ required to support the 5G vision (IMT.VISION)
Parallel work in 5 main areas to minimize overlap with other 5G SDO’s:
  High level network architecture, championed by Dr Namseok Ko, ETRI, Korea;
  Network softwarization, championed by Prof Akihiro Nakao, University of Tokyo, Japan;
  End-to-end quality of service, championed by Dongwook Kim, ex KT Corporation; Olivia Heeyun Choi, KT Corporation;
  Front haul / back haul, championed by Dr Frank Effenberger, Huawei Technologies; Dr Gyaneshwar C. Gupta, Oki Electric Industry Co., Ltd.
  Emerging networking technologies - information centric networking (ICN), championed by Dr Paul Polakos, Cisco Systems; Dr Marc Mosko, PARC.
Led production of final document with 85 identified gaps in XX areas and delivery to SG-13 in December 2015.
Meeting | San Diego (8-9 June 2015) | Geneva (13-14 July 2015) | Turin (21-24 September 2015) | Beijing (27-30 October 2015)
Input docs | 34 | 26 | 34 | 27
Output docs | 1 | 7 | 6 | 2
Meeting report | O-001 | O-002 | O-009 | O-015
Remote participants | 18 | 30 | 22 | 11
Total participants | 60 | 75 | 55 | 63
+ multiple conference
Calls, Work Shops etc.

## Slide 27: Output Document Structure: Executive Summary + Gaps + Supplemental info
A.19 Mobility management for distributed flat network | Priority: High
Description: As the IMT-2020 core network is envisioned to be a flat distributed network, which is composed of the multiple distributed gateways to cope with traffic explosion and latency requirements of applications, mobility management should be studied aligning with those architectural changes. | 
Related work: 3GPP, SG13 | 
A.18 End-to-end network management in a multi-domain environment | Priority: High
Description: Multiple network management protocols in different network domains make it difficult to support unified network operations over multiple network domains. A unified end-to-end network management should be considered to ensure compatibility and flexibility for the operation and management of an IMT-2020 network. | 
Related work: SG13 | 
A.17 OAM protocols | Priority: High
Description: OAM protocols are not standardized in some parts of IMT networks such as the front haul network. Standard OAM protocols should be studied for fault management and performance management between network equipment that may be commonly used across the IMT-2020 network. | 
Related work: | 

## Slide 28: ITU-T 5G wireline FG-IMT-2020 Phase II (2016)
Renewed end of 2015 for all of 2016 (Ashwood-Smith chair), Vice Chairs mostly same with substitution within NTT.
New Terms of Reference as follows:
  Demonstrations or prototyping with other groups (e.g., with open source community);
  Network softwarization and ICN;
  Network architecture refinement;
  Fixed mobile convergence;
  Network slicing for front haul/back haul;
  New traffic models and associated QoS and OAM aspects applicable to IMT-2020 architecture.
Slower pace - Four meetings in 2016 – First is March in Seoul.
Outputs A: Several draft recommendations close to final ready to be progressed by ITU in 2017.
Outputs B: Proof of concept of softwarization, possibly joint open source orchestrator.
Other suggestions welcome ... We can do quite a bit with this FG in 2016

## Slide 29
Thank You