## Slide 1: ITU-T SG17 updates
Koji Nakao
WP2/17 Chair of ITU-T SG17
Liaison Officer of Q13/17

## Slide 2: Security Areas covered by SG17
Cybersecurity – Cybex
Countering spam
Information Security Management
Fundamental security: PKI, X.509…
Identity Management (IdM)
Application security
  Home network, IoT, ITS, smart grid, smartphone, SDN, IPTV, web services, etc.
  Cloud computing, big data analytics, and telebiometrics.
Covered by Q6/17
Question 13 (Security Aspects for ITS communications) was formally approved at the last SG 17 meeting in September, 2017.

## Slide 3: Approach taken by SG17 for developing security standards (6 steps)
High level requirement : kick-off to study
Reference Model The reference model should be identified for security considerations;
Threats analysis Based on the model, threats should be identified and analyzed;
Risk Assessment Based on the threats, risk should be assessed and identified;
Security Requirements Based on the risk assessment, security requirements should be developed;
Security Controls Based on the requirements, security controls (countermeasures) should be identified and implemented.

## Slide 4: Direction for ITS security in SG 17 (Question 13)
Hierarchy of Standards/Recommendations for Secure ITS
The following figure can be identified as a hierarchy of Standards/Recommendations for secure ITS in ISO and ITU-T from SG17 perspective. There are three Areas classified in this hierarchy for our considerations.

## Slide 6: Area 2): (General) Security Guideline for Secure ITS
Standards/Recommendations developed in this area can be identified as high-level (general) security guidelines (e.g. Code of Practice) for secure ITS environments. Documents studied in this area should be based on Reference Architecture (RA) of ITS, Vocabulary as common terms, and possible Use Cases which are developed in the area 1) in the above figure.

## Slide 7: The following documents may be categorized in area 2:
Recommendation ITU-T X.1373 (Secure software update capability for intelligent transportation system communication devices) (published)
Draft Recommendation ITU-T X.itssec-2 (Security guidelines for V2X communication systems) (Target for the final version of this Recommendation is September 2018)
Security Guideline/Recommendation (by WP29/TFCS) (Target for the final version of this document is March 2018)

## Slide 8: Draft Recommendation ITU-T X.1373
Secure software update capability for intelligent transportation system communications devices (Status : Approved)
Scope:
  In the context of updates of software modules in the electric devices of vehicles in the intelligent transportation system (ITS) communication environment, this Recommendation aims to provide a procedure of secure software updating for ITS communication devices for the application layer. This includes a basic model of software update, its threat and risk analysis, security requirements and controls for software update and a specification of abstract data format of update software module.
  The procedure related to in-vehicle communication is the out of scope of this Recommendation. For reference, the procedure used in-vehicle in this Recommendation is informative.
  The procedure is intended to be applied to communication devices on ITS vehicles under vehicle-to-infrastructure (V2I) communication by means of the Internet and/or ITS dedicated networks. The procedure can be practically utilized by car manufactures and ITS-related industries as a set of standard secure procedures and security controls.

## Slide 9: General Model for a remote software update in Rec. ITU-T X.1373
Scope

## Slide 10: The following documents may be also categorized in area 2:
Recommendation ITU-T X.1373 (Secure software update capability for intelligent transportation system communication devices) (published)
Draft Recommendation ITU-T X.itssec-2 (Security guidelines for V2X communication systems) (Target for the final version of this Recommendation is September 2018)
Security Guideline/Recommendation (by WP29/TFCS) (Target for the final version of this document is March 2018)

## Slide 11: X.itssec-2(Overview)
  Revised draft at SG17 September 2017 meeting (see Attachment-1)
  Scope
  This Recommendation provides security guidelines for V2X communication systems.
Contents
  Analysis of threat for V2X communication systems
  The security requirements for V2X communication systems
  Use case of V2X communication systems
V2X
      V2V(Vehicle to Vehicle)
      V2I(Vehicle to Infrastructure)
      V2ND(Vehicle to Nomadic Devices)
      V2P(Vehicle to Pedestrian)

## Slide 12: Content of X.itssec-2
1. Scope
2. References
3. Definitions
3.1 Terms defined elsewhere
3.2 Terms defined in this Recommendation
4. Abbreviations and acronyms
5. Conventions
6. V2X communication systems
6.1 Overview
6.2 V2V communication system
6.3 V2I communication system
6.4 V2ND communication system
7. Threats
7.1. Threats in V2V communication system
7.2 Threats in V2I communication system
7.3. Threats in V2ND communication system
8. Security requirements
8.1. Security requirements for V2V communication system
8.2 Security requirements for V2I communication system
8.3 Security requirements for V2ND communication system
9. Examples for V2X security system
[Note: Clause 9 should be removed if there is no contribution.]

## Slide 13: Examples: X.itssec-2 (V2V/V2I)
  V2V/V2I communication type
< V2V warning propagation
- forward warning propagation >
< V2V beaconing>
< V2V warning propagation
- backward warning propagation>
<V2V platoon communication>
< V2I warning>
< V2V/V2I information exchange>

## Slide 14
Overview of the UN Task Force on Cyber Security and OTA Issues (CS/OTA)
Threats assessment related to V2X should be based on the result of WP29/TFCS (Recommendation)

## Slide 15: Mission of the Task Force
The task force works on certification-relevant requirements about cyber security, data protection and privacy, and over-the-air (OTA) updates
The first results of the task force’s work will be delivered in December 2017 to the WP.29 ITS/AD Informal Group as a guideline

## Slide 16
Current Status
Data protection
Software updates
Type approval aspects
Cyber Security
Security aspects
Security aspects
Legal aspects
out of scope
Threat analysis
pre- registration
post- registration
Develop flow diagram
Define mitigation principles
Define approval method
Table of threats
Develop guidance/recommendation for ITS/AD
Safety aspects
Develop
recommendation for safe execution
General Flow of works in WP29/TFCS and OTA

## Slide 17: Current Status
The task force has finished identifying key risks and threats
The task force has started to develop 18 mitigations
  Based on an extended CIA (confidentiality, integrity, availability) approach
  Reference documents for the mitigations have been identified
  The first draft Recommendation on Cybersecurity was discussed in Tokyo (8th) meeting
The task force is on target to meet its goals on time

## Slide 18
See the latest draft text of Recommendation on CyberSecurity in WP29/TFCS
This Recommendation will be finalized in Jan. 2018.

## Slide 20: Area 3): Specific Security Guideline for Gateway, ITS networks, Applications, Incident handling, etc.
Standards/Recommendations developed in this area can be identified as Security Guidelines for common components in ITS environments, including security specifications of ITS GW, ITS NW, Applications, etc. Documents studied in this area should be based on documents developed in area 1) and area 2) as in the above figure.
New work item on "Security requirements for vehicle accessible external devices" (see Attachment-2) (NWIP in ITU-T SG17 (September, 2017)
New work item, "Technical Framework for Intrusion Detection System on In-Vehicle Systems" (NWI in ITU-T SG17 (September, 2017))
New work item, "Security guidelines for vehicular edge computing“ (see Attachment-3) (NWIs in ITU-T SG17 (September, 2017))

## Slide 21: Additional updates:
We did hold a ITS security workshop on 28th August at Geneva. At the ITS security workshop, activities in WP29/TFCS_OTA was highlighted and SG17 did conclude to strengthen collaboration with WP29/TFCS as a conclusion of the workshop.
SG/17 would appreciate if CITS could consider the above updated information from SG17 for the future collaboration.
Regarding ISO/TC204, TC204/WG18 is our target for collaboration on ITS security with SG17. Based on the liaison statement from SG17 to TC204, we tried to seek out some common topics for collaboration between ITU-T SG17 and ISO/TC204. The F2F meeting will be considered for sharpening our common topics for our future collaboration.

## Slide 22: Attachments
Attachment-1:
Baseline text of the Draft Recommendation ITU-T X.itssec-2 (Security guidelines for V2X communication systems)
Attachment-2:
New work item on "Security requirements for vehicle accessible external devices"
Attachment-3:
New work item, "Security guidelines for vehicular edge computing"