## Slide 1
A new smart city infrastructure
enabled by ‘Vehicle domain service’
CITS meeting@Nanjing
2018-09-07
Kaname Tokita
ISO TC 22 / SC 31 / WG 8 Honda R&D Co., Ltd.
JSAE

## Slide 2: Overview
  Presenter’s profile
  Background
  Project status
  Introduction of vehicle domain service
  Smart traffic services and VDS
  Smart traffic architecture model proposal
  Harmonization in development

## Slide 3: Presenter’s profile
  Education
  The University of Tokyo, Graduation of Mechanical engineering Master’s program, Master of Engineering
  Organization
  Honda R&D Co., Ltd., Chief Engineer
  06M/Y EU5D CIVIC Project leader of electrical system test
  09M/Y US4D/2D CIVIC Project leader of electrical system design
  Field of specialty; Vehicle control system design/test, Vehicle communication system design/test
  ISO / IEC Expert
  ISO TC22 SC31 data communication expert, HOD of Japan
  ISO 15118-2 ED2 V2G CI PT2 Project leader (2015-2017)
  ISO TC22 SC31 WG8 vehicle domain service Convener
  ISO 23239 vehicle domain service project leader

## Slide 4: Background
  Spread of Information and Communication Technologies
  Recently information and the communication technology evolved with the explosive spread of smartphones drastically.
  The communication speeded up, cameras and the sensing devices became high definition and as for the CPU, an expressway became high-performance. The spread and increased production of these devices accelerated the cost reduction.
  Expected evolution of vehicle ICT
  The introduction of these to vehicles are expected by the generalized information and communication technology and spread of cost reduced devices.
  Particularly, the introduction of the information and communication technology about driving movement will be expected to complement a conventional incomplete domain, and to realize safer, more effective and multifunctional driving.

## Slide 5: ISO 23239 project status
  NWIP and AWI
  Discussion started in 7th ISO TC 22 / SC 31 data communication plenary meeting at VDA, Berlin in September 2017.
  NWIP was submitted to ISO-CS in November 2017.
  The proposal was approved in January 2018.
  New project and working group allocation
  The new project was started as ISO 23239, vehicle domain service.
  It was allocated under ISO TC 22 / SC 31 as the new WG 8.
  Liaison and harmonization
  Potential harmonization are under discussion with SAE and ISO TC 204 / WG3.
  Appreciated harmonization with standardization bodies about smart cities and smart traffic might be necessary.

## Slide 6: Definition of VDS
  Definition of Vehicle Domain System
  Data collection server service implemented in vehicle
  Data collecting application, to get safety or function relevant information from driving group partners around the server vehicle by itself without additional infrastructure data service.
Vehicle server
Driving group partners
Vehicles
Walkers
Bikes
Communication channel
VDS application
Partner
application
VDS function overview

## Slide 7: Target of VDS scope
  How to accept many various standards and specifications
  Too much standards on driving applications and communication channel already exists, also increasing continuously.
  From implementation point of vehicle application, it is necessary to confirm consistency and ensure compatibility of whole application within vehicle.
  Define requirement for vehicle side application
  harmonizing with all existing standards
  Check consistency of vehicle application
  Ensure conformance, compatibility and interoperability
  Economy and efficiency for implementation
  Global harmonization as ISO standard

## Slide 8: Definition of vehicle domain
  Vehicle domain and actors
  The master vehicle provides domain service to the actors registered in vehicle domain.
  The domain actors are vehicles, participants and sensors.
  The master vehicle collects information from actors to generate domain map information.
  Generated map is shared among domain actors.
Master vehicle
Actors of vehicle domain
Vehicle domain
Domain vehicle 1
Domain vehicle 2
Domain vehicle 3
Domain participants 1
Domain participants 3
Domain participants 2
Domain sensor 1
Domain sensor 2

## Slide 9: Data integration and identification of actors
  Identification of all actors ~ completion of domain map
  Once all reports are received by master vehicle, it will generate the whole map by integrating all information.
  Sensor reports are validated by comparing those from vehicles and participants.
  The data collection interface shall be uniquely defined for effective and speedy data collection and interoperability.
Unified interface
Master vehicle
Domain vehicle
Domain participant
Domain sensor
Master vehicle
Domain vehicle
Domain participant
Domain sensor
Dedicated interface
○
×

## Slide 10: Data calibration by master time synchronization
  Reporting data shall be calibrated by time synchronization
  Master vehicle generates the domain master time for data synchronization. It will request the calibrated data based on synchronized time to all actors.
Master vehicle
Data calibration by VDS master time synchronization
Vehicle domain
Domain vehicle 2
Domain vehicle 1

## Slide 11: Driving maneuver within operation domain
  Vehicle domain for driving maneuver have two areas
  It consists of preparation and operation domain.
  Vehicle domain system shall define only the method of data exchange and negotiation sequences.
Master vehicle
Vehicle domain
Domain vehicle
Preparation
Operation
Typical driving maneuver example of lane change

## Slide 12: Calibrated data collection of driving maneuver
  Master vehicle collects the calibrated data
  Master vehicle requests relevant data for maneuver negotiation to target domain vehicle with generated reference stepped time.
  Domain vehicle will report the calibrated data.
  Maneuver plan will be adjusted with target domain vehicle, if necessary.
Master vehicle
Vehicle domain
Typical calibrated response for driving maneuver negotiation
Synchronization request
Synchronized response
Domain vehicle

## Slide 13: Documents structure and development schedule
  Part 1:General system requirements and use case definitions
  AWI: 2018-01~
  WD is under development, CD will be expected in 2019-01~.
  Part 2:Application layer and sequence requirements
  PWI: ~2018-10, NWIP: ~2019-06
  Part 3:Network and transport layer requirements
  PWI: ~2018-10, NWIP: ~2019-06
  Part 4:Physical and data link layer requirements
  PWI: ~2018-10, NWIP: ~2019-12
  Part 5:Conformance tests for data collection interfaces
  PWI: ~2019-12, NWIP: ~2020-06

## Slide 14: Variations and implementation of smart traffic services
  Basic one way services
  Traffic information providing service; ITS applications on freeway or in the city
  Spot traffic monitoring; traffic participants data collection around an spot or intersection
  Group traffic monitoring; behavior monitoring about vehicles belongs to some (business) group, such as baggage or pizza delivery, trucks of logistic company or taxis
  Interactive two way services
  Vehicle certification service; Electric tall collection, other value added drive through services
  Driving maneuverer coordination; local traffic coordination by ITS infrastructure
  Overall smart city traffic optimization service
  Traffic optimization consists of whole traffic data collection and traffic control in smart city.
  Whole data collection; integrate various business groups, such as public transport, business logistics and customer driving vehicles
  Traffic controls; signal timing control, priority lane control, accessible area control will be provided.

## Slide 15: Smart traffic services provided by VDS
  Traffic monitoring
  VDS will collect information of all actors within its vehicle domain.
  VDS will complete the instant actors map of vehicle domain.
  VDS will issue the traffic monitor report including instant actors’ map to be used other domain actors.
  Traffic coordination
  VDS will coordinate driving maneuver plan with other relevant vehicle actors within vehicle domain.
  More complex coordination, such as multiple or sequential coordination will be enabled.
  Traffic optimization support
  Traffic optimization consists of whole traffic data collection and traffic control.
  VDS will provide the local whole data collection interface and part of traffic control by route recommendation.
  They will be connected to LDM with traffic management servers to optimize traffic flows in smart cities.

## Slide 16: Smart city information exchanges modeled by systematic approach
  Systematic approach will generalize the functions in smart city.
  Whole of explicit functions and implicit rules are generalized to be modeled.
  Modeling will be performed in use case definitions.
  Use cases are located on geography and classified on business.
  Geographical scale covers from home to country.
  Business domain covers from customer to centralized management.

## Slide 17: Introduction of smart traffic architecture model proposal
  Definition of Smart Traffic Architecture Model proposal
  Horizontal axis; customer, commercial&consumer, business, public and central traffic manager
  Vertical axis; home, town&street, city, state&intercity and country
  Various business use cases will be located in each business domain.
 | Traffic manager | Public | Business | Commercial/Consumer | Customer
Country |  |  |  |  | 
State / Inter-city |  |  |  |  | 
City |  |  |  |  | 
Town / Street |  |  |  |  | 
Home |  |  |  |  | 
Area
Function
Smart City Traffic Manager
ITS Information Service
OEM Telematics
TAXI Management
Car sharing Service
Baggage Delivery
Food Delivery
Logistics Transport Manager
Bus Monitor Manager
LRT Monitor Manager
Local Dynamic Map Server
Traffic Operator
Traffic Monitor

## Slide 18: VDS allocation in smart traffic architecture model
  Vehicle domain service is located in STAMp
  VDS will be located from home to city on geographical and customer to public in business
  VDS will be connected explicitly or implicitly with other services
 | Traffic manager | Public | Business | Commercial/Consumer | Customer
Country |  |  |  |  | 
State / Inter-city |  |  |  |  | 
City |  |  |  |  | 
Town / Street |  |  |  |  | 
Home |  |  |  |  | 
Area
Function
Smart City Traffic Manager
ITS Information Service
OEM Telematics
TAXI Management
Car sharing Service
Baggage Delivery
Food Delivery
Logistics Transport Manager
Bus Monitor Manager
LRT Monitor Manager
Local Dynamic Map Server
Traffic Operator
Traffic Monitor
Vehicle Domain Service

## Slide 19: Development of VDS in smart city architecture model
  Vehicle domain service in smart traffic architecture.
  VDS will be allocated in STAMp and connected with other services.
  Many of information data containers are exchanged with other STAMp services.
  Many functions of VDS will be completed in cooperation with other services in STAMp.
  Smart traffic architecture model shall be developed with VDS.
  VDS works as low end interface and computing of STAMp.
  VDS is scope of ISO / TC 22 / SC 31.
  VDS would like to harmonize in smart traffic architecture model with ITU-T.

## Slide 20: The End
  Thank you for attention!