## Slide 1: IPWAVE Working Group of IETF, an updated status report
Alexandre PETRESCU, CEA
March 2019

## Slide 2: Contents
What is IPWAVE Working Group
Main WG item: IPv6 over 802.11 OCB
Additional WG item: Problem Statement and Use Cases
Current status

## Slide 3: IPWAVE Working Group
IP Wireless Access in Vehicular Environments (IPWAVE) is a Working Group at the Internet Engineering Task Force (IETF).
Works on “V2V and V2I use-cases where IP is well-suited as a networking technology”.
Liaisons with ISO TC 204, SAE, ETSI ITS, IEEE.
Group formed in year 2016, after successful Birds-of-a-Feather (BoF) www.ietfjournal.org/intelligent-transportation-systems-and-the-ietf/
Email list, roughly 400 subscribers www.ietf.org/mailman/listinfo/its

## Slide 4: Main Work Item: IPv6 over 802.11-OCB
draft-ietf-ipwave-ipv6-over-80211ocb-34 publicly accessible
IEEE 802.11p is a MAC and PHY layer for vehicular wireless networks:
  Operates Outside the Context of a BSSID (802.11-OCB).
  Works at 5.9GHz bands channels with a short 10MHz width.
  Requires the use of 802.11 “QoS Data” headers.
  Higher power levels are allowed (33 dBm, 40 dBm, country-specific).
  Future evolutions: 802.11-NGV, 802.11bd.
Running an IP layer on 802.11-OCB requires the definition of a few parameters:
  EtherType is 0x86DD
  Minimum MTU size is 1280 bytes
  TID is 001 ‘Background’, ‘AC_BK’
  Ethernet Adaptation Layer makes 802.11 headers from Ethernet II headers
  ‘Stable’ and ‘Opaque’ Interface Identifiers of variable length (1..118)

## Slide 5: Additional WG item: Problem Statement and Use Cases
draft-ietf-ipwave-vehicular-networking-07 publicly accessible
Exercise in identifying gaps and open areas, prioritize for potential upcoming work;
Analyse address autoconfiguration, routing, mobility management, DNS, service discovery, security and privacy – for IP networking in vehicular environments;
Describes general problems;
Describes IP-related problems;
Mentions also the use of IP in cellular networks for vehicular environments.

## Slide 6: Current Status
The main WG item “IP-over-OCB”:
  Several independent documents have been submitted
  One joint document has been produced, and adopted by vote, as a WG item
  discussed publicly in the WG
  reviewed by the 6Man Working Group (“IPv6 Maintenance”)
  Last Called twice in IPWAVE, with multiple comments
  Demonstrated: (1) during Hackathon in spring 2019, (2) in some deployed Road Side Units (IP-RSUs), (3) in some vehicle-to-vehicle trials.
  Submitted to IESG for debate and approval towards becoming RFC.
  IETF’s INT and IoT Directorates reviews.
  Expecting finalising discussions in Prague IETF, March 2019.
  New work directions.