## Slide 1
ITS Radiocommunications Policies in Japan
July 4, 2016
Yuji Nakamura
Director of New-Generation Mobile Communications Office,
Radio Dept., Telecommunications Bureau,
Ministry of Internal Affairs and Communications (MIC),
Japan

## Slide 2
ITS Development in Japan

## Slide 3: ITS promotion framework of Japanese Government
MLIT
Ministry of Land, Infrastructure, Transport and Tourism
Cabinet Secretariat
(IT Strategic Headquarters)
Cabinet Office
(Council for Science, Technology and Innovation)
Road Bureau
Deployment of road infrastructure
Road Transport Bureau
Safety standards for automobile
NPA
National Police Agency
Road traffic safety
MIC
Ministry of Internal Affairs and Communications
Info-Communication Technology for ITS
METI
Ministry of Economy, Trade and Industry
Promotion of the automobile industry
3

## Slide 4: Current Situation of ITS in Japan
ETC
Target detection system in front
- On-vehicle radar system using radio waves, supersonic waves and infrared ray, and camera
- Detecting vehicles and obstacles in front
- Warning, emergency brake, keeping inter-vehicle distance
Obstacles detection system around vehicle
- radar system using radio waves and supersonic waves, and camera
- Detecting obstacles and warning
Advanced Driver Assistance Systems
- V2V, V2I and V2P communications via 700MHz band radio waves
Probe information
- Probe information collection by each car maker
- Providing each users with traffic information
VICS (Vehicle Information and Communication System)
- Since 1996
- traffic information through FM-multiplex broadcasting, radio beacons and infrared beacons
- over 51 million vehicles as of March 2016
DSRC (Dedicated Short Range Communication)
ETC (Electronic Toll Collection) since 2001
- over 74 million units as of May 2016
ITS Spot since 2011
- About 1600 locations mainly on expressways nationwide
- Providing drivers with safe driving support information
Enhancement of ITS by effective use of Information Communication Technology
4

## Slide 5: ITS Radiocommunications in Japan (1)
Electronic Toll Collection System (ETC)
Roadside Broadcasting
(Highway radio)
700 MHz ITS
（Advanced Driver Assistance Systems）
Avoiding Vehicle Collisions by vehicle-to-vehicle communications.
左から合流車、注意
ITS spots provide information detected by roadside sensors.
Dedicated Short Range Communication (DSRC・ITS Spot)
(1) Text display type
(3) Map display type
(2) Simplified Graphic display type
Vehicle Information and Communication System (VICS)
76～90
MHz
755.5～764.5
MHz
2.5GHz
5770～5850
MHz
1620
kHz
76～77
GHz
78～81
GHz
60～61
GHz
22～29
GHz
(2) Simplified Graphic display type
kHz
GHz
Millimeter Wave Radar
24/26 GHz Band UWB Radar or 79 GHz Band High-resolution Radar
76 GHz Band Long-distance Radar
5

## Slide 6: ITS Radiocommunications in Japan (2)
 | Spectrum | Service | Introduction time
Roadside Broadcasting (Highway Radio) | 1620kHz | Provide Traffic information | Since 1980
VICS (Vehicle Information and Communications System) | 76-90MHz (FM multiplex broadcasting) 2.5 / 5.8GHz (Radio beacon) | Provide Traffic information | Enacted in 1994
ETC (Electronic Toll Collection) | 5.8GHz | Collect highway toll | Enacted in 1997
DSRC (Dedicated Short Range Communication) | 5.8GHz | Provide various information | Enacted in 2001 (Revised in 2007)
700 MHz ITS （Advanced Driver Assistance Systems） | 760MHz | Provide safety information | Enacted in 2011
Millimeter-wave radar | 24/26GHz 60/76GHz 79GHz | Detect obstacles | Enacted in 2010 Enacted in 1997 Enacted in 2012
6

## Slide 7: ITU-R Recommendation on Radio Interface Standards of V2X
Specifications | ETSI | IEEE | ARIB（Japan） | TTA（Korea）
Frequency band | 5855-5925 MHz | 5850-5925 MHz | 755.5-764.5 MHz (Single Channel) | 5855-5925 MHz
Channel width | 10 MHz | 10 MHz or 20 MHz | Less than 9 MHz | Less than 10 MHz
Modulation system | BPSK OFDM, QPSK OFDM, 16QAM OFDM, 64QAM OFDM | 64-QAM-OFDM, 16-QAM-OFDM, QPSK-OFDM, BPSK-OFDM 52 subcarriers | BPSK OFDM, QPSK OFDM, 16QAM OFDM, | BPSK OFDM, QPSK OFDM, 16QAM OFDM Option : 64QAM OFDM
Data transmission rate | 3, 4.5, 6, 9, 12, 18, 24, 27 Mbps | 3, 4.5, 6, 9, 12, 18, 24, 27 Mbps (10MHz) 6, 9, 12, 18, 24, 36, 48, 54 Mbps (20MHz) | 3, 4.5, 6, 9, 12, 18 Mbps | 3, 4.5, 6, 9, 12, 18 Mbps Option : 24, 27 Mbps
Media Access Control | CSMA/CA | CSAM/CA | CSMA/CA | CSAM/CA, Option : Time slot based CSMA/CA
FDD/TDD | TDD | TDD | TDD | TDD
7
○ ITU-R Recommendation M.2084
“Radio interface standards of vehicle-to-vehicle and vehicle-to-infrastructure communications for Intelligent Transport Systems applications”
○ World first commercial services of V2V (October 2015)

## Slide 8: WRC-15 Results (Spectrum for Short Range Radar)
77-81 GHz band Spectrum Allocation
77
81
80
79
78
76
75
Past Allocation
WRC-15 approved this allocation.
Long Range Automotive Radar
Radio Location Service
Short Range Automotive Radar
Amateur and Amateur Satellite
Fixed
Radio Astronomy
Agenda Item 1.18
77.5 - 78 GHz Additional Primary Allocation
frequency (GHz)
8

## Slide 9: WRC-19 AI-1.12: ITS Application
Agenda for the 2019 World Radiocommunication Conference
1.12 to consider possible global or regional harmonized frequency bands, to the maximum extent possible, for the implementation of evolving Intelligent Transport Systems (ITS) under existing mobile-service allocations, in accordance with Resolution 237 (WRC-15);
Global or regional harmonization of spectrum for ITS Application
9

## Slide 10
10
Alert sounds
Pre-collision Brake
(Automated braking)
Radar
ETC
Car navigation, etc.
FM multiplex
broadcasting
Radio Beacon
Optical Beacon
ETC 2.0
Connected Cars
Provision of traffic jam Information, charge setting, etc.
Advanced driving support by utilizing camera or radar
（autonomous type）
Highly advanced driving support by combining V2V communication with high-resolution radar, etc.（autonomous plus cooperative type）
Automated Driving
Development of ITS
Now
(Already become popular)
Now～Near Future
(Recently becoming popular)
Future
White lane
markings
Lane keep assist
Alert sounds
Development of ITS utilizing Radiocommunications
VICS

## Slide 11
Automated Driving R&D Program
(SIP-adus) in Japan

## Slide 12: SIP (Cross-Ministerial Strategic Innovation Promotion Program)
（参考）
SIP is aiming to realize Innovation through promoting R&D at all stages by enhancing cross-ministerial cooperation.
CSTI designated research themes based on the expected extent of impact to solve societal issues and enhance economic growth.
CSTI appointed Program Director (PD) for each research theme and allocates the budget.
SIP-adus (Automated Driving for Universal Services) tries to realize automated driving technologies.
CSTI
Governing Board
PD (Program Director)
Promoting committee
●PD (chair)
●Related ministries,
Management agencies,
Experts from academia and
public sector
Research organizations
Universities,
Corporations,
Research institutes, etc.
Established for
each project
Management Agency (Funding Agency)
- Governance Structure -
12
*CSTI : Council for Science, Technology
and Innovation

## Slide 13: SIP (Strategic Innovative Promotion Program) - Overview
○ Infrastructure Radar System
Developing 79 GHz band high-resolution radar which can identify pedestrians, cars and etc.
○ V-V Communication and V-I Communication
Drawing up communications protocol and etc.
○ V-P (Pedestrian) Communication
Developing direct communications style which uses dedicated terminals, mobile phone network application style system and etc.
Aiming to realize Science & Technology Innovation through promoting R&D overlooking from basic research to implementation and commercialization by cross-ministerial cooperation.
13
Pedestrian,
bicycle
Building
Alert
Car（including automated driving car）
Prediction on collusion
and Alert
Alert
Detect something in blind spot for drivers
MIC’s efforts in SIP
Use case of merging
on the free way
Identify cars and motorcycles
Identify pedestrians and bicycles

## Slide 14
Integrated Field Evaluation in 2017
1. Dynamic Map
2. Human Machine Interface
3. Cyber Security
4. Pedestrian Assistance
5. Next Generation Public Transportation
Focus areas:
Integrating research achievements, SIP-adus will: - conduct integrated field evaluation tests in 2017 - develop sustainable framework for deployment - contribute to develop standards and guidelines
14

## Slide 15
Dynamic Map
Static (<1month )
Semi-static ( < 1 hour )
Semi-dynamic ( < 1 min )
Dynamic ( < 1 sec )
  Basic Map Database
  Digital cartographic data
Topological data with unique
Road Facilities
Planned and forecast
traffic regulations
road works
weather forecast
Traffic Information
accidents
congestion
local weather
Information through V to X
surrounding vehicles
pedestrians
timing of traffic signals
Link
Basic Map
Time frame
Hierarchical structure of digital ‘Map’ layered by time frame
Linked layers
A planning company will be established soon to promote marketing and preparation for business start-up on Dynamic Map, based on SIP-adus study results so far.
15

## Slide 16: Roadmaps of Automated Driving System
Difficulty of technology
Levels of Automated Driving System（”Public-Private ITS Initiative/Roadmaps 2016 ” - IT Strategic Headquarters）
16
Categories |  | Outline | Examples of expected service | Schedule for commercialization
Level ４ ※１ | Full Automated Driving Systems | All of the acceleration, steering and control operations are done by the automobile (other than drivers). | Full Automated Driving Systems (non remote control type) | By 2025 ※Target year
 |  |  | Full Automated Driving Systems (remote control type) in limited areas | By 2020
Level ３ | Semi-Automated Driving Systems | All of the acceleration, steering, and braking operations are done by the automobile. (Drivers respond to emergencies) | Auto pilot | By 2020 ※Target year
 |  | More than one of the acceleration, steering and braking operations is done by the automobile at the same time. | Semi auto pilot | By 2020
Level ２ |  |  |  | 
 |  |  | Automated lane change | By 2017
 |  |  | Adaptive cruise control, Lane keep assist | already commercialized
Level １ | Safety Driving Support Systems | Any of the acceleration, steering or braking operations is done by the automobile. | Pre-collision Brake | Some of the systems are already commercialized
－(informational) |  | Alerting drivers etc. | Alerting drivers of nearby vehicles and red light | 

## Slide 17
Current Status and Future Trends of Mobile Communications in Japan

## Slide 18: Number of Subscribers (Mobile Phones and BWA)
Chart: Fiscal Year
| 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015.12
BWA | 0.15 | 0.807 | 2.296 | 5.1 | 7.46 | 19.46 | 30.88
3.9世代携帯電話(LTE) | 0.026 | 2.3 | 20.5 | 46.41 | 67.78 | 82.75
第3世代携帯電話(3G) | 0.09 | 7.16 | 16.69 | 30.35 | 48.33 | 69.91 | 89.22 | 99.6 | 109.06 | 118.1 | 125.86 | 115.54 | 97.6 | 84.91 | 71.67
第2世代携帯電話 | 20.88 | 31.53 | 41.53 | 51.14 | 60.94 | 69.03 | 68.5 | 64.83 | 57.65 | 43.43 | 27.17 | 13.77 | 7.9 | 3.12 | 1.41 | 0.05
（Million）
Number of Subscribers (as of December 2015) ・Mobile Phones and BWA Total：157million（124.1%）
（breakdown）
・Mobile Phones: 154 million （122.4%） ・3G: 72million （56.8%） ・3.9G (LTE): 83million （65.6%）
・BWA: 31million （24.5%）
※Population 126 million（as of January 1, 2015）
Analog mobile phone service (2G) ended in July 2012
3G Service started in March 2001
BWA service started in July 2009
LTE Service started in December 2010
Source: Ministry of Internal Affairs and Communications
2G (Analog)
3G (IMT-2000)
3.9G (LTE)

## Slide 19
Chart: Average Monthly Mobile Data Traffic per subscriber
| Mar.2013 | June.2013 | Sept.2013 | Dec.2013 | Mar.2014 | June.2014 | Sept.2014 | Dec.2014 | Mar.2015 | June.2015 | Sept.2015 | Dec.2015 | Mar.2016
加入者当たり | 2985.2892 | 3276.4779 | 3751 | 3964.7651 | 4434.9204 | 4749.7541 | 5209.2979 | 5293.2096 | 5628.6049 | 5929.0404 | 6597.4792 | 6567 | 6932
Chart: Average Monthly Mobile Data Traffic
| Mar.2013 | June.2013 | Sept.2013 | Dec.2013 | Mar.2014 | June.2014 | Sept.2014 | Dec.2014 | Mar.2015 | June.2015 | Sept.2015 | Dec.2015 | Mar.2016
総トラヒック | 421.9539 | 469.8237 | 546.3726 | 586.155 | 671.7418 | 729.8516 | 822.3608 | 871.8109 | 968.9804 | 1032.2674 | 1181.6371 | 1216.9212 | 1328.6503
Transition of Mobile data traffic over the last three years
Increased 1.2 times
over one year!
Increased 1.4 times
over one year!

## Slide 20: Evolution of Mobile Communications Systems
Traffic speed will be 10,000 times faster in 30 years
1990
2000
2010
2020
1980
(bps)
10k
1G
100M
10M
1M
100k
Analogue
9.6Kbps
1G (Analogue Based)
Voice
PDC
cdmaOne
28.8Kbps
64Kbps
Packet Communications
2G (Digital Based)
W-CDMA
384Kbps
CDMA2000
1x EV-DO
2.4Mbps
HSDPA
HSUPA
14.4Mbps
E-Mail
Photos
(still images)
Web Browser
Movie
3G (IMT-2000)
3.5G
LTE
100Mbps
LTE-Advanced
3.9G
1Gbps
4G
(year)
Capacity increased by introducing OFDMA & MIMO
10G
5G
Capacity increased by transition from TDMA to CDMA
A New Generation Comes
Every 10 Years
5G: The Fifth Generation mobile Communications Systems

## Slide 21: Key Capabilities of 5G
Ex: Quick transmission of Ultra high definition TV (4K/8K).
comparable to optic fiber
✓ Key Capabilities for 5G (IMT-2020) :
1 Ultra high speed data (eMBB) Peak data rate 10Gbps (100 x current LTE)
2 Ultra Low Latency (URLLC) Ultra Low Latency 1ms （1/10 of current LTE system）
3 Massive Machine Type Connections (mMTC):
Connection Density 100 devices/km² （100 x current LTE）
✓ 5G is expected to create a new market as a key infrastructure of IoT
Key Capabilities
for 5G
Ultra Low Latency
(URLLC)
Ultra High Speed Data
(eMBB)
Massive Machine Type Connections
(mMTC)
Ex: Automated Driving, Remote control Robots (real-time remote control, IoT for mission critical)
Ex: Massive Simultaneous Connections for sensor networks in small area, Smart Meters, Infrastructure Maintenance etc.
Large numbers of devices, sensors and terminals
Automated Driving Cars
Source: MIC, Nikkei Communications 4/2015

## Slide 22: Changes in earnings structure that 5G will bring
Home Security
Smart
Meters
Internet of Things
/Others
Automotive
Industrial Equipment
Main Target of 4G
New Fields 5G will target
Small # of
Connections
High Profits
Source: Nikkei Communications April 2015
Large # of
Connections
Smart Phones / Tablets
Low Profits
Current Business Field
5G Business Strategies needs to consider making new partnerships with a wide variety of industries
✓ Once 5G arrives, new markets will be created for the Internet of Things such as cars, industrial devices, and smart meters rather than in businesses in traditional devices such as smartphones
✓ There will be a need to make new partnerships with wide a variety of industries to deal with the changes in profit structures that will come about due to 5G mobile

## Slide 23: Roadmap toward 5G realization for 2020 and beyond
2012
2014
2015
2016
2017
2018
2019
2020
2021
2013
●Report ITU-R M.2320(11/2014) Future technology trends of terrestrial IMT systems
●ITU 5G International Workshp
●Recommendation ITU-R M.2083 : IMT Vision
ARIB
2020 and Beyond Adhoc
5G Requirements and Applications
Propose & Evaluate Interface
Strategic guidance on R&Ds, standardization activities, international cooperation
Activities by ５ＧＭＦ
R&Ds on 5G Technologies
５Ｇ Standardization Activities
World Radio Conf.
（WRC-15）
ITU Radio
Communications
Assembly （WRC-12）
World Radio Conf.
（WRC-19）
Deployment
Established on September 30th, 2014
✓ Promote three activities to support 5G realization for 2020 and beyond
1. Support activities by Fifth Generation Mobile Forum (5GMF)
2. R&Ds on 5G Technologies through Industry-Academic-Government Cooperation
3. Standardization Activities at the ITU and 3GPP
✓ The 5G System Trial to test radio access, networks, and applications for 5G will be started in Tokyo and local cities of Japan in FY2017
Promote R&Ds on 5G key technologies through Industry-Academic-Government Cooperation from 2015
Tokyo Olympic/
Paralympic Games
Rugby
World Cup
5G implemen- tation
5G System
Trial
Promoting Body
R&Ds
International Affairs
Study on spectrum for 5G as a preparation of WRC-19 with attention to international harmonization
(year)