## Slide 1
FGAI4H-M-038
E-meeting, 28-30 September 2021
Source: | Philips; MedSec | 
Title: | Cybersecurity AI/ML and data lifecycles | 
Purpose: | Information & Discussion | 
Contact: | Pat Baird, Philips Catherine Lowe, MedSec | E-mail: Pat.Baird@Philips.com E-mail: CatherineLowe@MedSec.com
Abstract: | This presentation contains a summary of cybersecurity and AI/ML risk management issues for discussion at Meeting M. | 

## Slide 2: Cybersecurity AI/ML and Data Lifecycles
Intended audience includes people that are familiar with DEL 2.2 particularly Annex C-7.
Includes additional and supplemental security requirements and best practices that were focused on the product development lifecycle.
Identifying and understanding the data management lifecycle, methods of communication and how the data is stored, transmitted and the interchange across trust boundaries are critical to security risk management
NIST Cybersecurity Framework best practices and Risk Management
**Note – The cybersecurity controls and information presented is separate to general IT Security Practices. Although, there may be overlap, cybersecurity has emerged as a standalone field with its own frameworks and is focused on 'networked' systems.

## Slide 3
Risk and data management is the classification of data based on the quality elements and the ‘attractiveness’ of the asset
Data collected during the development, testing, and improvement of a ML application could be a very ATTRACTIVE target for malicious actors.
This method should be considered as part of the risk assessment and evaluation.
Supervised & Unsupervised Learning
Cybersecurity and Machine Learning

## Slide 4: SaMD – Data Lifecycle
Safety Risk Management
Privacy Risk Management
Cybersecurity Risk Management

## Slide 5: Data Quality Elements and TPLC Development Lifecycle
Clinical Feasibility
Initiation
Clinical Feasibility
Concept
Clinical Feasibility
Planning
Implementation
Requirements Analysis
Development
Test
Design
Operations/Maintenance – Support/Services
Accuracy
Completeness
Consistency
Credibility
Currentness
Accessibility
Compliance
Confidentiality
Efficiency
Precision
Explain ability
Traceability
Understanding
Availability
Portability
Recoverability
AI/ML Software Development Total Lifecycle
Pre and Post Market Product Security Framework

## Slide 6: Product Security Framework
Premarket
Post market

## Slide 7
Threat Modeling and Security Risk Assessment is a continuous approach to cybersecurity risk management

## Slide 8: Cybersecurity NIST Framework
Machine learning methods should have requirements for anomaly detection by following a risk-based approach for potential security/privacy issues.

## Slide 9: Cybersecurity Premarket Controls for AI/ML
Secure Design - Modularized approach
The highly iterative, autonomous, and adaptive nature of software as a medical device (SaMD) requires a new, total product lifecycle (TPLC) regulatory approach that facilitates a rapid cycle of product improvement and allows these devices to continually improve while providing effective safeguards.
Risk Management – AI/ML TPLC
Risk Management file inclusive of safety, security and privacy assessments/evaluation
Threat modeling AI data elements and including data flow diagram with FMEA (required for V&V) against training dataset and clinical data (required as traceability matrix; addition of attack trees for high-risk devices)
Corresponding data sheets describing the data set split and hold out set which should be traceable for V&V
Supplier Management using SBOM for vulnerability management
Additional source of control identified with respect to supplier management with the use of an annual audit of SBOM and Manufacturer Disclosure Statement for Medical Device Security (MDS2) (applicable for hospitals)
Labeling requirement (ex. expected outcomes, target population, residual risk analysis)
Data sheets characterize data set and model cards (results after training – parameter and thresholds, algorithm itself for training, purpose, etc...)
Episodic testing for Cloud (ex. AWS)
Data criteria and identification requirements as part of the TPLC
Testing
Independent third-party penetration testing
Verification and Validation requirements of data model and software patch management
Unsupervised ML practices for anomaly detection (use of synthetic data)

## Slide 10: Cybersecurity Post-market requirements for AI/ML
Support and Services - Cyber forensics requirements and support
For example, in situations in which tampering with clinical data or images might be possible, a “fingerprint” hash of the data might be extracted and stored at the moment of capture. Comparison of this original hash to that of the data fed through a targeted algorithm would allow investigators to determine if that data had been tampered with or changed after acquisition. Such an intervention would rely on a health IT infrastructure capable of supporting the capture and secure storage of these hashes.
Vulnerability monitoring and management
Vulnerability monitoring including threat intelligence, National Vulnerability Database should be reviewed a minimum quarterly or if possible monthly basis
Patch Management – software and firmware (incl. OTS)
Seamless patching (i.e. No downtime or user interaction);
Orchestrated patch management based on a periodic frequency to minimize interruptions and downtime
Cybersecurity Signal detection, refinement and evaluation for interoperable systems
Training Mandatory
Lack of security training for users (lack of IT resources with specific AI/ML skillsets)
Most users are not up to date on patches, systems deployed including O/S are not qualified and installed on a frequency that is acceptable.
Structured approach and process for incoming complaint or issue with respect to assessing risk (safety, security, and privacy).
Mandatory training for all stakeholders that are involved with the device whether they’re a clinician using AI for patient care and/or support/services who are maintaining the device for safety and effectiveness.
Training for clinicians to understand the reported outcomes and the target populations in which the SaMD is to be used (i.e. CME credits)
Training for Support and Services (incl. third party servicers) on the device to ensure safety and effectiveness

## Slide 11: Question and Answer Discussion
Does the group think the larger audience needs some education on this topic?
There are some unique considerations for ML-related vulnerabilities; although there is literature on this topic, there isn’t much in the way of standards
  Do we want to supplement DEL2.2 with ML-specific considerations, or do you want to wait for standards to be developed & approved (eg 3+ years from now..)

## Slide 12: References
ISO 14971 Medical devices — Application of risk management to medical devices
TIR 57 Principles For Medical Device Security - Risk Management
TIR 97 Principles For Medical Device Security – Post market Risk Management For Device Manufacturers
NIST Cybersecurity Framework 1.1
NIST-SP800-53 Security and Privacy Controls for Information Systems and Organizations
NIST Privacy Framework: A Tool for improving privacy through enterprise risk management
NESTcc-Active-Surveillance-Roadmap-for-Public-Comment
NIST Special Publication 800-128 Guide for Security-Focused Configuration Management of Information Systems
HSCC-MEDTECH-JSP-v1.pdf (healthsectorcouncil.org) – Medical Device and Health IT Joint Security Plan
Principles and Practices for Medical Device Cybersecurity - http://www.imdrf.org/docs/imdrf/final/technical/imdrf-tech-200318-pp-mdc-n60.pdf