## Slide 1
Public Safety Network (A2A) Deployment in Korea and 3GPP Standardization issues
Ph.D. DJ (Dae-Jung) KIM, Director, TTA
Document No: | GSC-19_111
Source: | TTA
Contact: | DJ (Dae-Jung) KIM, kdj@tta.or.kr
Agenda Item: | 3.11

## Slide 2
Network Deployment plan for critical communication (A2A) in Korea
3GPP Standardization status and issues (A2A)
Contents

## Slide 3: 1. Public Safety Network Deployment plan in Korea(1)
■ History
May 2014 : President announced to initiate “SafeNet” project due to the Sewol Ferry Tragedy
May 2014 : Government announced “SafeNet” Deployment Plan in the cabinet council meeting
July 2014 : MSIP decided to adopt “LTE for Public Safety technology” for “SafeNet”
Oct. 2014 : “SafeNet “ ISP launched by MPSS (~March 31st, 2015)
Nov. 2014 : Prime Minister’s Office decided SafetNet’s radio frequency allocation range: 700MHz 20MHz bandwidth - Uplink 718~728MHz, Downlink 773~783MHz
Apr. 2015 : “SafeNet “ ISP completed, and Review progress ongoing
■ Overview (governance framework)
[Ministry of Science, ICT and Future Planning]
Support and Develop the technologies on Public Safety
MSIP
MPSS
[Ministry of Public Safety and Security]
Implement SafeNet, Develop the related policies
TTA
Standardization, Certification and Test

## Slide 4: 1. Public Safety Network Deployment plan in Korea(2)
■ Deployment Plan
2014.3Q: RFI, 2015.1Q: ISP
2015.2Q: RFP Open, Final Contract
2015.3Q: Pilot Project
Providing nationwide “SafeNet” services
Stage I (2014-2015)
Stage II (2016)
Stage III (2017)
8 province Deployment
~ 2015.12(Pilot Deployment)
~ 2016.12(8 Provinces)
~ 2017.12(Nationwide)
■ Deployment Overview
2015-2017
Period
Spectrum
20MHz (Up:718~728MHz, DN: 773~783MHz)
Budget
840 Million Dollar (Estimation)
User
8 Sectors, 330 Org., 200,000 Responders

## Slide 5: 2. 3GPP Standardization Status
MSIP decided to adopt “LTE for Public Safety” technology for “SafeNet” (July, 2014)
However, Work is still underway in Release 13 of 3GPP. So LTE standards will be continuously enhanced to meet public safety application requirements.
Release12, Dec.2014: GCSE, D2D
Release 13, Mar.2016: MCPTT, IOPS, ePROSE, MBMS_enh
Evolution
3GPP Rel12 Freeze: Mar ‘15
3GPP Rel13 Freeze: Mar ‘16
Group Com. System Enablers (R12)
LTE Proximity Services – Device Relay (R13)
Isolated E-UTRAN Operation for Public Safety (R13)
D2D (R12)
Mission Critical PTT (R13)
Korea is actively contributing to 3GPP for the expeditious completion of 3GPP Rel.13 Work Items that directly impact the deployment of Korea PSBN

## Slide 6: 2. 3GPP Standardization Status – Issue(1)
In Time Standardization of 3GPP Specification and Product Release: Rel.13 should support most of functions for public safety within the scheduled time frame to implement public safety Network in 2017.
Stage | Function | Rel.13 | 
 |  | Status | Plan (2015.06)
1 | Req. | completed | ~ 2014.09
2 | Architecture | Completed (with granted exceptions) | ~ 2015.06
3 | Protocol | In progress | ~ 2015.12
(ANS.1 Freezing) |  |  | ~ 2016.03

## Slide 7: 2. 3GPP Standardization Status – Issue(2)
‘16
‘17
‘15
Project Phases
3GPP Release Plan
‘18
R13 (eProSe, MC-PTT, IOPS)
R12 (ProSe, GCSE)
Phase I (Pilot)
Phase II (8 Major Provinces)
Phase III (Nationwide)
User Devices
EPC
Rel 12
GCSE
(eMBMS)
Rel 13
MC-PTT
IOPS
Rel 13
Rel 12
prose
MCPTT
eprose
GCSE
Available
Available
Available
Should be Available (sw upgrade)
Should be Available (SW upgrade)
Should be Available
Should be Available
Available
Available
Available
Available
Available
Available
Should be Available
Should be Available
Should be Available
Should be Available
For the initial stage of pilot networks, several optimized partial functions of the related standards will be used for the public safety network until completing 3GPP release 13 WIs.
Optimized Essential Functions
After that, the related Work Items such as MCPTT, IOPS, eMBMS and eProse functions will be completed and should be available before 2017..
Completion of the related Work Items

## Slide 8: 2. 3GPP Standardization Status – Issue(3)
Although it is expected to implement the network by pre-standard at the initial stage, After the completion of 3GPP Rel.13 standard, the cost minimization of updating deployed network should be considered. For this, we should try to pursue the setting of 3GPP standard by software upgradable function as much as possible.
Minimal Cost of Network update
It is important to encourage vendors to make the related products based on harmonized standards in order to provide entire services of public safety.
On-time products
We will encourage the adoption of Standardized Public Safety LTE Network to other countries to create economy of scale market.
Global harmonized spectrum is another key factor for success, – Specially PPDR AI, WRC Agenda 1.3
Globalization of Public Safety LTE Network

## Slide 9: Thanks for your listening.
DJ KIM • TTA • kdj@tta.or.kr