## Slide 1
HOSTED BY
26-27 September 2017
Document No: | GSC-21_014
Source: | TTA
Contact: | Hyun Seo Oh
Agenda Item: | 5.03
V2X Frequency Harmonization for C-ITS
Dr. Hyun Seo Oh, ITS/Vehicle ICT PG,TTA

## Slide 2
Introduction
V2X communication technology : 5.9GHz WAVE vs. LTE V2X
C-ITS pilot test & applications in Korea
V2X frequency assignment for ITS
TTA V2X communication standards
Concluding remarks

## Slide 3
V2X Communication Technology
V2V and V2I Wireless Networking for Vehicle Safety & C-ITS
US WAVE (Wireless Access in Vehicular Environment) & EU ITS G5
Less than 100msec Latency and 1km Radio Coverage
Frequency Band : 5.855 ~ 5.925GHz
V2I
V2V
RSE
OBE
RSE
Center
OBE
Emergency
Brake Warning

## Slide 4
V2X communication Specification
Item | USA | EU | Korea | Japan
Frequency Band(GHz) | 5.855~5.925GHz (7 CH) | 5.855~5.925GHz (7 CH) | 5.855~5.925GHz (7 CH) | 700MHz (1 CH)
Channel Bandwidth | 10MHz, 20MHz | 10MHz | 10MHz | 10MHz
Modulation Type | OFDM (BPSK, QPSK, 16QAM,64QAM) | OFDM (BPSK, QPSK, 16QAM,64QAM) | OFDM (BPSK, QPSK, 16QAM,64QAM) | OFDM (BPSK, QPSK, 16QAM,64QAM)
MAC | CSMA/CA | CSMA/CA | CSMA/CA (Time Slot based) | CSMA/CA
Data Rate | 3,4.5,6,9,12,18,24,27, 36, 48, 54 | 3,4.5,6,9,12,18,24, 27 | 3,4.5,6,9,12,18,24, 27 | 3,4.5,6,9,12,18

## Slide 5
LTE V2X Technology
Coexistence study between WAVE and LTE V2X in 3GPP
LTE V2X interworking standard in ISO CALM architecture
LTE V2X interworking standard in TTA Communication platform
RSE
E-Node B
Network
Center
LTE V2V
LTE V2I
802.11p V2V
802.11p V2V

## Slide 6
Pilot Testing in Korea
V2V Field testing to verify V2X based C-ITS applications [2014~2017]
System Configuration: 3000 Terminals, 95 RSE, Traffic Center
Terminal Types: Head Up Display(HUD), Navigation, Smart Phone
Head Up
Display
Navigation
Smart
Phone
GPS ANT
HMI
ECU Interface
WAVE ANT
WAVE Module

## Slide 7
6 Categories & 15 Applications
Service Categories | Applications
Vehicle Safety | Vehicle Collision Warning Road Hazard Warning Road and Weather Condition Warning Road work warning
Intersection Safety | Intersection Collision Warning Signal Phase/Timing Information
Protection for Disabled Person | Yellow Bus Warning School Zone Warning Pedestrian Waning
Emergency Situation | Emergency Warning Emergency Preemption Warning
Cooperative Traffic Management | Location based Position Information Gathering Location based Traffic Information Provision
Smart Tolling | Multi-lane Toll Charging
Public Transportation Management | Public Transportation Management

## Slide 8
ITS Frequency Band
5.825
5.835
5.845
5.855
5.865
5.875
5.885
5.895
5.905
5.915
5.925
Frequency
(GHz)
USA
EU
5.770 ~ 5.850 GHz (70MHz)
Japan
5.835 ~ 5.855
(20MHz)
Korea
5.855~5.875
Non-safety ITS
5.875~5.905
ITS road-safety
R
172
174
176
178
180
182
184
5.905~5.925
Future extension
5.855
5.865
5.875
5.885
5.895
5.905
5.915
5.815
5.805
5.795
5.785
5.795~5.815
(20MHz)
5.925
5.855~5.925(70MHz)
ITS(DSRC)
ITS(DSRC)
ITS(G5)
ITS(DSRC)
C-ITS
700MHz

## Slide 9
Frequency Assignment in Korea
Frequency assignment completed in 2016
Frequency Band: 5.855~5.925GHz(70MHz)
Applications : Vehicle Safety and C-ITS
Technical Requirements
  Channel Bandwidth : less than 10MHz
  Modulation : OFDM
  Transmitted Power : Max. 100mW(20dBm)
SCH
CCH
SCH
SCH
SCH
SCH
SCH
Frequency
5.855 5.865 5.875 5.885 5.895 5.905 5.915 5.925 [GHZ]
* CCH : Control Channel, SCH : Service Channel

## Slide 10
TTA Standard
Vehicle Communication Technology
  TTAK KO-06.0175/R1: Vehicle Communication System Stage 1: Requirement
  TTAK KO-06.0193/R1: Vehicle Communication System Stage 2: Architecture
  TTAK KO-06.0216/R1: Vehicle Communication System Stage 3: PHY/MAC Layer
  TTAK KO-06.0234/R1: Vehicle Communication System Stage 3: Networking Layer
  TTAK KO-06.0242/R1 : Vehicle Communication System Stage 3: Application Protocol Interface
  TTAK KO-06.0440: Methods of Measurement for WAVE PHY Layer(IEEE 802.11p)
Vehicle Communication Technology
  TTAK KO-06.0344: In-Vehicle Signage System for Vehicle Safety Guidance Stage 1: Requirements
  TTAK KO-06.0344-Part II: In-Vehicle Signage System for Vehicle Safety Guidance Stage 2: Data Exchange

## Slide 11
Concluding Remarks
Regarding WRC-19 AI 1.12, Korea supports relevant ITU-R studies on evolving ITS applications.
Also, supports the frequency band 5.855-5.925 MHz as globally or regionally harmonized spectrum for V2X based ITS applications in the view of the previous APG-19 meeting
Coexistence and interworking on 5.9GHz V2X and LTE V2X needs to be studied
  Option A : Primary use for 5.9GHz V2X, Secondary use for LTE V2X if channel is idle.
  Option B : Separate frequency band allocation for 5.9GHz V2X(WAVE, ITS G5) and LTE V2X

## Slide 12
Thank you
For more information, please contact: Hyun Seo Oh
hsoh5@etri.re.kr:
ETRI:
www.etri.re.kr