## Slide 1: Home Networking activities in TTC
Kenji KORO
TTC
Next-Generation Home Network system WG
Document No: | GSC17-PLEN-32
Source: | TTC
Contact: | Kenji KORO
GSC Session: | PLEN
Agenda Item: | 6.14

## Slide 2: Highlight of Current Activities
Standardization about Home Networking (HN) in Japan
  HEMS operation in Japan was required to specify at an early stage, so TTC specified several standard and technical reports as follows.
      Communication protocol (interface) under the layer of ECHONET Lite;
        JJ-300.10: Home network Communication Interface for ECHONET Lite (IEEE802.15.4/4e/4g 920MHz-band Wireless)
        JJ-300.11: Home network Communication Interface for ECHONET Lite
        (ITU-T G.9903 Narrow band OFDM PLC)
      TR-1043: Implementation guidelines of Home network communication interface
      Planning to study interworking between TR-069 and G.9973 for end device control
  Propose to SG13: Y.cloud-hemsarch: (Proposal for initiating study on architecture of the HEMS cooperating with the Cloud)
Cooperation with the related SDOs and Fora
  ITU-T, BB-Forum, HGI, DLNA, UPnP, etc.
      MoU between TTC and ZigBee Alliance, Wi-SUN Alliance.
  Cooperation in Japan
      New Generation Network Promotion Forum in Japan:
          IP network WG: Research technical and application demands
      HATS: Interoperability test about NAT Traversal.

## Slide 3: Strategic Direction
TR-069 is well known as the technical specification entitled CPE WAN Management Protocol (CWMP), but interworking with HN internal apparatus is not sufficiently defined.
About this problem, TTC will study the interworking between TR-069 and G.9973 for end device control.

## Slide 4: Challenges
Consider the cooperation between G.9973 and TR-069.
Figure Sample of the information flow between ACS and HTIP(G.9973)
Note: ACS (Auto Configuration Server)
HTIP (Home-network Topology Identifying Protocol )

## Slide 5: Next Steps / Actions
TTC will examine the cooperation about the access method to the HTIP information by CWMP.
  Propose to BBF, how to manage the HTIP information at ACS.

## Slide 6
Supplementary Slides

## Slide 7: Supplementary Slides
ECHONET Standardization
Layer
5-7
Layer
1-4
ECHONET
Communication Control
Absorption of Protocol Differences
Application
ECHONET Address
PLC
Low power RF
IRDA
IP
Ether
ECHONET Lite
Communication Control
Protocol Free
Application
IEC62480
IEC62394
IEC/ISO
14543-4-1
IEC/ISO
24676
IEC/ISO
14543-4-2
IEC62457
ECHONET Lite
Standardization
ECHONET Lite requires the separate specifications for L1 to L4 for global interoperability.
ECHONET Lite Overview

## Slide 8: Supplementary Slides
Figure ECHONET Lite Layer protocol model in TTC TR-1043
5-7 | ECHONET Lite |  |  |  |  |  |  | ECHONET Lite over L2 frame
4 | UDP |  |  |  |  |  |  | 
3 | IPv4 IPv6 |  |  | IPv6 6LowPAN | IPv4 IPv6 |  | IPv6 6LowPAN | 
2 | IEEE802.3 Family | G.9961 G.9972 | IEEE1901 | ITU-T G.9903 | IEEE802.11 Family | IEEE802.15.1 Family PAN Profile | IEEE802.15.4 IEEE802.15.4e/g | 
1 | IEEE802.3 Family | G.9960 G.9963 G.9964 G.9972 | IEEE1901 | ITU-T G.9903 | IEEE802.11 Family | IEEE802.15.1 Family | IEEE802.15.4 IEEE802.15.4e/g | 
Medium | UTP Optical Fiber | Power Line |  |  | Wireless (2.4/5G) | Wireless (2.4G) | Wireless (920MHz) | 
Ethernet
G.hn
IEEE1901
JJ-300.11
G.9903
Wi-Fi
Bluetooth
JJ-300.10
Wi-SUN Wi-SUN
ZigBee IP
Layer

## Slide 9: Supplementary Slides
Figure 1. System Configuration
Figure 2. Functional Model with Protocol Conversion
    SG13: Y.cloud-hemsarch
    (Architecture of the HEMS cooperating with the Cloud)