## Slide 1: Automotive Security
Security aspects on Intelligent Transportation Systems (ITS) and how to keep cars secure
Sep.12.2014
Jürgen Frank | Sr. System Engineer

## Slide 2: Agenda
Introduction
  Automotive Security Use-Case
  Security Timeline
Standards
  EVITA
  SHE
  HSM
  TPM
Security Modules

## Slide 3: Introduction

## Slide 4: Security Use Cases
In-Vehicle Security
Immobilizer / Component Protection
Mileage Protection
Secure Boot and Chain of Trust
Secure Communication
DRM - eCars
Connected Vehicle Security
Application download
DRM for content download/streaming
Remote ECU firmware update
Black-box for due government or insurance
Car-to-X communication

## Slide 5: Automotive Security - Timeline
HIS |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
1st SHE implementation |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
EVITA |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Hardware Security Module |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
HIS–HSM Specification |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
CSE2 (CobraC55 / Halo) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
CSE3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Next Gen. Security Module |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
 | 2008 |  |  |  | 2009 |  |  |  | 2010 |  |  |  | 2011 |  |  |  | 2012 |  |  |  | 2013 |  |  |  | 2014 |  |  | 
MPC564x - CSE
1st device MPC5746M - HSM
EVITA - Low/Medium/High Sec. Modules
HIS-SHE
CSE2
HIS - HSM
CSE3
N.G. HSM
?

## Slide 6: The Standards

## Slide 7: HIS – SHE Specification
Created by some German Car OEMs
Published as a official HIS standard (HIS => Herstellerinitiative Software, German for 'OEM software initiative')
Re-view of the Spec. by Freescale in an early phase
Key features of the SHE specification:
  A secure storage for crypto keys
  Crypto algorithm acceleration (AES-128)
  Secure Boot mechanism to verify custom firmware after reset
  Offers 19 security specific functions
  Up to 10 general and 5 special purpose crypto keys
juergen.frank@freescale.com

## Slide 8: Evita a project co-funded by the European Union http://www.evita-project.org
The objective of EVITA is to design, verify, and prototype an architecture for automotive on-board networks where security-relevant components are protected against tampering and sensitive data are protected against compromise.
High-Level
ECC-256
NIST FIPS GF(p)
AES based HASH
Medium-Level
Internal Core
50-250 MHz
Sec. Counter
Low-Level
AES-128
UTC Clock
AES-PRNG
EVITA HW-IF
Internal RAM
64 KBytes
Internal NVM
32+10 KBytes
EVITA Security Modules
Comment:
No OEM request EVITA modules  OEMs reference to SHE or HSM
Is not a specification, it’s a guidance
Already outdated on some aspects

## Slide 9: Trusted Platform Module
Main arguments against TPM:
High costs caused by integrating an external, additional chip inside an ECU
Sensitivity to attacks on the communication interface between ECU application core and HSM / replacing the TPM
The non-existence of debug/testing interfaces if a malfunctioned device needs to be analyzed
The high temperature range an automotive qualified product needs to satisfy (e.g. FLASH memory)
Is TPM2.0 able to fulfill the Car2x performance requirements (verify signature of >1000/sec) ?
 | Auto Security | TPM 1.2 | TPM 2.0
Specified | 2009 HIS-SHE; 2011 HSM | 2003/4 TCG Spec.; 2009 ISO/IEC11889 | DRAFT
Target Market | Automotive | PC | Embedded Systems, Automotive Profile available since 2 weeks
Algorithm | AES-128, CMAC HSM is prog. by customer | RSA, SHA1, HMAC, AES (optional) | RSA, ECC, SHA-1 /-256, HMAC, AES, other possible by supplier
Interfaces | on-die peripherals with master access and high clock | ext. SPI, I²C or LPC (28 / 32 pin package) / embedded in chips sets (e.g. Ethernet) / virtualized TPM | 
Clock | CSE ≥120 MHz / HSM ≥80 MHz | Typical 33 – 50 MHz | 
Internal core | SHE: SM or 32bit / HSM: 32bit | mainly 8/16 bit ; rarely 32 bit | 
Performance for 64bytes | SHE/HSM CMAC ~1µs | SHA1 155µs (TPM with 32bit-SC300™ core) | 

## Slide 10: NIS – National Institute of Standards
No automotive focus
Specifies most of the crypto algorithm (AES, SHA-1/2/3 etc.)
Use several time the championship approach (e.g. AES & SHE3)
Worries in the market (since Snowden), NSA- Dual_EC_DRBG issue

## Slide 11: Standards in the Regions
EMEA (mainly Germany)
  EVITA
    Initiator: EU- funded Europe CAR companies
    Published via Project web-page, guide not a spec.
  SHE Specification
    Initiator: German Car OEMs
    Published via HIS (Herrsteller Initiative Software) web-page
  Hardware Security Module
    Initiator: German Tier1 & Car OEM
    Published: not public available
US
  Technical acceptance of the SHE Specification (with small enhancements)
  See legal issues due HIS  SAE specification group
  HSM to complex for actual use-cases
ASIA
  Re-use of the SHE and HSM
  TPM still in discussion

## Slide 12: Security Modules

## Slide 13: Cryptographic Services Engine (CSE) Qorivva MPC564xB/C
CSE module implements the official HIS SHE-Specification
32-bit secure core working at 120 MHz
AES-128
  Supported crypto modes: ECB & CBC
  Throughput 100 Mbit/sec
  Latency 2μs per one encoding/decoding ops
CSE module interfaces:
  Crossbar master interface
  Configuration interface
Secure flash blocks assigned to the CSE module. Accesses from other masters are impossible.
PRNG seed generation via TRNG
CSE Core not programmable by customer
juergen.frank@freescale.com

## Slide 14: CSE2 Enhancements to CSE
Introduce new security flag per GPR-keys
Increased number of GPR-keys from 10 to 20
Secure Boot result storage in NVM (configurable by customer)
Reset Generation on Secure Boot Fail (configurable by customer)
juergen.frank@freescale.com

## Slide 15: Qorivva HSM Security Architecture
SSCM: System Status Configuration Module
PASS: Password And Device Security Module
TDM: Tamper Detection Module
HSM: Hardware Security Module
MPU: Memory Protection Unit
DCF: Device Configuration Format
Features:
Device life cycle scheme
Unique ID for each device
Debugger restrictions
Flash Protection
  OTP
  read / write & erase
  diary to log erasing-steps
Freescale Production
Customer Delivery
OEM Production
In-Field
Failure Analysis

## Slide 16: Hardware Security Module (HSM) v1: MPC5746M / MPC5777M & v2: MPC5748G / MPC5746C
HSM is free programmable by the customer, additional security algorithm could implemented in software
Features:
e200z0h core (v1: 100MHz / v2: 80 MHz)
4Kbytes Instruction cache
Secure Debugger Interface
Cryptographic Modules with AES-128, Random Number Generator, DMA
Sensor Interface – monitor for voltage, temperature and clock (v1)
Memory
  SRAM (v1: 40 Kbytes / v2: 32 Kbytes)
  Flash code: 2 x 64 Kbytes + 1 x 16KBytes data : 2 x 16 Kbytes
juergen.frank@freescale.com

## Slide 17: Flash Reprograming Security
MCU
OTP Flash (Configuration)
Pass Module
Password 1
256 bits
Password 2
256 bits
Password 3
256 bits
Password 0
256 bits
256 bit Challenge Register
CPU
LifeCycle State n
LifeCycle State 0
LifeCycle State 1
Flash Program Enable
Write/Erase Flash (Application)
Boot code (Password 0)
MCAL (Password 1)
OEM Code (Password 2)
Calibration (Password 3)
OEM Code (Password 2)
Configuration
Debug Enable/Disable
Flash Program Enable/Disable

## Slide 18
One Time Programable (OTP) definition:
A Flash block assigned as OTP cannot be erased.
Programming can only be done on an erased location.
Overprogramming is not possible.
DCF records
TDM
Flash Controller
Erase/Pgm
TDM - One Time Programable

## Slide 19: i.MX Trust Architecture Features
Trusted Execution
  Isolates execution of critical SW from possible malware
  TrustZone® Secure & Normal Worlds (processor modes)
  Hardware firewalls between CPU & DMA masters and memory & peripherals
High Assurance Boot
  Authenticated boot: prevents unauthorized SW execution
  Encrypted boot: protects SW confidentiality
  Digital signature checks embedded in on-chip boot ROM
  Run every time processor is reset
HW Cryptographic Accelerators
  i.MX family dependent
  Symmetric: AES-128, AES-256, 3DES, ARC4
  Message Digest & HMAC: SHA-1, SHA-256, MD-5

## Slide 20: i.MX Trust Architecture Features (continued)
Secure Storage
  Protects data confidentiality and integrity
  Off-chip: cryptographic protection including device binding
  On-chip: self-clearing Secure RAM
  HW-only keys: no SW access
HW Random Number Generation
  Ensures strong keys and protects against protocol replay
  On-chip entropy generation
  Cryptographically secure deterministic RNG
Secure Clock
  Provides reliable time source
  On-chip, separately-powered real-time clock
  Protection from SW tampering

## Slide 21: i.MX Trust Architecture Features (continued)
Secure Debug
  Protects against HW debug (JTAG) exploitation for:
    Security circumvention
    Reverse engineering
  Three security levels + complete JTAG disable
Tamper Detection
  Protects against run-time tampering
  Monitoring of various alarm sources
    Debug activation
    External alarm (e.g. cover seal)
    SW integrity checks
    SW alarm flags
  HW and SW tamper response

## Slide 22: CSE, HSM and the Security Standards
Security Standards | EVITA- Low | HIS-SHE | EVITA-Medium (HIS-Medium) | EVITA-High
Main features | UID Crypto engine | NVM is mandatory Fix function set | Programmable by customer | Public Key HASH
CSE/CSE2 |  |  |  | 
CSE3 |  |  |  | 
HSM (v1/v2) |  |  |  | 
next generation security module* |  |  |  | 
*feature set, still in discussion

## Slide 23: Freescale Devices with Security
Freescale Security Solution for Automotive products |  |  | 
 | Device | Platform | Module
MCU ( internal flash) | MPC564xB/C | Power Architecture® e200 | CSE
 | MPC5746M / MPC5777M |  | HSMv1
 | MPC5748G / MPC5746C |  | HSMv2
 | MPC5777C |  | CSE2
MPU (flash-less) | Vybrid ARM® Controller Solutions | ARM® Cortex®-Ax/Mx & ARM9/11 | TrustZone® + Sahara / CAAM
 | i.Mx ARM® 2x / 3x / 5x / 6x / 7x |  | 
Automotive
Consumer
juergen.frank@freescale.com
no automotive standards available

## Slide 24: Summary
Accepted Specifiction(s) for all regions (EMEA, US and ASIA)
  Actual, no international standards
  Actual, no public standards
Specification of the cryptographic functions
  Functions & Algorithm
  Performance (bandwidth, latency)
Additional security requirements
  e.g. protection schemes required