|  | INTERNATIONAL TELECOMMUNICATION UNION |
| --- | --- |
| ITU-T | G.874 Implementers’ Guide |
| TELECOMMUNICATION STANDARDIZATION SECTOR OF ITU | (27 May 2005) |
|  | SERIES G: TRANSMISSION SYSTEMS AND MEDIA, DIGITAL SYSTEMS AND NETWORKS |
|  | Implementers’ Guide for ITU-T Rec. G.874 (11/2001) Management aspects of the optical transport network element |

Summary

This document is an Implementers' Guide for ITU-T Recommendation of G.874 (11/2001).

Source

This document was agreed by ITU-T Study Group 15 on 27 May 2005.

(  ITU  2005

All rights reserved. No part of this publication may be reproduced, by any means whatsoever, without the prior written permission of ITU.

Table of Contents

1.0	Introduction	1

2.0	Terms to be removed from Rec. G.874	1

Implementers’ Guide for Recommendation G.874 
(Management aspects of the optical transport network element)

Implementers’ Guide for definitions and terms found in Rec. G.874

Abstract

SG15/WP3 has approved terminology Recommendations for Synchronous Digital Hierarchy (SDH) (Rec. G.780/Y.1351), Optical Transport Networks (OTN) (Rec. G.870/Y.1352) and Automatically Switched Optical Networks (ASON) (Rec. G.8081/Y.1353).

This Implementers’ Guide identifies terms originally listed in Rec. G. 874, which can now be removed from that Rec. and replaced with text pointing to the appropriate Terminology Rec. for the definition.  This Implementers’ Guide should remain in force until such time as Rec. G. 874 is revised and reissued.

# 1.0	Introduction

Study Group 15 has agreed to the development of a single source Recommendation for definitions currently found in Working Party 3 SDH/OTN/ASON Recommendations.  However, not all affected Recommendations are currently in process for revision.  To facilitate this transition, this Implementers’ Guide identifies the terms which can be removed and replaced when the initial source Recommendation is revised and reissued.  This Implementers’ Guide should remain in force until such time as Rec. G. 874 is revised and reissued.

# 2.0	Terms to be removed from Rec. G.874

The following table identifies the target term, with appropriate replacement definition text for the Recommendation identified in the title of this Implementers’ Guide.

| Original Term | Replacement text |
| --- | --- |
| 3.1 Optical Network Element (ONE): That part of a network element that contains entities from one or more OTN layer networks. An ONE may therefore be a standalone physical entity or a subset of a network element. It supports at least network element functions and may also support an operations system function and or a Mediation Function. It contains managed objects, a message communications function and a management application function. The functions of an ONE may be contained within an NE that also supports other layer networks. These layer network entities are considered to be managed separately from OTN entities. As such they are not part of the OMSN or OMN. | 3.1 The following terms are defined in ITU-T Rec. G.870/Y.1352: ( Inter-domain interface; ( Intra-domain interface. ( Optical Network Element (ONE) ( OTN management network (OMN) ( OTN management subnetwork (OMSN) |
| 3.2 OTN management network (OMN): An OTN management network is a subset of a TMN that is responsible for managing those parts of a network element that contain OTN layer network entities. An OMN may be subdivided into a set of OTN management subnetworks. |  |
| 3.3 OTN management subnetwork (OMSN): An OTN management subnetwork (OMSN) consists of a set of separate OTN ECCs and associated intra-site data communication links which have been interconnected to form a data communications network (DCN) within any given OTN transport topology. |  |
| 3.4 The following terms are defined in ITU-T Rec. G.7710/Y.1701: ( Local craft terminal; ( Management application function. | 3.2 The following terms are defined in ITU-T Rec. G.7710/Y.1701: ( Local craft terminal; ( Management application function. |
| 3.5 The following terms are defined in ITU-T Rec. G.709/Y.1331: ( General communication channel; ( General management communications overhead. | 3.3 The following terms are described in ITU-T Rec. G.709/Y.1331: ( General communication channel; ( General management communications overhead. |
| 3.6 The following term is defined in ITU-T Rec. G.784: ( Data Communications Channel. | 3.4 The following term is defined in ITU-T Rec. G.780/Y.1351: ( Data Communications Channel. |
| 3.7 The following terms are defined in ITU-T Rec. G.7712/Y.1703: ( Data Communications Network; ( Embedded Control Channel. | 3.5 The following terms are defined in ITU-T Rec. G.7712/Y.1703: ( Data Communications Network; ( Embedded Control Channel. |
| 3.8 The following terms are defined in ITU-T Rec. G.806: ( Atomic function; ( Management point. | 3.6 The following terms are defined in ITU-T Rec. G.806: ( Atomic function; ( Management point. |
| 3.9 The following terms are defined in ITU-T Rec. G.872: ( Inter-domain interface; ( Intra-domain interface. | (Editor’s note: Now defined in G.870/Y.1352.) |
| 3.10 The following terms are defined in ITU-T Rec. M.3010: ( Network element; ( Network element function; ( Operations system (OS); ( Q-Interface; ( Workstation function. | 3.7 The following terms are defined in ITU-T Rec. M.3010: ( Network element; ( Network element function; ( Operations system (OS); ( Q-Interface; ( Workstation function. |
| 3.11 The following term is defined in ITU-T Rec. M.3013: ( Message communications function. | 3.8 The following term is defined in ITU-T Rec. M.3013: ( Message communications function. |
| 3.12 The following terms are defined in ITU-T Rec. M.3100: ( Aggregate audible/visual indicators; ( Alarm reporting; ( Alarm report control interval; ( Alarm reporting control; ( Inhibited; ( Managed entity; ( Managed resource; ( Managed resource-specific; ( Management interface; ( Persistence interval; ( Qualified problem; ( Reset threshold report; ( Threshold report; ( Timed interval; ( Unit audible/visual indicator. | 3.12 The following terms are defined in ITU-T Rec. M.3100: ( Aggregate audible/visual indicators; ( Alarm reporting; ( Alarm report control interval; ( Alarm reporting control; ( Inhibited; ( Managed entity; ( Managed resource; ( Managed resource-specific; ( Management interface; ( Persistence interval; ( Qualified problem; ( Reset threshold report; ( Threshold report; ( Timed interval; ( Unit audible/visual indicator. |
| 3.13 The following term is defined in ITU-T Rec. X.700: ( Managed object. | 3.9 The following term is defined in ITU-T Rec. X.700: ( Managed object. |
| 3.14 The following terms are defined in ITU-T Rec. X.701: ( Agent; ( Manager; ( Managed object class. | 3.10 The following terms are defined in ITU-T Rec. X.701: ( Agent; ( Manager; ( Managed object class. |

_____________________________